## Slide 1: IEEE 802.17 Terms and Definitions Related to Performance
Khaled Amer
Interim Meeting
San Jose, CA
Sept 2001

## Slide 2: T&D input needed from the Perf Committee
Frame transmission time
  The amount of time elapsed between the time the first bit of a frame is submitted to a transmission medium and the time the last bit is submitted to that medium
Global Fairness
  Not needed - recommend removing it
Local Fairness
  Not needed - recommend removing it

## Slide 3: T&D input needed from the Perf Committee
MAC end-to-end delay
  The amount of time elapsed between the first bit of a frame submitted from the MAC client to the MAC layer at the source station and the first bit of the frame received by the MAC client at the destination station
Medium access delay
  The amount of time elapsed between the first bit of a frame submitted from the MAC client to the MAC layer and the first bit of that frame submitted to the transmission medium
Packetization delay
  No suggestions from perf committee - recommend removing it

## Slide 4: T&D input needed from the Perf Committee ...
Passthru delay
  The amount of time elapsed between the first bit of a passthru frame received by a station from the transmission medium and the first bit of that frame submitted to the transmission medium
Passthru delay buffer
  No suggestions from perf committee - recommend removing it
Propagation delay
  Recommend getting the formal definition from the IEEE dictionary or other previous standards.
  If not:
  The amount of time it takes a bit to move between two reference points on the same link of the transmission medium.

## Slide 5: T&D input needed from the Perf Committee ...
Protocol Stack delay
  No suggestions from perf committee - recommend removing it
Ring end-to-end delay
  The amount of time elapsed between the first bit of a frame submitted to the transmission medium by a source station and the first bit of that frame received from the transmission medium by the destination station
Ring latency
  See Ring end-to-end delay
Station passthru delay
  No suggestions from perf committee - recommend removing it

## Slide 6: Review of other T&D perf related definitions
Fairness
Flow control
Congestion control
Jitter
Latency