## Slide 1: RAH Harry Peng hpeng@nortelnetworks.com
Notes: Resilient packet ring in many ways is where Ethernet meets SONET and like any other encounter whether C or P,
It is a question of bridging the gap & to do that is a matter of G&T
However we do need context, so that the encounter has a useful outcome
Here I am proposing one possible context/framework for service differentiation in RPR

## Slide 2: RPR Applications
LAN
  Circumference < 5km
  Node count <64
MAN
  Circumference < 1000 km
  Node count < 128
RAN and WAN
  Well engineer ring to take advantage of Protection, port consolidation values

## Slide 3: Terms and Definitions
High priority traffic
  Class of traffic on the Ring with transport behavior that provides low bounded delay and jitter O[NxMTU] , no loss, and committed BW.
Medium Priority traffic
  Class of traffic on the Ring with transport behavior that provides bounded delay and jitter ~O[2xRTT] , no loss, and committed BW
  Also provide an Excess BW service above the committed if ring BW for Low priority is not used
Low priorty traffic
  Class of traffic on the Ring with transport behavior that provides bounded delay and jitter >O[2xRTT] , no loss, no guaranteed BW

## Slide 4: Terms and Definition
Transit path
  Logical connection from ringlet ingress to ringlet transmit scheduler. Packets received from ring ingress to be forward to downstream stations takes this path in the MAC.
  No reordering within the same class.
  When the transit scheduler is busy transmitting a packet, newly arrived packets are queued to be scheduled.
  All packets are transmitted till end of packed before the next scheduling event.
Add path
  Packet from the local station arrives at the scheduler via the add path. In the Add path there are up to 3 priority levels.
  All add path traffic are shaped:
  High priority traffic are guaranteed. It cannot be overprovision. Traffic Engineering is required. Synchronization of reservation information is also required .

## Slide 5: Transmit Scheduler Behavior
Transmit scheduler
  Contention resolution. Does not segment or preempt packets.
  Input jitter accumulation:
    Due to upstream station transmit simultaneously
    O[NxMTU]
    It is really O[NxB]. If B<= 1 MTU than above is correct
      N = number of station
      B = ring add burst size
  Transit jitter accumulation:
    Due to contention as down stream station transmitting.
      Add path jitter generation.
    High priority packet: O[NxMTU]
    Medium priority packet: >[NxMTU]-> trasit buffer size
    Low priority packet: > >[NxMTU ]-> trasit buffer size

## Slide 6: Terms and definitions: Application
Reserved Global BW
  Service:
    Guaranteed BW
    Low delay jitter O(NxMTU)
      where N= number of stattions
    Lossless on the ring
  BW is reserved all the way around the ring,
    BW reservation information is sent to all stations on the ring.
  Applies to ring high priority traffic
Reserved Link BW
  Service:
    Guaranteed BW
    Low delay jitter O(NxMTU)
      where N= number of stattions
    Lossless on the ring
  BW is reserved on a per link
    The reserved information is sent to all stations
  Apply to ring high priority traffic
Reserved-G is simpler to manage: less state values, state synchronization is required.
Reserved-L is managing station-station connections; better ring BW usage, more state values, state synchronization required

## Slide 7
Reclaimable
  Bandwidth reserved not being used can be used by another conversation of same or different priority.
  Conversation:
Non-reclaimable
  Bandwidth reserved for a conversation cannot be used by any body else.

## Slide 8: MAC Data Path I
Rate monitor on transit utilization. Congestion threshold is set accordingly.
Monitor transit medium and low usage
Receive
logic
Client
MAC
H
M
L
Client
Queues
Discard: RED, WRED
Queues: perVoQ, perClass
Scheduler: Shapers, GPS
Data.request
Data.indicate
Transmit
scheduler
Transit path
M
Rate monitors
Ingress shapers
M
H
M
Fainess
Fairness Msg
Fairness Msg
Add path

## Slide 9: MAC Data path II
If threshold are set as desired, fairness, and ingress shapers can provide the desired traffic behavior for the different classes.
There are ingress client queues! Where low priority packets suffers delay and may be loss.
Receive
logic
Client
MAC
H
M
L
Client
Queues
Discard: RED, WRED
Queues: per VoQ, perClass
Scheduler: Shapers, GPS
Data.request
Data.indicate
Transmit
scheduler
Transit path
M
Rate monitors
Ingress shapers
M
PTQ
STQ
M
Fairness
Fairness Msg
Fairness Msg
Thresholds

## Slide 10: Loss Requirement
802.17 is a Media Access Device
  Loss can occur at ring ingress and egress out side the MAC
    Buffers at ring add rate << ring rate
    Intelligent edge, which is scalable and feasible
  Ingress policed by fairness algorithm
    Provides jitter upper bound
  Not all protocol uses loss as congestion control
    UDP
  Carrier requirements:
    No packet loss
    0% preempt-able traffic

## Slide 11: Bottom Line
Loss for Lower than low priority traffic
  Rather lost in the client
No guaranteed on BW
  Provide fair and consistent access is better than variable burst with loss.