## Slide 1: PAH Harry Peng hpeng@nortelnetworks.com
Notes: Resilient packet ring in many ways is where Ethernet meets SONET and like any other encounter whether C or P,
It is a question of bridging the gap & to do that is a matter of G&T
However we do need context, so that the encounter has a useful outcome
Here I am proposing one possible context/framework for service differentiation in RPR

## Slide 2: Synchronous
Transmit is frequency locked to the receive.
Write rate = Read rate
Low frequency jitter and wander
CRU
Ringlet
In
clk
data
Transit Buffer
Write
Read
PLL
clk
data
CSU
Ringlet
Out
Rx
Tx
fc-tx = fc-rx
fc-rx+/- Y ppm

## Slide 3: Asynchronous
RX
  PHY uses CDR to recover clock from the line
  Receive data at Rate = upstream Tx oscillator: fc(rx)+/- Y ppm
Tx
  Transmit data at local oscillator baud rate= fc(tx)+/- X ppm
  Clock Accuracy
    Free run SONET +/- 20ppm
    Ethernet +/- 100ppm
  Clock stability, aging
Mismatch of Write and Read rate
  Starvation: fc(tx) > fc(rx)
  Overflow: fc(tx) < fc(rx)
CRU
Ringlet
In
clk
data
Transit Buffer
Write
Read
OSC
clk
data
CSU
Ringlet
Out
Rx
Tx
Fc(tx)+/- Xppm
Fc(rx)+/- Yppm

## Slide 4: Asynchronous
Asynchronous operation applies to ethernet and Byte escape method
Ethernet
  IPG and rate adaptation in Ethernet RS
    One byte adjusted in IPG for every 5000 bytes
Byte Escape
  Assumes PHY is doing the escaping
    PSAP interface is in native format
    Escaping occurs for both ingress and egress, balances out
    Reduces add rate
  Rate adaptation is the the SONET RS
Consistent Rate adaptation function preferred

## Slide 5: Synopsis
Starvation
  Have to make sure no starve on transmission
    Jumbo frames
    One extra byte for every 5000 data bytes (+/-100 ppm)
    Prefill FIFO before launching packet
  Add Idle on egress
    This is a bonus.
Overflow
  Delete Idles on ingress
    Delete one IDLE for every 5000 data bytes (+/- 100 ppm)
    Have to ensure there is enough Idle between packets so removing is not a problem