## Slide 1: Topology/Protection Comment Resolution Summary
Jason Fan, Section Editor
(jason@luminous.com)
Jim Kao, Technical Editor
(jkao@cisco.com)

## Slide 2: Clause 10 and Annex K
198 comments
  2 technical binding
  102 technical non-binding (8 editorials upgraded)
  94 editorial
Resolutions (technicals)
  58 accepted, accepted/dup
  36 accepted modified
  5 superceded
  4 withdrawn
  1 rejected
Editorial license requested

## Slide 3: Issues Covered
Minor text, figure, variable naming, etc. cleanups and corrections
  54 comments
Removal of spurious may and duplicate shall statements
  10 comments
Correction of badFcsUser operation, and MIB editors need to pick up definitions of station settings ATT fields
  269, 314, 383
Add description of protection time for strict mode traffic
  237
LRTT frames corrected to be wrap eligible
  297, 298
Added conditional support option to ATT table (mandatory if different from default, otherwise optional)
  304

## Slide 4: Issues Covered
Value within a missing ATT reported with default value of 0 or empty string, MIB editors to modify definition of station if index attribute
  320
Maximum configurable keepalive timeout increased back to 50 ms
  356
Trigger variables for the transmit TP frame state table to be set to FALSE only within that table
  344
Topology database example values to be made consistent with a functional ring
  329, 384
Cleanup of transmit TP frame state table
  371, 373, 374
Pre-condition for triggering TC frames is that topology is valid
  378

## Slide 5: Issues Covered
Modifications of secondary MAC address handling
  386, 387, 388, 391
  Validation only performed if topology is valid
  If substitution is supported, ringlet selection will support at least 32 addresses
  If 32 exceeded on ring, defect is reported. All addresses written into topology database
  Field to be provided in the topology database indicating which secondary MAC addresses are being used
  Validation state table to be split into two, one for received ATD frames, and the other for local configuration
  Secondary MAC addresses 1 and 2 independently reported on ring

## Slide 6: Issues Covered
In case of transit path failure, a station can report an SF on a single span or suspend transmission of keepalives on that span, or do the above on both spans
  357
Station receiving an LRTT response (not LRTT request) to reject LRTT frames received after more than 100 ms
  398
LRTT measurement information to be stored in topology database based on ringlet on which LRTT response is received
  402
Row descriptions in LRTT state table to be clarified
  404
Annex K to be deleted
  581

## Slide 7: Rejections
Comment 361 (TB)
  Contribution cited in the comment not available
  Commenter was present and agrees