## Slide 1
Project | IEEE 802 Executive Committee Study Group on Mobile Broadband Wireless Access <http://ieee802.org/20> | 
Title | Implication of End-user QoS requirements on PHY & MAC | 
Date Submitted | 2003-11-10 | 
Source(s) | Anna Tee | Voice: 972-761-7437 Fax: 972-761-7909 Email: a.tee@samsung.com
 | Joseph R. Cleveland | Voice: 972-761-7981 Fax: 972-761-7909 Email: jclevela@sta.samsung.com
 | Jin Weon Chang | Voice: +82-31-279-5117 Fax: +82-31-279-5130 Email: jwchang@ieee.org
Re: | 802.20 WG Call for Contributions | 
Abstract | This document gave a brief overview of the QoS classification and requirements by ITU and 3GPP, and used the information to derive the latency and error rate requirements for 802.20 in support of IETF DiffServ structure. | 
Purpose | Contribute to the discussion and development of the 802.20 Requirements on Latency and FER as related to QoS | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802 MBWA ECSG. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 
C802.2-03/106

## Slide 2: Implication of End-user QoS Requirements on PHY & MAC
Joseph Cleveland
Anna Tee
November 03, Albuquerque

## Slide 3: Scope of 802.20
As described in the PAR and quoted in Section 1.3 of 802.20 Requirements Document Rev. 8c [1]:
  “Specification of physical and medium access control layers of an air interface for interoperable mobile broadband wireless access systems, operating in licensed bands below 3.5 GHz, optimized for IP-data transport, with peak data rates per user in excess of 1 Mbps. It supports various vehicular mobility classes up to 250 Km/h in a MAN environment and targets spectral efficiencies, sustained user data rates and numbers of active users that are all significantly higher than achieved by existing mobile systems.”

## Slide 4: Applications
Examples of possible applications that are IP-based data, in mobility environment of up to 250 km/h in a MAN environment, as described in Section 2 of the Requirements document:
  VoIP / Video conferencing
  Audio / video messaging
  Video (e.g., MPEG2, MPEG4, H.323,…)
  Web browsing (HTTP, TCP)
  E-mail (UDP)
  File Upload and Download (FTP, TCP)
  Video and/or audio streaming
  IP multicast
  Interactive internet gaming
  Telemetry
  Location based services (e.g., E-911)
  Telematics (= a subset of the above + vehicular specific applications)
  …

## Slide 5: Application requirements to the end-users
Major parameters are:
  Data Rate
  Latency
  Latency variation
  Information loss ratio
Various applications can be classified into different groups, based on their latency and error tolerance requirements.

## Slide 6: User-centric Delay and Packet Loss requirements – ITU G.1010*
Source: ITU G.1010 [“Draft New Recommendation G.QoSRQT – End-user Multimedia QoS Categories”, ITU-T study group 12, contribution 37, August 2001]

## Slide 7: End-user QoS Categories Mapping - ITU G.1010

## Slide 8: UMTS QoS classes
Adopted performance targets similar to ITU-T’s collection of information - 3GPP TS 22.105 [3]
Four different QoS classes are defined in 3GPP TS 23.107 [4], as follows:-
Traffic class | Conversational class conversational RT | Streaming class streaming RT | Interactive class Interactive best effort | Background Background best effort
Fundamental characteristics | - Preserve time relation (variation) between information entities of the stream Conversational pattern (stringent and low delay ) | - Preserve time relation (variation) between information entities of the stream | - Request response pattern - Preserve payload Content | - Destination is not expecting the data within a certain time - Preserve payload content
Example of the application | - voice | - streaming video | - Web browsing | - Background download of emails

## Slide 9: Performance targets for Conversational/Real-Time Services (audio and video applications) - Source: 3GPP TS 22.105 V6.2.0 & G.1010
* Assumes adequate echo control
** Exact values depend on specific codec, but assumes use of a packet loss concealment algorithm to minimise effect of packet loss
Medium | Application | Degree of symmetry | Typical Data rates/ Amount of Data | Key performance parameters and target values |  | 
 |  |  |  | End-to-end One way Delay | Delay Variation within a call | Information Loss**
Audio | Conversational voice | Two-way | 4 - 64 kb/s | <150 msec Preferred* <400 msec limit* | < 1 msec | < 3% Packet Loss Ratio
Video | Videophone | Two-way | 16 -384 kb/s | < 150 msec preferred <400 msec limit Lip-synch : < 100 msec |  | < 1% Packet Loss Ratio
Data | Telemetry - two-way control | Two-way | <28.8 kb/s | < 250 msec | N.A | Zero
Data | Interactive games | Two-way | < 1 KB | < 250 msec | N.A | Zero
Data | Telnet | Two-way (asymmetric) | < 1 KB | < 250 msec | N.A | Zero

## Slide 10: Performance targets for Interactive Services – source: 3GPP TS 22.105 & ITU G.1010
Medium | Application | Degree of symmetry | Typical data rate/ Amount of data | Key performance parameters and target values |  | 
 |  |  |  | One-way Delay (response time) | Delay Variation | Information loss
Audio | Voice Messaging | Primarily one-way | 4-32 kb/s | < 1 sec for playback < 2 sec for record | < 1 msec | < 3% Packet Loss Ratio
Data | Web-browsing - HTML | Primarily one-way | ~ 10 kB | < 4 sec /page | N.A | Zero
Data | Transaction services – high priority e.g. e-commerce, ATM | Two-way | < 10 kB | < 4 sec | N.A | Zero
Data | E-mail (server access) | Primarily One-way | < 10 kB | < 4 sec | N.A | Zero

## Slide 11: Performance targets for Streaming Services – source: 3GPP TS 22.105 & ITU G.1010
Medium | Application | Degree of symmetry | Data rate/ Amount of data | Key performance parameters and target values |  | 
 |  |  |  | Start-up Delay | Transport delay Variation | Packet loss at session layer
Audio | Speech, mixed speech and music, medium and high quality music | Primarily one-way | 5-128 kb/s | < 10 sec | < 1 msec | < 1% Packet loss ratio
Video | Movie clips, surveillance, real- time video | Primarily one-way | 16 -384 kb/s | < 10 sec | < 1 msec | < 1% Packet loss ratio
Data | Bulk data transfer/retrieval, layout and Synchronisation information | Primarily one-way | 10 kB – 10 MB | < 10 sec | N.A | Zero
Data | Still image | Primarily one-way | < 100 kB | < 10 sec | N.A | Zero

## Slide 12: Value ranges for UMTS Bearer Service Attributes - 3GPP TS 23.107 V5.10.0
Traffic class | Conversational class | Streaming class | Interactive class | Background class
Maximum bitrate (kbps) | <= 16 000 | <= 16 000 | <= 16 000 – overhead | <= 16 000 – overhead
Delivery order | Yes/No | Yes/No | Yes/No | Yes/No
Maximum SDU size (octets) | <=1 500 or 1 502 | <=1 500 or 1 502 | <=1 500 or 1 502 | <=1 500 or 1 502
Delivery of erroneous SDUs | Yes/No/- | Yes/No/- | Yes/No/- | Yes/No/-
Residual BER | 5*10-2, 10-2, 5*10-3, 10-3, 10-4, 10-5, 10-6 | 5*10-2, 10-2, 5*10-3, 10-3, 10-4, 10-5, 10-6 | 4*10-3, 10-5, 6*10-8 | 4*10-3, 10-5, 6*10-8
SDU error ratio | 10-2, 7*10-3, 10-3, 10-4, 10-5 | 10-1, 10-2, 7*10-3, 10-3, 10-4, 10-5 | 10-3, 10-4, 10-6 | 10-3, 10-4, 10-6
Transfer delay (ms) | 100 – maximum value | 280* – maximum value |  | 
Guaranteed bit rate (kbps) | <= 16 000 | <= 16 000 |  | 
Traffic handling priority |  |  | 1,2,3** | 
Allocation/Retention priority | 1,2,3 | 1,2,3 | 1,2,3 | 1,2,3
Source statistic descriptor | Speech/unknown | Speech/unknown |  | 
Signalling Indication |  |  | Yes/No** | 
  *If the User Equipment (UE) requests a transfer delay value lower than the minimum value, this shall not cause the network to reject the request from the UE. The network may negotiate the value for the transfer delay.
  **If signalling indication is set to ‘Yes’, the UE should set the traffic handling priority to ‘1’.

## Slide 13: Current QoS requirement in 802.20
Support of IETF DiffServ (DS) [5] is described in Section 4.4.1 of the draft 802.20 requirements [1]
IETF DiffServ – classes of services specified in the DS codepoints
  Expedited Forwarding (EF) [6]
  Assured Forwarding (AF) – 4 subclasses with 3 levels of drop precedence through the mapping of DS codepoints [7]
  Best Effort
IETF DiffServ defined the QoS structure for IP packets at the Network Layer
How should the End user QoS requirements be mapped into the DiffServ classes at the Network layer?
How should the DiffServ requirements at the Network layer be translated to the related requirements at PHY and MAC layers in order to achieve the end-to-end QoS requirements?

## Slide 14: Information Flow between End-users
Transmitted information path
Received information path
Scope of IEEE 802.20 Standard

## Slide 15: 802.2 Logical Link Control (LLC)*
Three forms of service supported, as viewed from the network layer:
  Unacknowledged Connectionless mode
    No need to establish data link level connection
    For point-to-point, multicast and broadcast applications
  Connection mode
    Need to establish a data link level connection
    Provides data link layer sequencing, flow control and error recovery
    For point-to-point applications
  Acknowledged connectionless mode
    No need to establish data link level connection
    LLC acknowledgement required
    For point-to-point applications
  Source: IEEE 802.2 Standard [8]

## Slide 16: QoS Implication on PHY and MAC
User-perceivable performance described by QoS requirements
QoS requirements need to be accomplished from the transmitting to the receiving end
Impact of each layer along the transmission path need to be considered for an optimized system
=> Derive PHY and MAC layer requirements from User-driven performance requirements, based on reasonable assumptions on the apportionment between different layers.
Latency, Delay Variation and Error Rate are the main performance parameters related to the PHY and MAC layers.
Tradeoff between Latency and Error Rate performance in an optimized dynamic system.

## Slide 17: QoS Implication on PHY and MAC
Information loss
  Error correction at the PHY layer, may correct errors through re-transmissions
  Error detection at the MAC sublayer, corrected through re-transmissions, with increased latency ~ n x ARQ loop delay, where n = number of re-transmisisons
  Possible error detection at the LLC sublayer, corrected through LLC re-transmission, depending on the mode of operation at LLC sublayer
  Error detection at TCP layer, corrected through re-transmission, but with increased latency ~ M x Round Trip Time (RTT), M = number of TCP re-transmisisons
  For UDP, error packets will be detected and discarded without re-transmission
End-to-end Latency
Notes:
Dependent on traffic loading, protocols, and delay in the lower layers, in some cases
Dependent on distance between user terminal and base station
Dependent on Implementation

## Slide 18: IEEE 802 Error Rate Requirement
IEEE Std 802-2001 specified the error rate performance for IEEE 802 LANs and MANs in section 7.3 [9, 10]:
Probability of error of data delivered to the MAC Service Access Point (MSAP) at the receiver < 8x10-8 per octet of MAC Service Data Unit (SDU) length
For MAC SDU length = 1024 octets,
  MAC SDU packet error rate, Pe < ~ 8 x 10-5
Assume the same packet size and independent PER for each re-transmission,
Number of retransmissions | 1 | 2 | 3
Residual Packet Error Rate for Pe = 8 x 10-5 | 6.4 x 10-9 | 5 x 10-13 | 4.096 x 10-17
Residual Packet Error Rate for Pe = 0.25 | 6.25 x 10-2 | 1.56 x 10-2 | 3.9 x 10-3

## Slide 19: Recommended Latency and Packet Error Rate Performance Targets for IEEE 802.20
Latency & Error Rate for different application classes | Expedited Forwarding (EF) | Assured Forwarding (AF) | Best Effort (BE)
 | ~ 30 ms (TBR) | ~ 30 ms – 10 s (TBR) | >> 10 s (TBR)
Error Tolerant | 3 x 10-2 | 10-2 – 2.5 x 10-1 (TBR) | 2.5 x 10-1 (TBR)
Error Intolerant | 5 x 10-13 (TBR) | 5 x 10-13 – 8 x 10-5 (TBR) | 8 x 10-5
Assured Forwarding class can be further sub-divided into 4 subclasses
Mapping of applications to the various classes depend on implementation
Requirements for the proposal: to demonstrate that the error rates can be achieved with the corresponding latency

## Slide 20: Industrial QoS Related Activities
Standards organizations that are working on QoS issues:
  IEEE 802.11e, 802.11n (High Throughput WLAN Standard)
  IETF
  ITU-T, ITU-R
  3GPP
  T1A1
  3GPP2
Some of the Issues: [11]
  allocation of performance requirements along the transmission path traversed by the information packets, to achieve the end-to-end performance targets.
  IP QoS interoperability – differences in the definition of QoS classes by different standards for different technologies across the network that connects the two end-users.

## Slide 21: List of References
[1] Draft 802.20 Requirements Document – Ver. 8c, Oct. 28, 2003.
[2] ITU G.1010 [“Draft New Recommendation G.QoSRQT – End-user Multimedia QoS Categories”, ITU-T study group 12, contribution 37, August 2001]
[3] 3GPP TS 22.105, "Services and service capabilities“
[4] 3GPP TS 23.107, "QoS concept and Architecture"
[5] RFC 2475, “An Architecture for Differentiated Services”
[6] RFC 2598, “An Expedited Forwarding PHB”
[7] RFC 2597, “Assured Forwarding PHB Group”
[8] ANSI/IEEE 802.2(ISO/IEC 8802-2:1998), “Part 2, Logical Link Control”, 1998 edition
[9] IEEE Std 802 -2001, “IEEE standard for Local and Metropolitan Area Networks: Overview and Architecture”
[10] C802.20-03/83r1, “FER: Do We Need It?”, J. Cleveland et. al., Sept. 8, 03.
[11] http://www.itu.int/ITU-T/worksem/qos/index.html