## Slide 1: IEEE 802.20 MBWA Standard Development Project
Presentation of Contribution C802.20-03-105 Nov-10-2003
Dan Gal, email: dgal@lucent.com
Plurality of Technologies & Channel Bandwidths in the IEEE 802.20 Standard
C802-03/108

## Slide 2: Purpose
Indicate that the 802.20 standard may evolve into a multi-technology, multi-channel -bandwidth umbrella standard.
Promote an educated discussion and decision making, followed by an unambiguous definition of these requirements in the SRD*.
* SRD= System Requirements Document

## Slide 3: Outline
FDD, TDD Duplexing – what’s required of the technology proposals?
Multiple PHYs – with a common MAC or PHY-specific MACs, i.e, multiple–technology standard
Multiple Channel BWs
Conclusions
TDD
#2
TDD #1
FDD
#2
FDD #1

## Slide 4: Reference Documents
The IEEE 802.20 PAR
The 802.20 SRD version 8C.

## Slide 5: FDD & TDD Duplexing (1/2)
The PAR [1] has established a requirement for both FDD and TDD supported in the 802.20 standard.

## Slide 6: FDD & TDD Duplexing (2/2)
Neither the PAR, nor the 802.20 SRD (rev 8c) provide an explicit requirement that technology proposals support both FDD and TDD modes. Thus, -
It is reasonable to assume, that this is not a requirement. i.e., proposals may support either (FDD/TDD) or both. -- if this is the consensus requirement, it should be clearly stated in the SRD.

## Slide 7: Multiple PHY-MAC Combinations
Sections 3.1.1 and 3.1.2 of the SRD indicate: - two (or more) PHY-MAC standards - no common MAC

## Slide 8: Channel Bandwidth & Block Assignments
SRD section 4.1.3

## Slide 9: Channel BW & Block Assignments (2/4)
Problem: no channel bandwidth(s) specified in the SRD section 4.1.3
Interpretation 1: Any proposed technology must support deployment in all block assignments and its supported channel BWs may be one or more of the following: FDD BWs: 1.25, 5 , 10 , 20 MHz
TDD BWs: 2.5, 5, 10, 20, 40 MHz
Interpretation 2: Proposed technologies may only support a subset of the defined block assignments. No requirement on the channel BW.

## Slide 10: Channel BW & Block Assignments (3/4)
Additional issues:
Deployment may be required in a partial (frequency) block assignments.
A technology proposal that only supports a wide band channel (say, 20 MHz) will not be deployable in a narrow sub-block.
Need to be consistent with the requirement of section 4.3 of the SRD (see the next slide)

## Slide 11: Channel BW & Block Assignments (4/4)
SRD section 4.3: …”the design shall be readily extensible to wider channels…”

## Slide 12: Summary
We have shown that the PAR and SRD definitions of the following key radio technology characteristics: - FDD / TDD - PHY-MAC combinations, and - Channel bandwidth(s) are too vague or ambiguous and need further clarifications.
However redefined, these requirements may lead to an umbrella 802.20 standard that specifies multiple technologies and channel bandwidths.
The 802.20 working group needs to be aware of this outcome and make the appropriate decisions.