## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/mbwa> | 
Title | Comparison of SFBC and STBC for Transmit Diversity in OFDM System | 
Date Submitted | 2003-05-05 | 
Source(s) | Insoo Sohn ETRI Heesoo Lee ETRI Jae Young Ahn ETRI | Voice: +82-42-860-1027 Fax: +82-42-860-6732 Email: isohn@etri.re.kr Voice: +82-42-860-5375 Fax: +82-42-860-6732 Email: heelee@etri.re.kr Voice: +82-42-860-6421 Fax: +82-42-860-6732 Email: jyahn@etri.re.kr
Re: |  | 
Abstract | This contribution presents some simulation results for comparison between space-time block code (SFBC) and space-frequency block code (STBC) using METRA MIMO channel model. | 
Purpose | For informative use only. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802 MBWA ECSG. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 
IEEE C802.20-03/49

## Slide 2
Insoo Sohn, Heesoo Lee, Jae Young Ahn
May 2003
Comparison of SFBC and STBC for Transmit Diversity in OFDM System

## Slide 3: Contents
Transmit Diversity in OFDM Systems
STBC
SFBC
Simulation Environments
Simulation Results
Conclusions

## Slide 4: Transmit Diversity in OFDM Systems
Alamouti Transmit Diversity
  Tx diversity gain with no channel knowledge at transmitter
  Incorporated in 3G-CDMA (STTD)
Easily Applied to OFDM Systems
  Space-time block code (STBC)
    Multiplex two symbols onto two antennas over two successive time intervals
    Suitable for low vehicular speed
  Space-frequency block code (SFBC)
    Multiplex two symbols onto two antennas over two successive subcarriers
    Suitable for low delay spread channel environment
  Which scheme is suitable for MBWA system?
    MBWA should support various vehicular mobility classes up to 250 Km/h.

## Slide 5: Space Time Block Code (STBC)
Assume two transmit antennas
Assume the signal constellation has 2b elements.
  Example: BPSK (b=1), QPSK (b=2), 16-QAM (b=4).

## Slide 6: Space Frequency Block Code (SFBC)
Assume two transmit antennas
Assume the signal constellation has 2b elements.
  Example: BPSK (b=1), QPSK (b=2), 16-QAM (b=4).

## Slide 7: Simulation Environments
Basic OFDM Parameters
  Bandwidth : 20 MHz
  FFT Size (N) : 2048
  Used Subcarrier (Nsc) : 1536
  Subcarrier Spacing (Df) : 12.207 kHz
  Data Duration (Td) : 81.92 us
  Guard Interval (Tg) : 18.08 us
  Symbol Duration (Tsym) : 100 us
Perfect Channel Estimation

## Slide 8: Simulation Environments
MIMO Channel Parameters (source: 3GPP TR 25.876 V1.0.1)

## Slide 9: Simulation Environments
Data Rates
  Number of Subcarriers : 1536
Channel Model : MIMO Channel
  Scenario 1
    Case B, I-METRA Channel (Path #1 Rayleigh), 3 km/h
    Modulation Format : QPSK, 16QAM, 64QAM, 256QAM
    MIMO Scheme : SISO, T2R1 STBC, T2R1 SFBC, T2R2 SFBC
  Scenario 2
    Case B, I-METRA Channel (Path #1 Rayleigh), 60 km/h
    Modulation Format : QPSK, 16QAM, 64QAM
    MIMO Scheme : SISO, T2R1 STBC, T2R1 SFBC, T2R2 SFBC
  Scenario 3
    Case C, I-METRA Channel, 250 km/h
    Modulation Format : QPSK, 16QAM
    MIMO Scheme : SISO, T2R1 STBC, T2R1 SFBC, T2R2 SFBC
Modulation | BPSK | QPSK | 16QAM | 64QAM
DR (Mbps) | 15.36 | 30.72 | 61.44 | 92.16

## Slide 10: MIMO-OFDM Simulation
Scenario 1

## Slide 11: MIMO-OFDM Simulation
Scenario 2

## Slide 12: MIMO-OFDM Simulation
Scenario 3

## Slide 13: Conclusions
Space time block code (STBC) and space frequency block code (SFBC) were compared in METRA MIMO channel environment.
In walking speed of 3km/h, STBC and SFBC has similar performance in pedestrian A MIMO channel.
In vehicular speed of 60km/h & 250km/h, SFBC outperforms STBC method even in vehicular A MIMO channel, where variation in frequency domain is greater than pedestrian A case.
We propose the use of SFBC for transmit diversity in MBWA system.