## Slide 1
IEEE P802.20
Mobile Broadband Wireless Access
Project
IEEE P802.20 Working Group for Mobile Broadband Wireless Access (MBWA)
Title
802.20 Technical Requirements – Coexistence Background
Date Submitted
July 22, 2003
Re:
802.20 Technical Requirements and Evaluation Criteria
Abstract
This contribution establishes some background for technical work related to the co-existence portion of the 802.20 Technical Requirements Draft. Currently the section (in outline form) exists as an “appendix” to the draft requirements document. .
Purpose
The intent of this contribution is to establish a framework for coexistence activities within 802.20. The authors request that 802.20 discuss and affirm the inclusion of coexistence as part of the 802.20 workplan.
Source
Jim Tomcik
Ayman Naguib
Arak Sutivong
jtomcik@qualcomm.com
anaguib@qualcomm.com
araks@qualcomm.com
Notice
This document has been prepared to assist the IEEE P802.20. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release
The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.20.

## Slide 2: Coexistence Issues for 802.20
Dr. James D. Tomcik
jtomcik@qualcomm.com
Dr. Ayman Naguib
anaguib@qualcomm.com
Dr. Arak Sutivong
araks@qualcomm.com

## Slide 3: Co-Existence and Interference Resistance (From Doc 802.20-03/55)
Let’s Not Do It as an Afterthought!!
  Remember the “Alligator” Story!!
Approach
  Define Baseline Scenarios
  Co-existence against the “obvious” services
  Evaluate Projected Impacts of Traditional Technologies on MBWA and Vice Versa
  Co-Channel Interference Models
  Adjacent Channel Interference Models
  Impacts of TDD in Traditionally FDD Bands
  Let’s Identify Issues and Solve Them Before we Create Them

## Slide 4: Coexistence – First Thoughts
Where does Coexistence “Fit” Within the 802.20 Project
  Initially Thought to be Requirements Issue
  Is it part of Evaluation Criteria or Requirements?
Coexistence is a “HUGE” (and Important) Area
  Many Technologies are in Licensed Bands Below 3Ghz
  A Partial List of the Technologies:
    Legacy Cellular: AMPS, TDMA, GSM, IS-95
    3G Cellular: CDMA-2000, WCDMA
    Data Over Cellular: 1xEV-DV, 1xEV-DO, HSDPA, EDGE
    Miscellaneous: LMR, GPS, Others??
  Both TDD and FDD Technologies Have Been Planned by 802.20

## Slide 5: Coexistence Standards Work
IEEE 802:
  Coexistence has become a Major Part of 802’s Standards Development Process
  802 Is Developing Coexistence Scenarios for Unlicensed Technologies (802.11n and 802.15.3a)
Telecommunications Industry Association (TIA)
  TSB-84A(1999) – “Licensed PCS to PCS Interference”
    Develops a Framework for Coexistence Studies
    Develops a “Simplified” and a “Detailed” Approach
    Agreed Upon as a Basis for Studies, Planning, Resolution in the PCS Industry
3GPP and ETSI
  Coexistence is regularly included
  May Have Published Coexistence Framework –
    Need to Investigate Further
Others (802.16.2, 802.11g Adj. Channel Interference Study)

## Slide 6: Coexistence and 802.20
Possible 802.20 Air Interface Styles
  OFDM (?)
  OFDMA (?)
  Single Carrier (?)
  UWB (?)
  Something Else?
Most are Very Different From Existing Air Interfaces
Commercial Spectrum Operators Could Deploy Mixed Technologies
  Different Technologies for Different Services
  Different Availability, Error Rates, etc…
Conclusion: To Avoid Developing a Something Non-Viable, 802.20 Should Address how the Proposed Technology/ies Interacts With Other Technologies
  Intent is a “First Estimate Effort”
  Based on Standards-Type (Not Field, Necessarily) Information

## Slide 7: TIA TSB84A
Multiple Technologies Addressed (8 of Them!)
Establishes a Framework for CoExistence Studies
  Definitions
  General Interference Estimation Procedure
  Interference Estimation Methodologies
    Simplified Methodology
    Detailed Methodology
  Performance/Degradation Metrics
  Generic Receivers and Transceivers and Characteristics
  Propagation Models and Technology Specific Information

## Slide 8: Procedures – Major Steps
Determine Desired Accuracy
  - First Estimates, Field Estimates, System Planning, Resolution
Determine Performance Metric to Use
  - C/I, Receiver Desensitivity, Responses to Interference
Determine Available Input Data
  - Standards Data, Mfr’s Data, Measurements
Simplified or Detailed Methodology?
  - ??
Perform Computation/Simulation
Verify Results

## Slide 9: Interference Estimation – Simplified Process
Concepts: Iterferer and Victim Systems
  Interferer: Known number of interferers, locations
  Victim: Known receiver characteristics, location
Concepts: Victim Geometry and Interferer Geometry
  Victim Geometry: Factors Related to Physical Layout of Victim Receiver
  Interferer Geometry: geographic and physical factors representing the interfering source
Concepts: Victim Characteristics and Interferer Characteristics
  Victim Characteristics: factors related to victim’s performance and reactions to interferers
  Interferer Characteristics: Operating Parameters for Interference Source(s)
Concepts: The Calculation
  Algorithm to determine net values of signal strength of Noise, Desired Signal and Interference
Concepts: Degradation Metric
  Measure Chosen to Determine How Interference Affects the System
  Several Examples Given (e.g. BER)

## Slide 10: Simplified Estimation Process
Interferer
Geometry
Interferer
Characteristics
“Victim”
Geometry
C/(N+Sum(I))
“Victim”
Characteristics
Degradation
Metric
Calculation

## Slide 11: Performance Metrics
Two Methods Highlighted in TSB
Carrier to Noise Plus Interference Ratio
  Method Presumes that Link Performance is Directly Related to a Ratio of Desired Signal Strength to Unwanted Signal Strength
Receiver Desensitivity Degradation
  Presumes that Performance is Related to Increase in Receiver Noise Floor
Others Mentioned
  Eb/No , BER, FER

## Slide 12: Station Characteristics
TSB Develops Generic Receiver Structures for Both Base Station and Mobile Stations
  Structures are Specific to the Interference Problem
  Would have to specify common Front End Approach
TSB Develops Generic Transmitter Characteristics for Base Stations and Mobile Stations
  For the Modeled Transmitter Characteristics, Parameters are Provided
  Would Need To Develop Candidate Transmitter Characteristics for New Technologies

## Slide 13: Summary and Next Steps
Recommend that 802.20 Incorporate Coexistence as Part of the Air Interface Development Process
  Technology Submissions Should Include Parameters to Allow Verification that the Candidate Will Integrate Well in Existing Bands
  Goal is to Provide a First Look/Sanity Check on What’s Developed
  Simplified Process Recommended Where Possible
  802.20 Members Should Work Together to Develop a Common Simulation Approach
    Provides Confidence that the 802.20 Technology Will Minimize Interference with Existing Systems
Should 802.20 Investigate Other Approaches to Interference Estimation?
  TSB 84A Provides an Accepted Framework that could be Leveraged
  Detailed, Understood in the Industry
  Needs Some Extension for Candidate Technologies and TDD