## Slide 1: Coexistence Studies in 802.20
IEEE 802.20 Meeting #3
San Francisco, July 2003
Reza Arefi
reza.arefi@ieee.org
IEEE C802.20-03/72

## Slide 2: Definition of Coexistence
P802.15.2
  The ability of one system to perform a task in a given shared environment where other systems may or may not be using the same set of rules (doc. 99-134r2)
  Quite general but was written in dot15 context
P802.16.2
  No definition of coexistence is provided
802.19 TAG
  The ability of one system to perform a task in a given shared environment where other systems have an ability to perform their tasks and may or may not be using the same set of rules (doc. COEX-02020r1, Sydney meeting)
ITU-R usually refers to it as “Sharing”

## Slide 3: Coexistence Studies
802.19 addresses unlicensed bands coexistence within 802 wireless projects
Coexistence with geographical and/or spectral neighbors is key to successful 802.20 deployments in licensed bands
Objective is to create guidelines for preventing from harmful interference by determining levels of permissible, or acceptable, interference
Interference environment varies with deployment scenarios

## Slide 4: 802.20 Deployment Scenarios
PAR mandates licensed spectrum below 3.5 GHz allocated to the Mobile Service
Deployments under nation-wide licenses are likely to have:
  Multiple operators in the same service area
  Adjacent service areas (domestic as well as international)
Deployments in or adjacent to bands already used for commercial wide area services are also likely
No shared environment
  Co-channel in adjacent areas, or
  Adjacent channel in same area, but
  No co-channel in same area

## Slide 5: Specifics
From regulatory point-of-view, licensed co-channel operation in the same geographical area would not be allowed
Possibilities
  Co-channel across service boundary: geographical neighbors
  Adjacent channel within same service/geographic area: spectral neighbors
  Neighbor could be non-802.20 or another 802.20 of a different duplex
  It could be assumed that 802.20 geographical and spectral neighbors of the same duplex have much easier time coexisting with each other with reasonable coordination
    frame synchronization, power at service boundary, etc.

## Slide 6: Spectral Neighbors, Same Area
802.20 systems may need to coordinate with spectral neighbors
The number and the nature of spectral neighbors TDD and FDD systems may need to coordinate with are not necessarily the same
802.20 TDD
Lower neighbor
Upper neighbor
802.20 FDD
802.20 FDD
Middle neighbor(s)
Upper neighbor
Lower neighbor

## Slide 7: Geographical Neighbors, Same Frequency
Service areas for spectrum currently licensed to the Mobile Service below 3.5 GHz typically don’t overlap
  Protection is typically through power limit at service boundary, which may or may not be sufficient
For TDD-FDD case:
  Safe distance needs to be determined
1
2
Service boundary
f
1
2

## Slide 8: Service Rules
For each band, out-of-band emissions and service boundary levels are specified by regulatory authorities as Service Rules
  Implementations of 802.20 in each band should adopt these values to comply with the rules unless shown to be inappropriate, where more stringent levels should be used
    Example, service providers are voluntarily using tighter specifications than the rules require in the PCS band
Receiver performance, including filters, are typically not specified by the regulators

## Slide 9: Recommended Practice
A Coexistence Task Group could study the coexistence issues of 802.20 deployments in licensed bands below 3.5 GHz
  802.20 TDD with 802.20 FDD, probably the more challenging
  802.20 with non-802.20
This TG will produce a “Recommended Practice” document that gives guidelines and recommends best practices to minimize harmful interference among neighbors
Examples of pervious such activity:
  IEEE 802: 802.16.2 and 802.16.2a
  ITU-R, WP8F: DNR [IMT.COEXT]

## Slide 10: Procedure
Identify bands of interest
  Pick a few “primary candidate” bands
Perform simulations using typical equipment specifications
  Requires feedback from the WG on parameters such as TX power, RX threshold, ACS, ACLR, etc.
If service rules are not adequate, then recommend new guidelines through:
  For a given band, determine “safe” geographical and/or spectral distance between the two potentially interfering systems
  “safe” needs to be quantified, example, I/N= - 6 dB

## Slide 11: Proposal
Form an ad hoc group to work on a Coexistence PAR
Finalize the PAR by September meeting and submit to SEC for approval in November