## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | Repeater issues for MBWA | 
Date Submitted | 2003-09-15 | 
Source(s) | Taewon Ban, Dohyung Choi 6F 1010 Madu-dong Ilsan-gu Koyang-shi Kyunggi-do 411-350, Korea | Voice: 82-31-909-0803 Fax: 82-31-909-0661 Email: {twban, billchoi}@ktf.com
Re: | MBWA Call for Contributions | 
Abstract | This contributions investigates issues on a repeater for MBWA with an operator’s point of view. | 
Purpose | For Your Information | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 
IEEE C802.20-03/75

## Slide 2: Repeater issues for MBWA
Taewon Ban, Dohyung Choi
KT Freetel
Sep. 2003

## Slide 3: Introduction to Repeater
We need repeaters in order to
  Extend cell coverage.
  Remove holes such as in-building and underground within a cell coverage.
We can reduce the RAN deployment cost
  We can acquire wide coverage with low cost.
Types of a repeater
  Optical Repeater : Optical fiber is used between BS and repeater.
  RF Repeater : RF is used between BS and repeater.

## Slide 4: Repeater Deploy Scenario I
Repeater for holes within a cell

## Slide 5: Repeater Deploy Scenario II
Repeater for enhancing coverage

## Slide 6: Statistics for repeaters
Total number of BSs and Repeaters deployed in Seoul, Korea.
Type |  | Total number
Base Station |  | 309
Repeater | For coverage | 380
 | For holes | 9326
 | Subtotal | 9706

## Slide 7: Propagation Delay from repeaters
This is most serious for optic fiber repeaters enhancing coverage.
We can’t lay straight optic fiber from BS and repeaters.
Propagation speed within optic fiber is slower (2e8m/sec)

## Slide 8: Propagation Delay from repeaters (Cont)
For example : Case I
  Cell coverage size = 1000m, Repeater coverage size = 500m
  The length of optic fiber between BS and Repeaer = 1500m (In real system, this is impossible)
  The delay introduced by repeater RF elements = 5usec
  The additional delay from repeater
Propagation delay from BS to MS without repeaters
Optic fiber propagation delay from BS and to an optic fiber repeater
Propagation delay from an optic repeater to MS

## Slide 9: Propagation Delay from repeaters (Cont)
For example : Case II
  Cell coverage size = 3000m, Repeater coverage size = 1000m
  The length of optic fiber between BS and Repeater = 6000m
  The delay introduced by repeater RF elements = 5usec
  The additional delay from repeater
Propagation delay from BS to MS without repeaters
Optic fiber propagation delay from BS and to an optic fiber repeater
Propagation delay from an optic repeater to MS

## Slide 10: Additional delay from Repeaters
Additional propagation delay from repeaters
This issue is applied to all systems.
If a system can’t compensate additional delay spread produced by repeaters, performance will seriously deteriorate.
Notes: 기지국과 중계기로부터 신호를 모두 받는 단말의 경우 delay spread로 인해서 심각한 성능 저하

## Slide 11: Repeater and OFDM
To eliminate ISI (InterSymbol Interference), Guard Interval is introduced for each OFDM symbol.
Additional delay from repeaters should be taken into consideration for guard interval design.

## Slide 12: Repeater and TDD
For UL-DL interference free operation, guard period is introduced considering cell size.
For TDD system with repeaters, the structure of frame should consider this additional delay from repeaters.

## Slide 13: Conclusion
Repeaters are indispensable to mobile systems
Additional delay is introduced by repeaters
  All systems should consider additional delay spread from repeaters
  OFDM should consider repeaters on designing guard interval.
  TDD should consider repeaters on designing frame structure (guard time).