## Slide 1
IEEE C802.20-03/77
Project | IEEE 802 Executive Committee Study Group on Mobile Broadband Wireless Access <http://ieee802.org/20> | 
Title | Summary of delay profiles for MBWA | 
Date Submitted | 2003-09-08 | 
Source(s) | Jin Weon Chang | Voice: +82-31-279-5117 Fax: +82-31-279-5130 Email: jwchang@ieee.org
 | DS (Dong Seek) Park | Voice: +82-31-279-5090 Fax: +82-31-279-5130 Email: dspark@samsung.com
 | Joseph R. Cleveland | Voice: 972-761-7981 Fax: 972-761-7909 Email: jclevela@sta.samsung.com
Re: | 802.20 WG Call for Contributions | 
Abstract | This document provides summary of delay profiles that major international standard organizations suggested. | 
Purpose | Contribute to the discussion and development of the 802.20 Requirements and Channel Model. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802 MBWA ECSG. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: Summary of Delay Profiles for MBWA
Jin W. Chang
jwchang@ieee.org

## Slide 3: Contents
Rationale
Summary of standard delay profiles
  Delay profiles by ITU
  Delay profiles by COST 259
  Delay profiles by 3GPP
  Delay profiles by 3GPP2
Another delay profile reported
Concluding remarks
Recommendations

## Slide 4: Rationale
The intention of this contribution is to help discussions on delay spread in IEEE 802.20 MBWA.
Delay profile is very important since it can have major impact on the system performance.
Agreement needed on specific model set for evaluation criteria

## Slide 5: Delay Profiles by ITU[1]-i
Parameters for channel impulse response model
  Channel A: low delay spread case
  Channel B: median delay spread case

## Slide 6: Delay Profiles by ITU[1]-ii
Indoor office environment

## Slide 7: Delay Profiles by ITU[1]-iii
Outdoor to indoor and pedestrian environment

## Slide 8: Delay Profiles by ITU[1]-iv
Vehicular environment

## Slide 9: Delay profiles by COST 259[2]-i (TU, Typical Urban)
Notes: a research forum funded by the EU
the second successor of COST 207
The models in COST 259 are aimed at UMTS and HIPERLAN, with particular emphasis on adaptive antennas and directional channels.

## Slide 10: Delay profiles by COST 259[2]-ii (RA, Rural Area)

## Slide 11: Delay profiles by COST 259[2]-iii (HT, Hilly Terrain)

## Slide 12: Delay profiles by 3GPP[3]-i
- All taps have classical Doppler spectrum.

## Slide 13: Delay profiles by 3GPP[3]-ii
- All taps have classical Doppler spectrum.

## Slide 14: Delay profiles by 3GPP2[4]-i

## Slide 15: Delay profiles by 3GPP2[4]-ii
- FURP: Fractional UnRecovered Power shall contribute to the interference of the finger demodulator outputs as an independent fader.

## Slide 16: Another delay profile reported
Rappaport, T.S.; Seidel, S.Y.; Singh, R., “900 MHz multipath propagation measurements for US digital cellular radiotelephone,” Global Telecommunications Conference, 1989, and Exhibition. 'Communications Technology for the 1990s and Beyond'. GLOBECOM '89., IEEE , 27-30 Nov. 1989, Page(s): 84 -89 vol.1
Worst profile case for typical operating locations
RMS delay spread
  Urban: 2-3 us
  Hilly: 5-7 us

## Slide 17: Concluding Remarks
Delay spread is less than 10 us for most cases.
But there are certainly cases where the maximum delay spread is longer than 10 us in both ITU and European COST models:
  ITU model vehicular channel B,
  COST 259 HT,
  3GPP model Cases 2 and 7.

## Slide 18: Recommendations
Explicit requirement for delay spread?
Performance evaluation
  Having multi-delay profiles is reasonable for exact performance evaluation
  One profile needs to include taps having delay larger than 10 microseconds.  What performance does MBWA have with large delay spreads?
ITU-R M.1225
  ‘Although large delay spreads occur relatively infrequently, they can have a major impact on system performance.’
  ‘To accurately evaluate the relative performance of candidate RTTs, it is desirable to model the variability of delay spread as well as the “worst case” locations where delay spread is relatively large.’

## Slide 19: References
RECOMMENDATION ITU-R M.1225, “GUIDELINES FOR EVALUATION OF RADIO TRANSMISSION TECHNOLOGIES FOR IMT-2000,” 1997.
3GPP TR 25.943, “Deployment aspects,“ June 2002.
3GPP TS 25.101, "UE Radio Transmission and Reception (FDD),“ December 2002.
3GPP2 TSG-C.R1002, “1xEV-DV Evaluation Methodology (V13.1)”.