## Slide 1: FER: Do We Need It?
Joseph Cleveland
Anna Tee
Jin Weon Chang
Samsung
Spetember 15, 2003
IEEE C802.20-03/83r1

## Slide 2: Outline
Purposes for FER Requirement
Initial Requirement Statement
Comments Summary
Dilemma Posed by Comments
IEEE802 Statement
PDU and SDU Protocol Stack
Reference Model Partitioning
Proposed FER Requirement Model
Proposed FER Requirement Statement
Closing Comments

## Slide 3: Purpose of FER Requirement
Quantify the statement from the PAR:
  “Provide an efficient packet based air interface optimized for IP”
Baseline the minimum performance for the PHY and MAC layers of the air interface
Define a measurable system level performance requirement for air interface reliability

## Slide 4: 4.1.10: Frame Error Rate Requirement Initial Exploder Broadcast
The physical layer shall be capable of adapting the modulation, coding, and power levels to accommodate RF signal deterioration between the BS and user terminals. The air interface may use appropriate ARQ schemes to ensure that error rates are reduced to a suitably low level in order to accommodate higher level IP based protocols (for example, TCP over IP). The frame error rate shall be less than 1 percent, with 95% confidence, after channel decoding and before any link-level ARQ, measured under conditions specified in Section xx.

## Slide 5: Summary of Comments
Reference protocol & structure
  Ensure MAC SDUs error ratio not more than X while having PHY SDUs error ratio = Y
  Define a new layer structure for MBWA systems in IEEE802.20 which includes all features of MBWA characteristics.
  Frame application QoS requirements in a more unified and comprehensive manner through use of the diffserv architecture
  Move all ARQ to the MAC layer
  Requirement as written puts QoS in the PHY
  Should specify post-air-interface-ARQ in scenarios where air interface ARQ is in effect
  Most data comm systems do ARQ in combinations with the QOS

## Slide 6: Summary of Comments (cont)
MAC Protocol
  RLP is very effective in cleaning up the wireless channel so that TCP can be efficiently used.
  There is little difference between RLP frame and physical frame conceptually in cdma2000 systems.
  A funtionality of RLP is necessary but we don't have to use the same RLP as cdma2000 for MBWA.
Frame Size Issue
  Need to have length of frame or number of bits in frame.
  A generic requirement could bias towards short frames
  FER requirement as written favors small frame size
  If FER is taken in the context of maximizing throughput, the MAC layer SHOULD choose the largest possible frame size.

## Slide 7: Summary of Comments (cont)
Service Level
  Different applications having different target FER vs latency tradeoffs
  Air Interface (PHY+MAC) should include mechanisms to allow control of a range of latency vs. data loss/error rates subject to application types
  FER seems to be irrelevant absent the specifics of the design and would have different performance implications for different designs.
  Packet error rate and an operator's actions are deployment issues that more properly belong in the evaluation document
  Remove requirement since MBWA will provide diverse services with different error and ARQ requirements

## Slide 8: Summary of Comments (cont.)
General & misc.
  Requirements for adaptive modulation and coding, and for power control covered elsewhere
  Focus on high level functional requirements and not specify specifics such as frame length.
  Keep the requirement “simple”
  If spectral efficiency is the primary requirement here, then perhaps we do not need a separate frame error rate requirement.

## Slide 9: The FER Requirement Dilemma
Make it simple
Make it measurable
Make it inexpensive to test
  Specify by application type increases testing cost
Make it application independent
  Addressing all possible applications unrealistic
  Terminal providers will need a common base line for optimal IP network performance
versus
Do not have a baseline FER requirement
LETS LOOK AT THE BASICS

## Slide 10: IEEE Std 802®-2001: 7.3 Error Rates
Error performance of IEEE 802 LANs and MANs is required to be such as follows:
  b) For wireless physical media: Within a single access domain, the probability that a MAC Service Data Unit (MSDU) is not delivered correctly at an MSAP of an intended receiving MAC service user, due to the operation of the Physical layer and the MAC protocol, shall be less than 8 × 10-8 per octet of MSDU length.
  c) The probability that an MSDU delivered at an MSAP contains an undetected error, due to operation of the MAC service provider, shall be less than 5 × 10-14 per octet of MSDU length.

## Slide 11: PDU and SDU In Protocol Stack
SDU
SDU
PDU
PDU
Layer N SAP
Sending Entity
Receiving Entity
Layer N+1 SAP
Layer N-1 SAP
SDU
PDU
SDU
PDU
Layer N
Layer N+1

## Slide 12: Reference Model Partitioning
PMD
Sublayer (Radio)
PLCP
Sublayer (FEC)
MAC
Sublayer
PhSAP
PMD_SAP
Data Link
Layer
PHY
Layer
LSAP: LLC Service Access Point
MSAP: MAC Service Access Point
PhSAP: PHY Service Access Point
PLCP: PHY Layer Convergence Protocol
PMD: Physical Medium Dependent
LSAP
MPDU
MSDU
LLC
Sublayer
MSAP

## Slide 13: Proposed FER Requirement Model
Specify FER or BER for SDU delivered to MSAP
Specify FER or BER for SDU delivered to PhSAP
Require flexibility to disable ARQ or to operate at higher FER or BER for SDU frames
Give requirements for specific applications in Evaluation Document
Data Link
Layer
PMD
Sublayer (Radio)
PLCP
Sublayer (FEC)
MAC
Sublayer
PhSAP
PMD_SAP
PHY
Layer
LSAP
LLC
Sublayer
MSAP

## Slide 14: Recommended FER Requirement
The PHY and MAC layers SHALL be capable of adapting the modulation, coding, FEC and ARQ and power levels to ensure that SDU frame error rates are reduced to a level to meet performance requirements of higher protocol layers (e.g., TCP over IP).
For a frame error rate of TBD for a 1024 byte SDU frame size delivered to the PhSAP, the probability that a MSDU is not delivered correctly at an MSAP due to the operation of the Physical layer and the MAC protocol, SHALL be less than TBD per octet of MSDU length.
The PHY and MAC layers MAY operate at higher frame and octet error rates for different applications, such as for decrease latency in real time applications (e.g., VoIP or streaming video).

## Slide 15: Closing Comments
Need a defined reference model first
Need reference model layer and sublayer functions defined
Need a requirement that defines the expected performance baseline for the “IEEE802.20 air interface optimized for IP”
Need adherence to existing IEEE802 specifications