## Slide 1
IEEE C802.20-03/87

## Slide 2: Status of 802.20 Evaluation Criteria
IEEE 802.20 Evaluation Criteria CG
IEEE 802.20 Interim Meeting
September 15-19, 2003

## Slide 3: Evaluation Criteria Status
Two conference calls since the July plenary
Consensus reached on several issues:
  Cell layout, Full-duplex simulations, TCP model, backhaul network delay and loss models
Version 05 of the Evaluation criteria document available (C802.20-03/78).
Open issues:
  Sectorization, mobility modeling, higher layers protocol models, control signaling models, definition of spectral efficiency, fairness criteria and performance metrics etc.
Three conference calls scheduled between the September interim and November plenary
Notes: 10/7,28 11/4 12:00 – 2PM EDT

## Slide 4: Cell Layout
Decision to use 19-cells Wrap-around technique for system simulations.
Statistics collected from all the cells.

## Slide 5: Fully-duplex Simulations
Decision to include both UL and the DL in a fully duplex fashion in the same simulation run.
Allow to accurately model the traffic, physical and MAC layer dependencies between the uplink and the downlink.
This issue can be revisited later on as more details on the evaluation methodology, channel models, traffic models and proposals become available.

## Slide 6: TCP Model
Decision to use a simplified TCP model:
  connection establishment phase
  slow start phase
  connection release phase
Other details of TCP such as congestion avoidance are not modeled.
The details of the model are specified in in the Evaluation criteria document.

## Slide 7: Network delay/loss model
Decided not to model any packet loss in the Internet (lossless packet transmission)
Decision to model the one-way Internet packet delay using a shifted Gamma distribution:
  The delay is independent from packet to packet.

## Slide 8: Sectorization
The question is what should be the number of sectors per cell modeled?
The issue is also related to modeling of the multiple antenna techniques
Should there be a single mandatory baseline configuration e.g. omni-cell, 3-sector cell etc?

## Slide 9: Spectral efficiency
How to define the spectral efficiency in the context of multi-sector and/or multiple-antenna cells?
  B/s/Hz/cell ?
  b/s/Hz/sector ?
  b/s/Hz/antenna ?
Need to arrive on a acceptable definition of spectral efficiency so that different proposals can be compared on a fair basis.

## Slide 10: Mobility model
The CG decided not to model the actually moving mobiles in the simulations
Mobility at the physical layer is taken care of by modeling fast fading corresponding to the mobile speed.
However, some mobility model is still needed e.g. in order to analyze the handoff schemes etc.

## Slide 11: Higher Layer Protocols
Need input from requirements and the traffic modeling CG on the types of applications supported.
Models for higher layer protocols such as HTTP, RTSP and RTP etc. as applicable can then be specified.

## Slide 12: Control signaling modeling
Examples of control signaling are scheduling grants transmission, channel quality feedback, and ARQ ACK/NACK Feedback etc.
MAC states and signaling to enable state transitions modeled explicitly in the system simulations.
Inputs needed

## Slide 13: Performance Metrics
List of performance metrics is incomplete.
Input needed from the traffic modeling CG on the list of applications supported before the application specific performance metrics can be defined.

## Slide 14: Fairness criteria
A fairness criteria needed in order to guarantee minimal level of throughput to all users in the system.
A fairness criteria can be defined as a constraint on the user throughput CDF
  For example, normalized throughput CDF should lie to the right of the Fairness criteria curve.
Input needed