## Slide 1: An Alternative Approach for Enhancing Security of WMANs using Physical Layer Encryption By Arpan Pal Wireless Group Center of Excellence for Embedded Systems Tata Consultancy Services India
IEEE C802.20-03/88

## Slide 2: Agenda
Security Threats of Wireless MAN
Proposed System Overview
Proposed System Features
How the proposed system mitigate the security
threats
Conclusion

## Slide 3: Security Threats of Wireless MAN
Human Initiated Events
Data Privacy
Data Forgery
Denial of Service
Hardware Errors
Data Privacy, Data Forgery and Denial of Service
are the main security events that need to be addressed
Ref:- Alan Chickinsky, “Wireless Security Threats”,
IEEE C802.20-03/06, January 2003

## Slide 4: System Overview – Traditional System
Read Transmitted PHY params info
Configure
Baseband PHY Transmitter
PHY config params
Framed data from Media Access Control (MAC) layer
Transmitter Front-end
sent using prior-known PHY config
PHY params info
+
Add before actual data
Transmitter
PHY config params
Framed data To Media Access Control (MAC) layer -
Hacker can access only at here
Receiver Front-end
Receiver
Baseband PHY Receiver
Configure
Decode Tx PHY params info using prior-known PHY config

## Slide 5: System Overview – Proposed System
Read Transmitted PHY params info + KEY2
Configure
Baseband PHY Transmitter
PHY Transmitter config params
Framed data from Media Access Control (MAC) layer
Transmitter Front-end
sent using prior-known PHY config
PHY Transmitter param info + KEY2
+
Add before actual data
Transmitter
PHY Receiver config params
Framed data To Media Access Control (MAC) layer -
Hacker can access only at here
Receiver Front-end
Receiver
Baseband PHY Receiver
Configure
Decode transmitted PHY params info using prior-known PHY config
Modifications to Tx Algorithms based on KEY2
Encrypt with KEY1
Modifications to Rx Algorithms based on KEY2
Decrypt with KEY1

## Slide 6: Proposed System Features
KEY1 delivered to valid users using some secure
key distribution mechanism
Possible Physical layer system parameters encrypted
using KEY1
  Error Control Coding Rate
  Type of Modulation
  Length of Packet
  Second Level Key KEY2
Possible Physical layer system parameters modified
using KEY2
  Interleaving Pattern
  Phase offset of OFDM symbols
  Constellation Mapping

## Slide 7: Proposed System - Example
KEY2 can be varied from packet to packet
One may modify using random numbers seeded by KEY2
  Phase offset of OFDM symbols at IFFT input
  Note:- Phases of only data points (excluding pilots and zero padding) should be altered
Error Control Coding Rate
Modulation Type
Packet Length
KEY2
XOR
Random No. Generator
Encrypted Output
KEY1

## Slide 8: Proposed System – Application to 802.20
Physical Layer of 802.20 is evolving
OFDM could be an integral part of PHY given the
operational scenario
The proposed scheme can easily be adapted
to the 802.20 OFDM PHY
The proposed scheme is not limited to OFDM PHY only

## Slide 9: Mitigation of Security Threats - Data Privacy
Known-Plaintext Attack
Recording of encrypted data at MAC level
Key can be found out if Data is known
Proposed Scheme prevents hackers from recording correct
encrypted data at MAC level
  ( wrong FEC rate, wrong modulation, unknown phase
  offset, unknown interleaving pattern etc.)

## Slide 10: Mitigation of Security Threats - Data Forgery
Unauthorized users insert data into network as valid user
  Replay
  Mimicking
Proposed Scheme prevents hackers from both Replay and
Mimicking
  Replay is not possible as the data recorded at MAC layer
  is totally wrong and hence cannot be replayed
  to generate a valid message
  Mimicking is not possible because this needs finding out
  the key first (using Known-Plain-Text attack)

## Slide 11: Mitigation of Security Threats - Denial Of Service
Intruder can flood network with valid and invalid messages
Channel jamming at RF level
Proposed Scheme prevents hackers from sending valid
messages as they don’t know the Key
Invalid messages can be filtered out in the PHY level as
the encryption is taking place in PHY layer itself
Channel jamming at RF level cannot be prevented

## Slide 12: Conclusion
Data Privacy, Data Forgery and Denial-of-Service
(valid messages) at MAC layer (software) can be prevented
Denial-of-Service (invalid messages) can be prevented
using PHY layer message integrity check
Denial-of-Service (Channel jamming at RF level)
cannot be prevented
To break into the proposed security scheme, hackers need
costly hardware set-up
Even with Hardware set-up, breaking the system
in Real-time is extremely difficult – the PHY level ciphering
substantially increases the entry barrier for break-in
A good KEY distribution scheme need to be explored

## Slide 13: Thank You
Email: arpan_pal@tcscal.co.in