## Slide 1: Status of 802.20 Channel Models
IEEE 802.20 WG Session #4
September 15-19, 2003
Qiang Guo
Editor, Channel Modeling Correspondence Group
C802.20-03/89

## Slide 2: Current Status of 802.20 Channel Models
A conference call has been held since July plenary
Consensus reached on a few channel model issues:
  Inclusion of outdoor-to-indoor model into channel model set
  Unifying MIMO/SIMO/MISO/SISO channel models
Open issue
  Two discrepant views on the maximum delay spread in MBWA channel models and the frequency of occurrence of such channels in the real world
Two more conference calls scheduled
  October 14, 2003,2:00 - 3:00pm EDT
  October 29, 2003, 2:00 - 3:00pm EDT

## Slide 3: Outdoor-to-Indoor Model
Decided to examine the ITU pedestrian model as starting point and then look into how to extrapolate it to the outdoor-to-indoor model
There was also a consensus that very little is known about the MIMO nature of outdoor-indoor model

## Slide 4: ITU Outdoor-to-Indoor and Pedestrian Model [1]
BS with low antenna heights, located outdoor
Small cell size
Low transmit power
Pedestrian users located on streets and inside building
Doppler rate set by walking speeds, with occasional higher rates due to vehicular reflections
Geometrical path loss rule of R-4 is appropriate, but R-6 may be encountered due to trees and other obstructions
Building penetration loss averages 12 dB with a standard deviation of 8 dB

## Slide 5: MIMO/SIMO/MISO/SISO Models
Decided to specify MIMO channel model first, and then tweak the parameters so that it will approximate the characteristics of SIMO/MISO/SISO models
Need to specify guidelines for setting the key parameters of model based on a selected set of test environments, such as micro/macro, typical urban/suburban/rural, outdoor-to-indoor, etc
Making sure the model have appropriate delay spread, Doppler spread, and spatial characteristics that are typical of licensed bands below 3.5 GHz

## Slide 6: MIMO/SIMO/MISO/SISO Models (Cont)
Considering separate SISO models would confuse the process of comparing SISO techniques to MIMO/MISO/SIMO techniques, because it would be difficult to guarantee a fair comparison between the two
The spatial characteristics of MIMO model will heavily influence the Doppler characteristics, which would make it difficult to compare a Jakes-faded SISO model to a spatial MIMO model

## Slide 7: Maximum Delay Spread
Two different opinions on the maximum delay spread in MBWA channel models and the frequency of occurrence of such channels in the real world
  Need to define a vehicular channel model for MBWA, which would have power delay profile less than ITU Vehicular B
  Satisfy ourselves with the ITU Vehicular B model
In order to accurately evaluate candidate physical-layer technologies, it is desirable to model the variety of delay spreads, which is justifiable based on real world channel measurements.
Information regarding delay spread measurement campaign would help 802.20 Channel Modeling CG understand the issue and reach group consensus

## Slide 8: Delay Spread Measurements on a Mobile Broadband Channel at 3.6 GHz [2,3]
As reported in [2,3], an experimental mobile broadband communication system developed for the purpose of evaluating candidate physical-layer technologies
Data collected by this experimental system also used to characterize the 2x2 MIMO channel impulse responses
The delay spread characteristics of a 20MHz channel at 3.675 GHz is summarized here, based on a series of field experiments conducted in a suburban area
As described in [3], outdoor measurements were performed on various driving routes around the base
Vehicle speed varies from 0 to 60 mph

## Slide 9: Delay Spread Measurements on a Mobile Broadband Channel at 3.6 GHz [Cont]
Delay spread measurements are calculated from power delay profiles given by the magnitude squared of the estimated channel impulse response
The channel impulse response is determined with a frequency-domain channel estimator designed using the fact that all the transmitted data is known
A correlator operating in the time-domain was also designed to detect multi-path components with delays of up to 25 μS
With this correlator, it was observed that the maximum delay spread beyond 10 μS is statistically insignificant
  A total of 5474 profiles, including 2142 profiles captured at LOS locations and 3332 profiles captured at NLOS locations

## Slide 10: Statistics of RMS and MAX Delay Spread (in micro-second)
 | ALL | LOS | NLOS
RMS Delay Spread in 95% | 1.75 | 0.90 | 2.0
Max Delay Spread in 95% | 5.3 | 2.3 | 6.1

## Slide 11: References
Recommendation ITU-R M.1225, “Guideline for Evaluation of Radio Transmission Technologies for IMT-2000,” 1997.
C802.20-03/12, “Antenna Arrays for MBWA: Overview and Field Experiments”.
C802.20-03/19, “Frequency-Domain-Oriented Approaches for MBWA: Overview and Field Experiments”.