## Slide 1: Preparing for Convergence
Joseph Cleveland
Jim Mollenauer
Anna Tee
IEEE C802.20-03/97

## Slide 2: Topics
Proposed Requirement
Rationale
  Ubiquitous Services
  Wireless World
  Business / Market Environment
  Use Case Scenarios
  Planned Converged Solutions
Considerations

## Slide 3: Proposed Requirement
The system shall provide the capability to handoff a call session from one 802.20 BTS to another 802.20 BTS based on system loading, signal strength, capacity and tier of service. Additional weighting factors may also include back haul loading, least cost routing, location, velocity.
The 802.20 system shall provide the capability to bridge networks at Layer 2 per IEEE 802.1 Logical Link Control (IEEE 802.2).
The system shall provide the capability to interoperate with other wireless networks (e.g., GSM/EDGE, CDMA2000, 1XEV/DO, etc.) in order to transfer a call session between an 802.20 BTS and an access point (i.e., BTS) in the other network. The interworking between networks shall be based on Mobile IP.

## Slide 4: Model for Convergence & Interoperability
802.3
MAC
802.3
PHY
802.11
MAC
802.11
PHY
802.15
MAC
802.15
PHY
802.16
MAC
802.16
PHY
802.20
MAC
802.20
PHY
802.2 Logical Link Control
802.1 Bridging
Physical
Layer
Data
Link
Layer
IPv6 / Mobile IP
App
1
App
N
• • • •
SIP
• • •
3G/DO/DV
MAC
3G/DO/DV
PHY
LAC
Convergence
Layers
Convergence / Interworking at Layer 2

## Slide 5: Rationale: Ubiquitous Experience
Work
Domain
Home
Domain
Mobile
Domain
Portable Remote
Access Services
Field Service Apps
Hotel/Motel
Portable Services
Mobile Commerce
Services
Mobile Office (Voice
and Data Apps)
High BW Connectivity
Video Streaming
-
Conferencing Apps
Portable
Office
Reservations
-
Listings
Directions Services
Video Streaming
-
Conferencing Apps
Video Streaming
-
Conferencing Apps
Seamless
Ubiquitous
Experience
IEEE802.20 Objective:

## Slide 6: Rationale: Market / Business Environment
Ubiquitous experience  Convergence of services
  Multiple air interfaces will be available
  No one air interface will provide ubiquitous experience
  Expect to support for cellular services on the WLAN segment
  ‘Handoff’ from high-cost macro-network  WLAN/WPAN
Providers need flexible deployment options
  Limited initial 802.20 coverage
  Convergence (interworking?) expected with ‘existing’ services
  Options for more advanced interworking

## Slide 7: Rationale: Market / Business Environment
Vendors need well-defined requirements
  High volume for low cost
  HO / interworking signaling support common across vendors
  Interoperability + compliance testing a “must”

## Slide 8: Rationale: Global Wireless Standards
IEEE 802.15 Bluetooth
IEEE802.15.3a
UWB
MAN
<20 km
LAN
<100 m
PAN
<10 m
ETSI HiperPAN
IEEE 802.11 WirelessLAN
ETSI HiperLAN
IEEE 802.16 WirelessMAN
ETSI HiperMAN HIPERACCESS
IEEE 802.20
(proposed)
3GPP, GSM/EDGE
WCDMA
3GPP2
CDMA2000
1xEV/DO/DV
Notes: <number>
<footer>
<header>
<date/time>
ETSI HIPERMAN following 256 OFDM mode of 802.16a

## Slide 9: Rationale: Planned Converged Solutions
Marketplace is moving to converged solutions
  GSM/EDGE + WiFi
  GSM + Bluetooth
  CDMA2000 +WiFi
  IP-Based PBX + WiFi
  IP-Based PBX + CDMA2000
  IP-Based PBX + CDMA2000 + WiFi

## Slide 10: Use Case: Wireless Platforms
Portable
Licensed and Unlicensed
Consumer DSL level service
Mobile
Licensed
Wideband Data Rates
Nomadic
Cellular
Wideband
2.5G, 3G
802.20
Destination
Based
802.11 Hot Spots
802.16e
Localized
Based
802.15 PANs

## Slide 11: Use Case: Nomadic / Mobile Scenario
INTERNET
BACKBONE
SEEKS BEST
CONNECTION
802.11
Connection
802.20
CDMA2000

## Slide 12: Use Case: Coverage Domains and Throughput
Cdma2000
1xEV/D0/DV
GPRS
UWB
802.15.3a
WLAN
802.11b
Throughput (Mbps)
50
10
2
1
100
10
50
1000
500
Blue
tooth
Range (m)
No Mobility
Mobility
802.20

## Slide 13: Considerations: High Throughput and Mobility
Higher throughput at longer ranges
  Better bits/second/Hz at longer ranges
Scalable system capacity
  Interoperability provides easy addition of channels to maximize cell capacity
  Flexible channel bandwidths accommodate allocations for both licensed and unlicensed spectrum
Quality of Service
  Connection oriented MAC supports data, voice and video
  Definable service levels
  Ubiquitous coverage support
    Interoperable with other IEEE802 air interfaces
    Interoparable with other macro-cell networks
Cost & Investment Risk
  Interoperable equipment lets operators purchase equipment from more than one vendor
  A stable, standards-based platform improves OpEx by sparking innovation in services, coverage, applications, convergence
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Considerations: Support Recommendations
Define MAC functionality
  MAC sub-layers must be clearly defined
  Separate control block must be included in the MAC which controls the establishment of channels
  Define bidirectional primitives (MAC  PHY) for triggering handoffs
  Define timing parameters and allowed latency for primitives
Define LLC functionality
  Common LLC is used across all the 802.xx family of standards
  Provide hooks in LLC for better interoperability with handoff management
  Use same hooks for the LLC and the MAC
Define addressing principles
Define interface requirements to upper layers
Define triggers and supporting algorithms

## Slide 15: Considerations: Definitions
Plan for multiple AT vendors and interoperability + compliance testing
Plan for multiple AP/Node-B vendors and interoperability + compliance testing
Access terminal decides HO / Interworking action
Support for ubiquitous network - Always Best Connected