## Slide 1: IEEE 802.20 MBWA Standard Development Project
Presentation of Contribution C802.20-03-98 Nov-11-2003
Dan Gal, email: dgal@lucent.com
Title: Evaluation of 802.20 Proposals – Coexistence-Affecting Characteristics

## Slide 2: Purpose
Help define a criteria for evaluating the Coexistence capabilities of IEEE 802.20 technology proposals.

## Slide 3: Outline
The ITU-R IMT-2000 evaluation process.
RF characteristics that determine a radio transceiver’s ability to coexist with other mobile radio technologies.
Recommendations

## Slide 4: ITU-R Reference Documents
[1] Recommendation M.1455: “KEY CHARACTERISTICS FOR THE INTERNATIONAL MOBILE TELECOMMUNICATIONS-2000 (IMT-2000) RADIO INTERFACES” [2] Recommendation SM.329-7: “SPURIOUS EMISSIONS”
[3] Recommendation M.1225: “GUIDELINES FOR EVALUATION OF RADIO TRANSMISSION TECHNOLOGIES FOR IMT-2000”

## Slide 5: ITU-R IMT-2000’s Key Characteristics
The IMT-2000 3G Radio Transmission Technologies (RTT) evaluation process required data on key RF characteristics.
They were defined in ITU-R Recommendation. M.1455 [1]
The key RF characteristics that determine a radio’s coexistence performance are highlighted below (in the next slide)

## Slide 6: Coexistence-Affecting Key RF Performance Characteristics (1/2)
Radio Transmitter:
Transmit power & emission mask
ACLR*
Spurious Emissions
Frequency Accuracy & Stability * ACLR = Adjacent Channel Leakage (power) Ratio

## Slide 7: Coexistence-Affecting Key RF Performance Characteristics (2/2)
Radio Receiver:
Sensitivity
Intermodulation sensitivity
Blocking
Spurious response
Selectivity

## Slide 8: Transmitter Characteristics (1/5)
3.3.1 Emission Mask
The maximum transmit power and emission mask should be stated (for both MS and BS).
If the proposed radio technology supports several power classes, they should be specified as well.
Test results and a statement on the specified emission mask(s) are required.

## Slide 9: Transmitter Characteristics (2/5)
3.3.2 ACLR
ACLR is defined as the attenuation of the transmit power which is “spilled” into the adjacent channels (due to filtering imperfections).
It is measured relative to the carrier signal power and expressed as dBc attenuation values.
ACLR is a function of the frequency offset from the assigned channel frequency.
Test results and a statement on the specified ACLR are required.

## Slide 10: Transmitter Characteristics (3/5)
3.3.3 Spurious Emissions
ITU-R Recommendation M.329-7 [2] defines spurious emissions as “Emission on a frequency, or frequencies, which are outside the necessary bandwidth and the level of which may be reduced without affecting the corresponding transmission of information. Spurious emissions include harmonic emissions, parasitic emissions, intermodulation products and frequency conversion products but exclude out-of-band emissions.”

## Slide 11: Transmitter Characteristics (4/5)
3.3.3 Spurious Emissions (cont’d)
Spurious emissions are generated by non-linear components in the transmitter in the process of carrier signal generation, mixing, modulation and amplification.
Test results and a statement on the specified performance levels for each type of spurious emission are required.

## Slide 12: Transmitter Characteristics (5/5)
3.3.4 Frequency Accuracy and Stability
Frequency accuracy is expressed in PPM (parts per million) and is a measure of the frequency deviation from the assigned carrier frequency.
Frequency stability is a measure of this deviation that is caused by operational time-varying factors such as temperature, humidity etc.
Test results and a statement on the specified frequency accuracy and stability are required.

## Slide 13: Receiver Characteristics (1/5)
3.3.5 Receiver Sensitivity
Reference [1] defines receiver sensitivity as the minimum power, measured at the antenna port, at which the frame error rate (FER) or bit error rate (BER) are below a certain specified limit.
Sensitivity is a function of the information bit rate, Eb/No, temperature and the receiver noise-figure (NF).
Test results and a statement on the specified receiver sensitivity levels are required.

## Slide 14: Receiver Characteristics (2/5)
3.3.6 Intermodulation Sensitivity
Defined as the levels of out-of-band interfering signals that when mixed in the receiver front-end, produce an in-band third order non-linearity product.
Test results and a statement on the specified receiver intermodulation sensitivity levels are required.

## Slide 15: Receiver Characteristics (3/5)
3.3.7 Receiver Blocking
Receiver blocking is the effect of a strong out-of-band signal, present at the input of the receiver, on the receiver’s ability to detect an in-band wanted signal.
The blocking signal reduces the specified receiver sensitivity by a certain number of dB's.
Test results and a statement on the specified receiver blocking performance levels are required.

## Slide 16: Receiver Characteristics (4/5)
3.3.8 Spurious Response
Spurious response in a receiver occurs when unwanted signals, having frequencies other than the tuned frequency, produce a receiver output as if they were wanted signals.
Spurious response is specified in terms of the frequencies and signal levels that produce such unwanted receiver output.
Test results and a statement on the specified receiver spurious response performance are required.

## Slide 17: Receiver Characteristics (5/5)
3.3.9 Selectivity
Receiver selectivity is a measure of the receiver’s ability to reject signals from adjacent channels while receiving a wanted signal on its tuned frequency.
Selectivity is specified as the ratio (in dB) of the adjacent channel signal level to the assigned channel signal level in which a reference BER/FER is maintained.
Test results and a statement on the specified receiver selectivity performance are required.

## Slide 18: Recommendations
Adopt and incorporate this contribution into the 802.20 Evaluation Criteria document.
Define a detailed evaluation methodology for assessing the coexistence capability (of proposals) in a well defined representative RF environment and scenarios.