## Slide 1: Status of 802.20 Channel Models
IEEE 802.20 WG Session #6
January 12-15, 2004
Qiang Guo
Editor, Channel Modeling Correspondence Group
C802.20-04/01

## Slide 2: Current Status of 802.20 Channel Models
A list of key working items have been identified and sent to the email reflector:
    Add Indoor Pico-cell to the MBWA channel environments;
    Investigate the MIMO nature of Outdoor-to-Indoor model;
    Determine the reference values of spatial channel model parameters;
    Determine and validate the statistical distributions of PAS and angular parameters in both CASE-IV & CASE-V;
    Provide the detailed algorithm for generating channel model parameters in various MBWA channel environments;
    Investigate and determine the correlation values between channel model parameters;
    Model inter-cell/inter-sector interference;
    System level calibration and implementation;
    Provide the algorithm for generating channel model parameters in the case of antenna polarization (optional);

## Slide 3: Indoor Pico-Cell Channel Environment
The ITU Indoor Office Model [1] is proposed as the MBWA Indoor Pico-cell channel environment
This selection is consistent with the rest of MBWA channel environments
This environment is characterized as
  Very small cell radius (approximately 100m BS-to-BS distance),
      Based on ITU Indoor Office Deployment Model, 10000 per floor (total 10 floors)
      A large office building with an open floor plan layout, with1000 potential user per floor
      Office cubicles are separated by movable partitions
  Both base stations and pedestrian users are located indoor
  High angle spread and very low delay spread
  Low mobility (0 – 3 km/h)
  The model is sensitive to antenna heights and scattering environment (such as walls, floors, and metallic structures)

## Slide 4: Path Loss Model for Indoor Pico-Cell
The indoor path loss is based on the COST 231 model:
where R is the distance between BS and MS in meters, n is the number of penetrated floors (n=4 is an average for indoor office environment)
A log-normal shadow fading standard deviation of 12 dB can be expected for indoor pico-cell
Fading ranges from Ricean to Rayleigh with Doppler frequency offsets set by walking speeds

## Slide 5: Percentage of ITU Channel Environments
Test Environment | Channel A |  | Channel B | 
 | rms Delay Spread (ns) | Percentage of Occurrence (%) | rms Delay Spread (ns) | Percentage of Occurrence (%)
Indoor Office | 35 | 50 | 100 | 45
Outdoor-to-Indoor and Pedestrian | 45 | 40 | 750 | 55
Vehicular | 370 | 40 | 4000 | 55

## Slide 6: Indoor Pico-Cell Test Environment
MODELS |  | CASE-VI |  | CASE-VII | 
PDP |  | Indoor-A |  | Indoor-B | 
Doppler Spectrum |  | Classical |  | Classical | 
No. of Paths |  | 6 |  | 6 | 
Path Power (dB) | Delay (ns) | 0 | 0 | 0 | 0
 |  | -3.0 | 50 | -3.6 | 100
 |  | -10.0 | 110 | -7.2 | 200
 |  | -18.0 | 170 | -10.8 | 300
 |  | -26.0 | 290 | -18.0 | 500
 |  | -32.0 | 310 | -25.2 | 700
Speed (km/h) |  | 3 |  | 3 | 

## Slide 7: Indoor Pico-Cell Test Environment
Channel Scenario | Urban Micro | Indoor Pico
Number of paths (N) | 6, 11 | 6, 12
Number of sub-paths (M) per-path | 20 | 20
Mean AoD at BS | 200 | 200
Per-path rms AS at BS | 5o (LOS and NLOS) | 25o , 35o (LOS and NLOS)
BS per-path PAS Distribution | Laplacian | U(-180o, 180o)
Mean AoA at MS | 680 | 680
Per-path rms AS at MS | 350 | 1050
MS Per-path PAS Distribution | Laplacian | U(-180o, 180o)
Mean total RMS Delay Spread | 0.251s | 0.035, 0.1s
Distribution for path delays | U(0, 1.2s) | U(0, 0.31s), U(0, 0.7s)
Lognormal shadowing standard deviation | NLOS: 10dB LOS: 4dB | NLOS: 12dB LOS: 4dB
Pathloss model (dB), d is in meters | NLOS: 34.53 +38 log10(d) LOS: 30.18 + 26log10(d) | 

## Slide 8: Outdoor-to-Indoor Model
Decided to examine the ITU pedestrian model as starting point and then look into how to extrapolate it to the outdoor-to-indoor model
There was also a consensus that very little is known about the MIMO nature of outdoor-to-indoor model

## Slide 9: ITU Outdoor-to-Indoor and Pedestrian Model [1]
BS with low antenna heights, located outdoor
Small cell size, low transmit power
Pedestrian users located on streets and inside building
Doppler rate set by walking speeds, with occasional higher rates due to vehicular reflections
Geometrical path loss rule of R-4 is appropriate, but R-6 may be encountered due to trees and other obstructions
Log-normal shadow fading w/ standard deviation of 10 dB for outdoors and 12 dB for indoor
Building penetration loss averages 12 dB with a standard deviation of 8 dB

## Slide 10: ITU Outdoor-to-Indoor and Pedestrian Deployment Model [1]
Potential subscribers include both outdoor and indoor users
The indoor coverage is to be provided by the outdoor base stations
This requires that additional loss duo to building penetration be accommodated in the link budget

## Slide 11: Outdoor-to-Indoor MIMO Channel Model
The MIMO channel matrix can be separated into a LOS matrix and a NLOS Rayleight matrix [5]
The LOS matrix is an option for urban micro, outdoor-to-indoor, and indoor pico-cell only
LOS modeling will not be defined for suburban or urban macro cases duo to the low probability of occurrence

## Slide 12: Outdoor-to-Indoor MIMO Channel Model
For the NLOS case, the Ricean K factor is set to 0, thus the fading is determined by the combination of sub-rays
For the LOS case, the Ricean K factor is based on
where d is the distance between MS and BS in meters
The probability for LOS or NLOS depends on various environmental factors
For simplicity, the probability of LOS is defined to be unity at zero distance, and decreases linearly until a cutoff point, e.g, at d=433m, where the LOS probability is zero

## Slide 13: Outdoor-to-Indoor MIMO Channel Model
The K-factor and shadow fading standard deviation will all be chosen based on the selected outdoor-to-indoor path, i.e., from LOS to NLOS

## Slide 14: Reference Values of MIMO Model
For the purpose of link level simulations, reference values of the average correlation are given below [6]
The reference values are provided for the calibration of simulation software

## Slide 15: Reference Values of MIMO Model
 | Antenna Spacing | AS (degrees) | AOA (degrees) | Correlation (magnitude) | Complex Correlation
BS |  | 5 | 20 | 0.9688 | 0.4743+0.8448i
 |  | 2 | 50 | 0.9975 | -0.7367+0.6725i
 |  | 5 | 20 | 0.3224 | -0.2144+0.2408i
 |  | 2 | 50 | 0.8624 | 0.8025+0.3158i
 |  | 5 | 20 | 0.0704 | -0.0617+i0.034
 |  | 2 | 50 | 0.5018 | -0.2762-i0.4190
MS |  | 104 | 0 | 0.3042 | -0.3042
 |  | 35 | -67.5 | 0.7744 | -0.6948-i0.342
 |  | 35 | 22.5 | 0.4399 | 0.0861+0.431i
 |  | 35 | 67.5 | 0.7744 | -0.6948+i0.342

## Slide 16: References
Recommendation ITU-R M.1225, “Guideline for Evaluation of Radio Transmission Technologies for IMT-2000,” 1997.
Draft 802.20-PD V10, “802.20 Requirements Document”.
J. Medbo and P. Schramm, “Channel Models for HIPERLAN/2 in Different Indoor Scenarios”, ETSI BRAN 3ERI085B.
ETSI UMTS 30.03 V3.2.0, “Selection Procedures for the Choice of Radio Transmission Technologies of the UMTS”, 1998.
J.P. Kermoal, L. Schumacher, P.E. Mogensen and K.I. Pedersen, “Experimental investigation of correlation properties of MIMO radio channels for indoor picocell scenario,“ in Proc. IEEE VTC2000 Fall, Boston, MA, vol. 1, Sept. 2000, pp. 14-21.
3GPP & 3GPP2 SCM AHG, “Spatial Channel Model Text Description”, SCM Text V6.0.