## Slide 2: VoIP Models for 802.20 System Performance Evaluation
Farooq Khan
IEEE 802.20 Interim Meeting
Vancouver, BC, Canada
January 12-16, 2004

## Slide 3: Voice over IP (VoIP)
The MBWA will support VoIP services.
QoS will provide latency, jitter,
and packet loss required to enable
the use of industry standard Codec’s.

## Slide 4: VoIP Capacity Analysis
VoIP capacity can not be estimated based on raw data throughput:
  Assuming 10Kb/s voice source, theoretical capacity of 802.11b is 11M/10K=1100  550 two-way VoIP sessions.
  However, in practice only a few VoIP users can be supported in 802.11b!
  The reasons for such a low capacity are:
      Low payload to overhead ratio for short VoIP packets and
      Inherent inefficiency in 802.11 MAC
A sophisticated system simulation with appropriate VoIP model is required to accurately evaluate 802.20 system capacity.

## Slide 5: VoIP Packet
A VoIP packet contains vocoder frame and
various protocol headers.

## Slide 6: Potential Models for VoIP
Source bit rates do not assume any Voice Activity Detection (VAD)
Voice source coders differ in terms of bit rate, number of bits per frame and the vocoder frame duration.
EVRC: Enhanced Variable Rate Codec (TIA/EIA/IS-127)

## Slide 7: Protocol Overhead
RTP/UDP/IP overhead
  12+8+20 = 40 bytes (320 bits)
MAC overhead example – 802.11
  MAC header size: 34 bytes (272 bits)
  PHY header size: 24 bytes (192 bits)
802.16 has a smaller MAC overhead
  A 16-bit connection identifier (CID) is used to identify a session in place of 48-bit MAC addresses in 802.11.
In the evaluation of 802.20, some of the MAC/PHY overhead would be proposal dependent
  optimize MAC/PHY design

## Slide 8: Effect of protocol overhead
Vocoders with larger frame duration suffer less from
per packet protocol overhead.

## Slide 9: RTP/UDP/IP Hdr. compression
Assuming 40-bytes RTP/UDP/IP header compressed
down to only 2-bytes (16-bits)

## Slide 10: VoIP Frame Aggregation
Multiple vocoder frames can be aggregated to form a bigger VoIP packet
Pros: Higher payload to overhead ratio because a single set of protocol overhead applies to an aggregated packet
Con: Packet delay increases

## Slide 11: VoIP Frame Aggregation (2)
Assuming packet aggregation (bundling) over 60ms

## Slide 12: Frame Aggr.+Hdr. compression
Packet aggregation (bundling) over 60ms
Compressed RTP/UDP/IP header: 2 bytes (16-bits)

## Slide 13: Voice Activity Detection (VAD)
Typical voice conversations contain approximately 50 percent silence.
Voice Activity Detection (VAD) sends RTP packets only when voice is detected.
In TIA/EIA/IS-871, the voice activity factor is 0.4 with 29% full rate (8.6Kb/s), 4% half rate, 7% quarter rate and 60% eighth rate voice frames.
The G.729 Annex-B and G.723.1 Annex-A codecs include an integrated VAD function

## Slide 14: VoIP Performance Metrics
One way packet delay
  Packet delay includes the vocoder lookahead delay (e.g. 7.5ms for G.723.1), total air-interface delay, IP network delay and the receiver processing delay etc.
  Low one-way delay required to maintain good interaction between the two ends.
  Good (<150ms), Acceptable (150-300ms), Unacceptable (>300msITU G.114 requirement).
Delay jitter (standard deviation of delay)
  Excessive jitter may lead to loss of packets in the receiver jitter buffers.

## Slide 15: VoIP Performance Metrics (2)
Packet loss rate
  Transmission errors
  Dropped packets due to delay threshold
Packet loss rate of 1% acceptable?
Loss rate on aggregated VoIP packets?
  Multiple consecutive vocoder frames are lost due to a missing aggregated VoIP frame.
Impact of loss rate on RT/UDP/IP header compression?

## Slide 16: Summary
A VoIP Traffic model required for 802.20 system capacity analysis
The model should capture:
  RTP/UDP/IP overhead
  MAC/PHY overhead
Techniques that potentially enhance capacity can be considered in the VoIP model:
  RTP/UDP/IP header compression
  Voice activity detection (VAD)
  Vocoder frame aggregation (bundling)
Appropriate VoIP performance metrics (one-way delay, jitter and packet loss rate etc.) and corresponding target values also need to be defined.