## Slide 2: 802.20 Evaluation Criteria Update
Farooq Khan
IEEE 802.20 Interim Meeting
Vancouver, BC, Canada
January 12-16, 2004

## Slide 3: Evaluation Criteria Status
Two conference calls (12/16 and 1/6) since the November Plenary
The discussion focused on the following items:
  Interface between link and system simulations
  System simulation calibration
  Simulation of various channel bandwidths
  Fairness criteria
  Phased approach for technology evaluation

## Slide 4: Link-system Interface (LSI)
The evaluation criteria would specify an acceptable interface between link and system simulations.
  This is needed because the link and system simulations are performed separately (the simulation complexity would be very high if joint link and system simulations are required).
The group discussed 2 potential solutions to the link-system interface:
  Use actual link curves
  Specify an LSI methodology
It was also pointed out that the group may not need to specify any link-system interface at all. It can be left to individual proposals to justify and validate the link-system interface used in the simulations.

## Slide 5: Use actual link curves
In this option, link curves are produced for each of the coding, modulation and channel model combinations.
The channel models currently being specified in the channel modeling correspondence group are based on a stochastic approach and therefore results in infinite combinations making this approach impractical.
Therefore, if the link curve approach is to be used, we need to have a small set (4-5) of discrete channel models.

## Slide 6: Specify an LSI methodology
Using this option, a single AWGN curve (or a small set of curves) is used as reference.
The deviations ("fudge factors") from this reference curve for different coding, modulations and channel model realizations are determined based on some analytical formula.

## Slide 7: System simulation calibration
The evaluation criteria would specify a system simulation calibration process.
However, it is not clear, at this stage, to what level of detail different simulations need to be calibrated.
The group is open to proposals to nail down the calibration specifications.

## Slide 8: Simulation of various channel bandwidths
The objective of the evaluation criteria group is to have a small number of preferred channel bandwidths for simulation purpose.
  However, people will be free to simulate the full set of channel bandwidths.
  At this point, it seems too early to specify this small set of channel bandwidths for simulations.
It was also discussed that a small number of spectrum allocation (over which the results are quoted) can be specified.
The individual technology proposals may then split the total spectrum into a given number of carriers w/ reuse of 1 or greater than 1 (if needed by the technology).

## Slide 9: Fairness criteria
Fairness criteria based on the normalized throughput currently specified in the document may apply to only a subset of applications such as full buffers case.
The values used in the fairness criteria CDF curve may need to be revisited.
The individual fairness criteria (or outage criteria) would be needed on a application by application basis in the absence of the fairness criteria based on normalized throughput.
The group also discussed the possibility of using fairness as the performance metric rather than as a constraint.
  Fairness metric would be provided as output of the simulations.

## Slide 10: Phased Approach for Technology Evaluation
The group agreed in principle to adopt a phased approach for technology evaluation.
  Start with lowest complexity simulations and incrementally add more details
  3-4 phases may be specified
The details of the various phases are TBD.