## Slide 2: 802.20 Traffic Models Update
Farooq Khan
IEEE 802.20 Interim Meeting
Vancouver, BC, Canada
January 12-16, 2004

## Slide 3: Traffic Models Status
Once conference call (12/2) since the November Plenary
The discussion focused on the following items:
  Specification of traffic mix
  Higher layer protocol models
  FTP traffic model
  Full buffers (Infinite backlog) model
  Mobile station buffer size considerations
  VoIP Traffic model
  Wireless multi-party Gaming traffic model
  User scenarios

## Slide 4: Specification of traffic mix
Traffic modeling group foresees scenarios where various traffic types are simulated simultaneously.
Currently only a list of traffic types is provided
  Issue of percentage of various traffic types in a mixed scenario is still open.
Contributions invited on possible traffic mix scenarios (percentage of different traffic types) and potential phases of simulations etc.

## Slide 5: Higher layer protocol models
Input on higher layer protocols for applications other than web browsing.
For web browsing application, the consensus is to use HTTP/1.1 protocol.

## Slide 6: FTP traffic model
The group discussed if the current model is a realistic representation of an FTP user behavior in practice.
In particular, it was questioned if "think time" applies to the FTP model the same way as the web browsing model.
  For FTP, another request can be generated while the previous file is downloading in the background.
Contributions on whether we need to modify the existing FTP traffic model.

## Slide 7: Full buffers model
Full buffers is currently not considered as a traffic type
Input on whether we need to include a simulation case with Full buffers traffic only.
  For example, a first stage simulation for “calibration” purposes.

## Slide 8: Mobile station buffer size
The group discussed if the mobile station buffer size limitations need to be considered in the evaluation phase.
Two options were pointed out:
  Adding a maximum buffer size constraint or
  Allowing infinite buffer size with average and distribution of buffer occupancy collected as output metrics.
It was also mentioned that requirements on delay and jitter may already capture the buffer limitation aspect and it is not necessary to include any buffer size constraint separately.

## Slide 9: VoIP Traffic model
VoIP is one of the traffic types to be simulated in the 802.20 evaluation.
Currently, there is no model specified for the VoIP traffic.
Contributions are invited on potential VoIP models suitable for 802.20 air-interface evaluation.

## Slide 10: Wireless Gaming traffic model
Wireless multi-party wireless gaming is an important application that needs to be considered in 802.20 system evaluation.
Input required on mobile wireless gaming models.

## Slide 11: User scenarios
The group discussed if:
  all the user scenarios (Laptop, PDA, Smart phone, machine-to-machine) need to be considered or
  only a subset of the user scenarios can be simulated.
In order to capture different user scenarios, parameters values of some traffic models (e.g. web browsing) would be adapted to the user scenario
  For example, heavy, medium or light web browsing application.