## Slide 2: Some retrospect
Link budget template
  shall be completed for both the forward and reverse links for each deployment environment and each test case service.
  Link level simulations are used to determine the required Eb/(N0 + I0) and the required C/I of their RTT to meet the performance criteria.
  Path loss formulas are used to determine the maximum range and the coverage area.

## Slide 3: Some retrospect
Note on Link budget template
  For Eb/(N0+I0), the significance and method of calculating this value will vary from RTT to RTT, so the proponent must give a detailed explanation of their method for calculating this value and its significance in determining capacity and coverage of the RTT.
  In particular, the proponent must state explicitly what frequency reuse ratio and traffic loading per sector are assumed in determining this quantity

## Slide 4: Some retrospect
Deployment model
  used to extract critical parameters, such as coverage efficiency and spectrum efficiency.
  also give a general idea of the amount of infrastructure required to provide service to the specified model deployment area.
  The simulations used to complete the link budget template are required to complete the model deployment for each test environment.

## Slide 5: remarks
To use link budget template, should
  Define test case service for AI by traffic model, bit rates, BER, delay constraint, etc
  Define the evaluation criteria for cell search and synchronization, random access procedure, etc, as Eb/(N0+I0) for traffic channel
  Define the realistic noise interference models for performance evaluation especially for adjacent cell interference

## Slide 6: Realistic Noise Model
Long scramble code CDMA system
  For reuse factor one, all users take over all the time-frequency resource simultaneous.
  The interference from adjacent cells is power dependant.
OFDM system
  Different users may take over different time frequency resource, and the noise from adjacent cells may act like hits
  The noise interference is also dependant on time-frequency multiplexing method

## Slide 7: Performance criteria
Traffic channel
  Define test case service by bit rates, BER, delay constraint, traffic model
  Eb/(N0+I0) versus service requirement
Cell search and synchronization
  Time, frequency, power resource constraints
  Eb/(N0+I0) versus probability and time duration
Random access
  Time frequency resource constraints
  Eb/(N0+I0) versus probability and time duration