## Slide 1: Status of 802.20 Channel Models
IEEE 802.20 WG Session #7
March 15-19, 2004
Qiang Guo
Editor, Channel Modeling Correspondence Group
C802.20-04/30

## Slide 2: Current Status of 802.20 Channel Models
One conference call (3/3/04) since Session#6
A list of key working items have been identified
    Add Indoor Pico-cell to the MBWA channel environments;
    Investigate the MIMO nature of Outdoor-to-Indoor model;
    Determine the reference values of spatial channel model parameters;
    Determine and validate the statistical distributions of PAS and angular parameters in both CASE-IV & CASE-V;
    Provide the detailed algorithm for generating channel model parameters in various MBWA channel environments;
    Investigate and determine the correlation values between channel model parameters;
    Model inter-cell/inter-sector interference;
    System level calibration and implementation;
    Provide the algorithm for generating channel model parameters in the case of antenna polarization (optional);

## Slide 3: MIMO Channel Model for Simulations
The description is in the context of a downlink system, i.e., the BS transmits to MS
The following figure shows a MIMO channel model with S transmit antennas and U receive antennas

## Slide 5: MIMO Channel Model (continue)
For an S element BS array and a U element MS array, the channel coefficients for one of N multi-path components are given by an complex matrix,
The broadband MIMO radio channel transfer matrix can be modeled as
where
and

## Slide 6: MIMO Channel Model (continue)
Notice that the above equation is a simple tapped delay line model in a matrix format
The signals at the MS antenna array are denoted,
Similarly, the signals at the BS antenna array are
The relation between the input and output vectors is
where it is assumed that zero-mean complex Gaussian distributed, i.e., is Raileigh distributed.

## Slide 7: Procedure for Generating Ch. Matrices
Specify an environment, i.e., suburban macro, urban macro, urban micro, or indoor pico.
Obtain the parameters to be used in simulations, associated with that environment.
Generate the channel coefficients based on the parameters.
Note:
  The received signal at MS consists of N time-delayed multi-path replicas of the transmitted signal.
  These N paths are defined by the channel PDP, and are chosen randomly according to the channel generation procedure.
  Each path consists of M sub-paths.

## Slide 8: Flowchart for Generating Ch. Matrices

## Slide 9: Definitions of Angular Parameters

## Slide 10: Environment Parameters
Channel Scenario | Urban Micro
Number of paths (N) | 6
Number of sub-paths (M) per-path | 20
Mean AoD at BS | 200
Per-path rms AS at BS | 5o (LOS and NLOS)
BS per-path PAS Distribution | Laplacian
Mean AoA at MS | 680
Per-path rms AS at MS | 350
MS Per-path PAS Distribution | Laplacian
Mean total RMS Delay Spread | 0.251s
Distribution for path delays | U(0, 1.2s)
Lognormal shadowing standard deviation | NLOS: 10dB LOS: 4dB
Pathloss model (dB), d is in meters | NLOS: 34.53 +38 log10(d) LOS: 30.18 + 26log10(d)

## Slide 11: Generating User Parameters for Urban Microcell Environments
Step 1: Choose the urban microcell environment.
Step 2: Determine various distance and orientation parameters.
Step 3: Determine the bulk path loss and log normal shadow fading parameters.
Step 4: Determine the random delays for each of the N multipath components.
Step 5: Determine random average powers for each of the N multipath components.
Step 6: Determine AoDs for each of the N multipath components.
Step 7: Randomly associate the multipath delays with AoDs.
Step 8: Determine the powers, phases, and offset AoDs of the M = 20 sub-paths for each of the N paths at the BS.
Step 9: Determine the AoAs for each of the multipath components.
Step 10: Determine the offset AoAs of the M = 20 sub-paths for each of the N paths at the MS.
Step 11: Associate the BS and MS paths and sub-paths. Sub-paths are randomly paired for each path, and the sub-path phases defined at the BS and MS are maintained.
Step 12: Determine the antenna gains of the BS and MS sub-paths as a function of their respective sub-path AoDs and AoAs.
Step 13: Apply the path loss based on the BS to MS distance and the log normal shadow fading determined in Step 3 as bulk parameters to each of the sub-path powers of the channel model.

## Slide 12: Generating Channel Coefficients
We denote the channel matrix for the nth multipath component (n = 1,…,N) as . The (u,s)th component (s = 1,…,S; u = 1,…,U) of is given by

## Slide 13: Future Works
Work with Evaluation Group to specify system level implementation and calibration methods
Fine-tune the channel model parameters

## Slide 14: References
Recommendation ITU-R M.1225, “Guideline for Evaluation of Radio Transmission Technologies for IMT-2000,” 1997.
3GPP & 3GPP2 SCM AHG, “Spatial Channel Model Text Description”, SCM Text V6.0.