## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | IEEE 802.20 MBWA Security Architecture | 
Date Submitted | 2004-3-11 | 
Source(s) | T.Charles Clancy clancy@waa-assoc.com William A. Arbaugh waa@waa-assoc.com WAA Associates, LLC. (443)-283-7641 | Paul Nguyen Paul.nguyen@ncr.disa.mil Defense Information Systems Agency Center for Standards Management - Networks Division (703)-681-2553 (703)-681-2794 (Fax)
Re: | Straw man Security Architecture | 
Abstract | This presentation presents a straw man security architecture for 802.20. The design goals of this architecture are to meet the 802.20 security and mobility requirements, meet U.S. DOD requirements for the protection of sensitive but UNCLASSIFED information, and be free of intellectual property claims. | 
Purpose | Informational | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 
IEEE C802.20-04/XXXX

## Slide 2: IEEE 802.20 MBWA Mobile Broadband Wireless Access Security Architecture
T. Charles Clancy
William A. Arbaugh
Paul Nguyen

## Slide 3: Overview
Design Requirements and Challenges
Potential Solution Set
Proposed Solution and Motivation
Next Steps and Timeline

## Slide 4: Design Requirements and Goals
Meet 802.20 Security and Mobility requirements.
  Support fast hand-offs
  Use current upper layer standards when appropriate
Meet minimum US DOD requirements for protection of sensitive but UNCLASSIFIED information (SBU).
  FIPS 140-2 compliant
  Support public key based mutual authentication
Free of intellectual property claims

## Slide 5: Solution Space
Confidentiality
  Control Messages: None
    Needed for trouble shooting
  Data: AES-CCM based solution is only algorithm/mode pair meeting all requirements.
Integrity
  Control Messages: HMAC-SHA1
    Prevents denial of service and session hijacking at the protocol level
  Data: AES-CCM

## Slide 6: Solution Space cont.
Authentication and Access Control
  IEEE 802.1X / EAP
    Some issues such as state machine synchronization and transitivity of trust, but adopted by 802.11 and most actively worked solution at the moment.
    Cross domain roaming issues currently unresolved.
  Kerberos
    Not as many issues as 1x/EAP but more complex.
    Supports cross domain roaming.
    Dictionary attack against default authentication method.
    Seems to be losing favor.

## Slide 7: Solution Space cont.
Default Authentication Method
  Public key systems have suffered deployment and management problems and are costly in terms of computation for clients.
  Password based systems suffer from dictionary attacks and the lack of key management.

## Slide 8: Proposed Solution
Confidentiality (Layer 2)
  Control Messages: None
  Data Messages: AES-CCM
Integrity (Layer 2)
  Control Messages: HMAC-SHA1
  Data Messages: AES-CCM

## Slide 9: Proposed Solution, cont.
Authentication and Access Control
  IEEE 802.1x / EAP
    Current approach embraced by 802.11 and actively being worked in IETF and IEEE.
    Should allow Interworking once cross domain roaming issues resolved.
    Supports multiple, standardized, authentication methods.
    Trust transitivity can be mitigated by ensuring that ALL base stations mutually authenticates with the AAA server and communicate via a secure channel.

## Slide 10: Default EAP Method
IEEE 802.11 defines EAP/TLS as the default method.
  Too slow (~800ms best case and ~3sec worst case) for fast roaming unless combined with back-end methods.
  Traditional password systems suffer from passive and active dictionary attacks (those that don’t, e.g. EKE, SPEKE, et. al. are patented).

## Slide 11: Default EAP Method, cont.
We’ve developed a method to “boot strap” a plain text password/PIN into a cryptographically strong password.
  Suffers from a very small window where a dictionary is attack can theoretically succeed, e.g. during initial registration only. We can prevent this attack with additional computation, but we’re not sure it is worth the cost.
  Supports strong key management, i.e. agreement on current session key and updating of authentication key.
  Will be submitted to the IETF for standardization and is IP free (we believe).

## Slide 12: Next Steps
Feedback from group (March)
Finalize design and authentication method (Early April)
Publish design and authentication method for review (Mid April)
Develop a C based reference implementation for the authentication method (End of April)
Update design and authentication as needed based on review (End of April / early May)
Presentation of final design document (May meeting)

## Slide 13: Questions?