## Slide 1: Spectral Efficiency Ad-hoc Closing Report
March 18, 2004

## Slide 2: Closing Report of SE Ad-hoc
The ad-hoc group did not reach consensus on a single option but is recommending two options for further consideration by the Working Group.
  A modification of Option 1 (referred to as Option 1b) which more explicit explanation of how the values in the table are to be interpreted.
  Option 3 with a proposed correction to one of the values
There was also discussion on the ramifications of mandatory requirements.
  One interpretation is that all mandatory requirements must be met be the final standard and if this is not feasible the requirements document will have to be revised.
  An alternate interpretation was that as long as the final standard did not violate the effective PAR, the requirements document would not require revision.

## Slide 3: Option 1b
The system spectral efficiency of the 802.20 air interface shall be quoted for the case of a three sector baseline configuration[1]. It shall be computed in a loaded multi-cellular network setting, which shall be simulated based on the methodology established by the 802.20 evaluation criteria group. It shall consider among other factors a minimum expected data rate/user and/or other fairness criteria, and percentage of throughput due to duplicated information flow. The simulations shall be run with the following three mobility classes, 3 km/h, 120 km/hand 250 km/h.
The values shall be quoted on a b/s/Hz/sector basis. The weighted average of the spectral efficiency shall be computed by multiplying the spectral efficiency at 3 km/h by x, the spectral efficiency at 120 km/h by y, and spectral efficiency at 250 km/h by z. (Where x,y,z > 0 and x+y+z=1).
[values TBD e.g. x=.4, y=.5, z=.1]
The weighted average system spectral efficiency of the 802.20 air interface shall be greater than:

## Slide 4: Option 1b
The spectral efficiency at different mobility speeds should degrade gracefully.
[1]Since the base configuration is only required for the purpose of comparing system spectral efficiency, proposals may submit deployment models over and beyond the base configuration.
Parameter | Spectral Efficiency Requirements and Targets |  |  | 
 | Downlink |  | Uplink | 
 | Required Minimum | Desirable Target | Required Minimum | Desirable Target
Spectral Efficiency (b/s/Hz/sector) | 1.2 | 2.4 | 0.6 | 1.2

## Slide 5: Option 3
In this document, the term “System Spectral Efficiency” is defined in the context of a full block assignment deployment and is, thus, calculated as the average aggregate throughput per sector (bps/sector), divided by the spectrum block assignment size (Hz)( taking out all PHY/MAC overhead).
For proposal evaluation purposes, the System Spectral Efficiency of the 802.20 air interface shall be quoted for the case of a three sector baseline configuration[1] and an agreed-upon block assignment size. It shall be computed in a loaded multi-cellular network setting, which shall be simulated based on the methodology established by the 802.20 evaluation criteria group. It shall consider, among other factors, a minimum expected data rate/user and/or other fairness criteria, QoS and percentage of throughput due to duplicated information flow.
[1]Since the base configuration is only required for the purpose of comparing system spectral efficiency, proposals may submit deployment models over and beyond the base configuration.

## Slide 6: Option 3
The system spectral efficiency of the 802.20 air interface shall be greater than the values indicated in table 4-1. The spectral efficiency at higher speeds than those shown should degrade gracefully.
Parameter | Channel Bandwidth |  |  |  |  |  |  | 
 | 1.25 MHz. @ 3km/hr |  | 1.25 MHz . @ 120km/hr |  | 5 MHz.@ 3km/hr |  | 5 MHz. @ 120 km/hr | 
 | DL | UL | DL | UL | DL | UL | DL | UL
Spectral Efficiency (b/s/Hz/sector) | 2.0 | 1.0 | 1.0 | 0.75 | 2.0 | 1.0 | 1.0 | 0.75

## Slide 7: Option 3m (Proposed simplification of table and correction)
The system spectral efficiency of the 802.20 air interface shall be greater than the values indicated in table 4-1. The spectral efficiency at higher speeds than those shown should degrade gracefully.
Parameter | Spectral Efficiency Requirements and Targets |  |  | 
 | Downlink |  | Uplink | 
 | 3 km/hr | 120 km/hr | 3 km/hr | 120 km/hr
Spectral Efficiency (b/s/Hz/sector) | 2.0 | 1.0 (1.5) (correction proposed) | 1.0 | 0.75