## Slide 1: IEEE 802.20 MBWA Standard Project
Contribution: C802.20-04-51r2 Date: May-12-2004
RF Performance Evaluation Criteria
Dan Gal dgal@lucent.com

## Slide 2: Abstract
Discussion of and proposed values for key RF performance characteristics, recommended for adoption by the IEEE 802.20 Evaluation Criteria document.

## Slide 3: RF Performance Evaluation Characteristics 1/2
Transmitter:
  Transmit power
  Emission mask
  ACLR*
------
* ACLR = Adjacent Channel (power) Leakage Ratio

## Slide 4
Receiver:
  Sensitivity
  Selectivity
  Blocking
RF Performance Evaluation Characteristics 2/2

## Slide 5: Transmitter Power
Define maximum peak transmit power per 1-MHz of channel bandwidth -
Proposal: - BS: +43 dBm/MHz
- MS: +27 dBm
Define limits for out-of-channel and out-of-band emission.
Proposal: adopt the FCC out of band limits
defined for the PCS band.

## Slide 6: Transmitter Emission Limits
Out-of-Channel channel emission limits:
  Channel Emission Mask approach, or
  ACLR approach (or both)
Proposal:
  define channel BW as containing 99% of the emission power, and, require ACLR minimum value:

## Slide 7: Transmitter ACLR
ACLR
ACLR is defined as the attenuation (relative to the carrier) of the transmit power which is “spilled” into the adjacent channels. ACLR is expressed as dBc attenuation values.
ACLR is a function of the frequency offset from the assigned channel frequency.
Proposal:
MS: 33 dB
BS: 45 dB

## Slide 8: Receiver Sensitivity
Receiver Sensitivity is defined as the minimum power, measured at the antenna port, at which the frame error rate (FER) or bit error rate (BER) are better (lower) than a required limit.
Sensitivity is a function of the information bit rate, Eb/No, operating temperature and the receiver noise-figure (NF). Sensitivity = S/No + KTB + NF.
Proposal: define required NF values (10 dB for MS and 5 dB for BS) and require minimum FER/BER values in conjunction with the evaluated traffic models.

## Slide 9: Receiver Selectivity
Receiver selectivity is a measure of the receiver’s ability to reject signals from adjacent channels while receiving a wanted signal on its tuned frequency.
Selectivity is specified as the ratio (in dB) of the adjacent channel signal level to the assigned channel’s signal level in which a reference BER/FER is maintained.

## Slide 10: Receiver Selectivity
Proposal for selectivity values:
MS: 33 dB
BS: 63 dB

## Slide 11: Receiver Blocking
Receiver blocking is the effect of a strong out-of-band signal (at channels other than the adjacent and spurious) on the receiver’s ability to detect a wanted signal in the tuned channel.
The blocking signal reduces the specified receiver sensitivity by a certain number of dB's.
Proposal: at 3 dB above sensitivity and BER 0.001, the blocking signal level and type: MS: -56 dBm (same technology) BS: -40 dBm (same technology); -15 dBm (CW)

## Slide 12: Recommendation
Agree upon or modify the proposed RF
performance values and adopt into the 802.20
Evaluation Criteria Document.

## Slide 13: FCC Emission Limits for the PCS Band
CFR 47, §24.238 Emission limitations for Broadband PCS equipment.
The rules in this section govern the spectral characteristics of emissions in the Broadband Personal Communications Service.
(a) Out of band emissions. The power of any emission outside of the
authorized operating frequency ranges must be attenuated below the
transmitting power (P) by a factor of at least 43 + 10 log(P) dB.”