## Slide 1: Status of 802.20 Channel Models
IEEE 802.20 WG Session #8
May 10-13, 2004
Qiang Guo
Editor, Channel Modeling Correspondence Group
C802.20-04/52

## Slide 2: Current Status of 802.20 Channel Models
A list of key working items have been identified
    Add Indoor Pico-cell to the MBWA channel environments;
    Investigate the MIMO nature of Outdoor-to-Indoor model;
    Determine the reference values of spatial channel model parameters;
    Determine and validate the statistical distributions of PAS and angular parameters in both CASE-IV & CASE-V;
    Review the detailed algorithm for generating channel model parameters in suburban macro channel environment;
    Investigate and determine the correlation values between channel model parameters;
    Model inter-cell/inter-sector interference;
    System level calibration and implementation;
    Provide the algorithm for generating channel model parameters in the case of antenna polarization (optional);

## Slide 3: MIMO Channel Model for Simulations
The description is in the context of a downlink system, i.e., the BS transmits to MS
The following figure shows a MIMO channel model with S transmit antennas and U receive antennas

## Slide 5: MIMO Channel Model (continue)
For an S element BS array and a U element MS array, the channel coefficients for one of N multi-path components are given by an complex matrix,
The broadband MIMO radio channel transfer matrix can be modeled as
where
and

## Slide 6: MIMO Channel Model (continue)
The (u,s) th element of the nth multi-path component channel matrix is given by
where

## Slide 7: MIMO Signal Model
Notice that the above equation is a simple tapped delay line model in a matrix format
The signals at the MS Rx antenna array are denoted,
Similarly, the signals at the BS Tx antenna array are
The relation between the input and output vectors is
where is AWGN, and

## Slide 8: MIMO Signal Model (Cont’)
The relation between the input and output vectors can be simplified

## Slide 9: Procedure for Generating Ch. Matrix
Specify an environment, i.e., suburban macro.
Obtain the parameters to be used in simulations, associated with that environment.
Generate the channel coefficients based on the parameters.
Note:
  The received signal at MS consists of N time-delayed multi-path replicas of the transmitted signal.
  These N paths are defined by the channel PDP, and are chosen randomly according to the channel generation procedure.
  Each path consists of M sub-paths.

## Slide 10: Environment Parameters
Channel Scenario | Suburban Macro
Number of paths (N) | 6
Number of sub-paths (M) per-path | 20
Mean AoD at BS | 50
Per-path rms AS at BS | 2o
BS per-path PAS Distribution | 
Mean AoA at MS | 680
Per-path rms AS at MS | 350
MS Per-path PAS Distribution | 
Mean total RMS Delay Spread | 0.17s
Distribution for path delays | 
Lognormal shadowing standard deviation | 8dB
Pathloss model (dB), d is in meters | 31.5 +35 log10(d)

## Slide 11: Generating User Parameters for Suburban Macrocell Environment
Step 1: Choose suburban macrocell environment.
Step 2: Determine various distance and orientation parameters.
Step 3: Determine the path loss and log normal shadow fading parameters.
Step 4: Determine the random delays for each of the N multipath components.
Step 5: Determine random average powers for each of the N multipath components.
Step 6: Determine AoDs for each of the N multipath components.
Step 7: Randomly associate the multipath delays with AoDs.
Step 8: Determine the powers, phases, and offset AoDs of the M = 20 sub-paths for each of the N paths at the BS.
Step 9: Determine the AoAs for each of the multipath components.
Step 10: Determine the offset AoAs of the M = 20 sub-paths for each of the N paths at the MS.
Step 11: Associate the BS and MS paths and sub-paths. Sub-paths are randomly paired for each path, and the sub-path phases defined at the BS and MS are maintained.
Step 12: Determine the antenna gains of the BS and MS sub-paths as a function of their respective sub-path AoDs and AoAs.
Step 13: Apply the path loss based on the BS to MS distance and the log normal shadow fading determined in Step 3 as bulk parameters to each of the sub-path powers of the channel model.

## Slide 12: Cross-Polarized Antennas
The channel models discussed so far assume that the antennas at BS and MS with identical polarization;
The use of antennas with different polarizations at the transmitter and receiver leads to polarization diversity gain;
Duo to the physical limit on handheld devices, cross- polarized antennas becomes the primary way to implement MIMO technique on small handheld devices;
Thus a MIMO polarization channel model is needed for 802.20 WG.

## Slide 13: Generating User Parameters for Suburban Macrocell Environment and Polarized Arrays
Step 1-12: the same as previous case
Step 13: Generate additional cross-polarized subpaths.
Step 14: Set the AoD and AoA of each subpath in Step 13 equal to that of the corresponding subpath of the co-polarized antenna orientation.
Step 15: Generate phase offsets for the cross-polarized elements.
Step 16: Decompose each of the co-polarized and cross-polarized sub-rays into vertical and horizontal components based on the co-polarized and cross-polarized orientation
Step 17: The power of each sub-path in the horizontal orientation is set relative to the power of each sub-path in the vertical orientation according to the polarization coupling ratio.
Step 18: At the receive antennas, decompose each of the vertical and horizontal components into components that are co-polarized with the receive antennas and sum the components.
Step 19: Apply the path loss based on the BS to MS distance from Step 2, and the log normal shadow fading determined in step 3 as bulk parameters to each of the sub-path powers of the channel model.

## Slide 14: Considerations for Evaluating MIMO Proposals
The operation of a MIMO technique should be described in sufficient details, including Tx and Rx algorithms, higher layer signaling to support MIMO, etc..
An example of the channel quality metric used for rate or link adaptation should be described.
Full mobility should be supported, including high-speed cases.
Realistic simulations should include effects such as delay, channel estimation error, signaling errors.

## Slide 15: References
Recommendation ITU-R M.1225, “Guideline for Evaluation of Radio Transmission Technologies for IMT-2000,” 1997.
3GPP & 3GPP2 SCM AHG, “Spatial Channel Model Text Description”, SCM Text V6.0.