## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | A new option proposed for 802.20 requirements on latency and packet error rates | 
Date Submitted | 2004-05-10 | 
Source(s) | Anna Tee 1301 E Lookout Dr., Richardson, TX 75082 | Voice: (972) 761-7437 Fax: (972) 761-7909 Email: atee@sta.samsung.com
 | Joseph Cleveland 1301 E Lookout Dr., Richardson, TX 75082 | Voice: (972) 761-7981 Fax: (972) 761-7909 Email: jclevela@sta.samsung.com
Re: | MBWA Call for Contributions, Session #8, May 2004 | 
Abstract | This is a contribution to the requirements on latency and packet error rate for the IEEE 802.20 system requirements document. A new, revised option is proposed with reference to similar requirements used in other wireless communication standards. | 
Purpose | For discussion and adoption into IEEE 802.20 System Requirements Document. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: A new option proposed for 802.20 requirements on latency and packet error rates
Anna Tee
Joseph Cleveland
May 10, 2004

## Slide 3: Topics
Effects of Wireless link on TCP performance
Error rate requirements in some current standards
Latency or Packet Transfer Delay
End user QoS categories recommended by ITU-T
Traffic classification by 3GPP
IETF QoS classification
Propose requirements for 802.20
References

## Slide 4: Effects of Wireless Link on TCP performance
Performance of TCP throughput over wireless links deteriorates significantly because of errors caused by the wireless link [1]
For example, IEEE 802.11b TCP throughput is only 4.3 Mbps, even the physical bit rate is 11 Mbps, i.e., only 39.1% of the maximum data rate is achieved
Packet losses in the link can trigger triple-duplicate acknowledgements and time-out mechanisms
TCP behavior such as congestion avoidance, slow-start affects TCP throughput
The PFTK model [3] is a model for the TCP Reno congestion avoidance mechanism for bulk transfer packet flows.

## Slide 5: TCP Throughput Variation with Packet Loss Rate & Round Trip Delay
TCP throughput based on PFTK model computed for ranges of packet loss rates and round trip delays
Maximum window size: 123 segments; maximum segment size (MSS): 536 bytes
TCP throughput decreases significantly as the packet loss rate increases beyond 10-4
At low packet loss rates, the TCP throughput decreases rapidly as the values of round-trip delay (RTD) increases. As the packet loss rate increases, it becomes the limiting factor for the TCP throughput, even when RTD is low.
Packet loss rate should be better than 10-4 while keeping the RTD as low as possible for the best performance in terms of TCP throughput.

## Slide 6: Effects of Packet Loss Rate with Round Trip Delay as a Parameter

## Slide 7: Effects of Round Trip Delay

## Slide 8: Error Rate Requirements in Current Standards
“Network performance objectives for IP-based services”: ITU-T Y.1541
  Parameters that are used in Y.1541 [4] are defined in ITU-T Y.1540 [5]
    IP packet transfer delay (IPTD)
    IP packet delay variation (IPDV)
    IP packet loss ratio (IPLR)
    IP packet error ratio (IPER)
  Six different classes of traffic based on IPTD and IPDV objectives
  All specified values are provisional, upper bounds
Network Performance Parameter | Class 0 | Class 1 | Class 2 | Class 3 | Class 4 | Class 5
IPTD | 100 ms | 400 ms | 100 ms | 400 ms | 1 s | U*
IPDV | 50 ms | 50 ms | U | U | U | U
IPLR | 1x10-3 |  |  |  |  | U
IPER | 1x10-4 |  |  |  |  | U
*U: Unspecified

## Slide 9: IEEE STD. 802-2001
“IEEE standard for local and metropolitan area networks: Overview and Architecture” [6]
  Defines the compliance with the family of IEEE 802 Standards
  Describes & explains relationship of the IEEE 802 standards to the OSI Basic Reference Model and Higher Layer protocols
Subsection 7.3 of IEEE Std. 802-2001 states that:
  Required error performance of IEEE 802 LANs and MANs shall be less than 8x10-8 per octet of MAC service Data unit (MSDU) length. While this error performance has to be accomplished at the physical layer for wired or optical fiber physical media, it is allowable for this error performance to be accomplished at the MAC service boundary in the case of wireless media.
For example: MSDU packet with 1500 octets,
  Required packet error rate => 1.2x10-4
  Value agrees closely with the IPER requirement specified in ITU-T Y.1541, in the case of ~1 MSDU / IP Packet

## Slide 10: Requirements on Error Rates in IEEE 802.16.3 [7]
Service | Maximum BER | Maximum Access Delay (One-Way)
Full Quality Telephony (Vocoder MOS >= 4.0) | 10-6 | 20 ms
Standard Quality Telephony (Vocoder MOS < 4.0) | 10-4 | 40 ms
Time Critical Packet Services | 10-6 | 20 ms
Non-Time Critical Services | 10-9 | Not applicable
Assuming bit errors are independent, for BER = 10-9,
=> Octet error rate ~ 8 x 10-9
10 times more stringent than Std. 802-2001 requirement
Thus, for a MSDU with 1500 octets, the packet error rate, assuming independent octet errors, is approximately:

## Slide 11: Error Rate Performance Supported by 3GPP
Ranges of BER that the network is required to support [8]:
  10-3 to 10-7 for real time applications
  10-5 to 10-8 for non-real time applications
Assuming bit errors are independent, for BER = 10-8,
=> Octet error rate ~ 8 x 10-8
Similar to Std. 802-2001 requirement
Thus, for a MSDU with 1500 octets, the packet error rate, assuming independent octet errors, is approximately

## Slide 12: Error Rate Performance in some Existing Cellular Communication Networks
Error rate performance of GSM as reported in [1] can support a bit error ratio of 10-3, which is then reduced to 10-8 in the nontransparent mode RLP, at the expense of variable, additional delay due to retransmissions, reducing the user throughput.
In IS-95 standard, frames are dropped after undergoing repeated retransmissions a number of times to limit the delay variation. The residual packet loss rate becomes 10-4.

## Slide 13: Video over IP Error Rate Requirements
For real-time video signal, ITU-T SG13 has recommended that IPLR must be at least 10-5 [10]
  Derived based on a BER of 10-9 for typical fiber optic network
  Worst-case assumptions:
    Packet size = 1500 bytes
    A bit error caused the whole packet to be lost
User Datagram Protocol (UDP): used for transport of most video streaming applications
UDP checksum is enabled
  => A packet may be discarded because of a single bit error
  UDP does not allow a re-transmission of the lost packet, the effects of losing a complete video packet could result in serious disruption to the video signal
UDP checksum is normally disabled in most applications
  Packets with bit errors will be received including the error bits
  Depending on the location of the error bits, the effects of the lost may be tolerable to the user at the receiving end

## Slide 14: Performance Requirements for Real-time Conversational Class - Voice
Conversational Voice
  Acceptable maximum FER = 3%
  General limits for one-way end-to-end delay as recommended by G.114:
    0 - 150 ms - preferred range
    150 - 400 ms - acceptable range with increasing degradation
  Requirement is also dependent on the error resilience of speech codec. For AMR speech codec: [9]
    Bit rate: 4.75 - 12.2 kbps
    Required BER:
      10-4 for Class 1 bits, 10-3 for Class 2 bits, a higher BER class at 10-2 might also be feasible.
      With codec frame length of 20 ms, the one-way end-to-end delay should be less than 100ms.

## Slide 15: Performance Requirements for Real-time Conversational Class - Others
Videophones
  Delay requirement: similar to conversational voice, with additional requirement on limits of lip-synch
  Maximum acceptable FER: 1%
Interactive games
  One-way delay value of 250 ms proposed in [8]
  Detail studies on multiplayer network gaming reported [11] the range of acceptable maximum round-trip time: 200 ms - 40 seconds, depending on the type of games, experience level of players
    Gaming can be : Conversational, Interactive or Interactive/Background
    Proposed residual BER requirement: 10-3, 10-5 / 6x10-8, or 10-5 / 6x10-8 respectively
    Proposed maximum one-way delay for the action game: 80ms.
Two-way control telemetry
  One-way delay limit: 250 ms proposed in [8]
  “0” information loss

## Slide 16: Performance Requirements for Interactive Class
Voice messaging:
  Similar error rate requirement as that of conversational class
  Delay: up to a few seconds
Web Browsing:
  Delay requirement: 2 - 4 seconds/page
  Recommended to improve to 0.5 second
High priority transaction services - E-commerce:
  Delay: 2 - 4 seconds
  Information loss: “0”
Email:
  Server to Server delay: several minutes or hours
  User to local server delay: 2-4 seconds

## Slide 17: Performance Requirements for Streaming Class – Audio/Video
Audio streaming:
  mainly an one-way application from server to user (s)
  Contents of the audio stream: high quality music or broadcasting
  Packet Loss rate requirement: 1% [13]
  Delay requirement: one-way delay = 10 seconds
Video streaming:
  Similar to audio streaming as described above
  MPEG-4 video: [9]
    Bit rate: 24 - 128 kbps or higher
    End-to-end delay: 150 - 400ms
    BER: 10-6 - 10-3 with significant degradation for the latter
Still image:
  Similar requirements to Video Streaming
  Error tolerance: dependent on the encoding and compression formats

## Slide 18: Performance Requirements for Streaming Class - Data
Bulk Data Transfer (File Transfers):
  May be classified as streaming service with relaxed delay tolerance
  “0” final information loss at the receiving end
Telemetry applications (Monitoring)
  Error rate and delay requirements: similar to that of the bulk data transfer

## Slide 19: Performance Requirements for Background Class
No stringent requirement on delay for the background class of services
Requirements for Fax:
  Delay: 30 seconds
  BER: less than 10-6 [13]
Low priority transaction services
  Short message services (SMS)
  Delivery delay: 30 seconds
  Email:
    Server to server delay: wide range with median of several hours

## Slide 20: Latency or Packet Transfer Delay
  ITU-T Y.1541 Model: Hypothetical Reference Path for Transfer Delay and Delay Variation Computation
  Path analysis for IPTD & IPDV in an IP network
  End-to-end One Way Transfer Delay = Path Delay + End-point Delay

## Slide 21: Path Delay & Variation Analysis Example
  ITU-T Y.1541 QoS Class 0
  US Diagonal path: Daytona Beach to Seattle
Element | Unit | IPTD/unit | Ave IPTD | IPDV/unit | Max IPDV
Distance | 4070 km |  |  |  | 
Route | 5087.5 km |  | 25 |  | 
Insertion Time | 200 bytes (VoIP) (1500 bytes) |  | 1 (8) |  | 
Non IP Net 1 |  |  | 15 |  | 0
IP Net 1 |  |  |  |  | 
Access, NA | 1 | 10 | 10 | 16 | 16
Distribution, ND | 1 | 3 | 3 | 3 | 3
Core, NC | 2 | 2 | 4 | 3 | 6
Internetwork GW, NI | 1 | 3 | 3 | 3 | 3
IP Net 2 |  |  |  |  | 
Access, NA | 1 | 10 | 10 | 16 | 16
Distribution, ND | 1 | 3 | 3 | 3 | 3
Core, NC | 4 | 2 | 8 | 3 | 12
Internetwork GW, NI | 1 | 3 | 3 | 3 | 3
Non IP Net 2 |  |  | 15 |  | 0
Total, ms |  |  | 100 |  | 62

## Slide 22: Statistics of Internet delay
Earlier studies presented in IETF [12] showed that the probability distribution function of one-way Internet delay is the shifted Gamma distribution
Mean delay values -
  Local routes: 10 ms
  International routes: 110 ms
Sprint’s Looking Glass tools
  Delay -
    Within the same state: ~ 20 ms
    Between East and West coasts: ~ 40 ms
    Between West coast and Asia: ~ 200ms

## Slide 23: One-way Delay & RTD
Overall one way delay in the mobile network from user equipment (UE) to the public land mobile network (PLMN) border: ~ 100 ms [8]
For a single user link, RTD of 10 ms is ideal in order to achieve TCP throughput of about 40 Mbps at IPLR of 10-4, based on results of PFTK model
RTD = 10 ms may not be realistic in practice due to constraints on the PHY and MAC layers, fairness considerations in the scheduling algorithm in a multiple access network etc.
Delay in IP network as discussed in the above section showed that it is almost impossible for RTD to be 10 ms or less

## Slide 24: End User QoS Categories as Recommended by ITU-T G.1010
Class | Interactive | Responsive | Timely | Non-critical
Delay | << 1 sec | ~ 2 sec | ~ 10 sec | >> 10 sec

## Slide 25: Applications & Services Classification by 3GPP
Class | Conversational | Streaming | Interactive | Background
Delay | <= 80 ms | <= 250 ms | unspecified | unspecified
Residual BER | 5x10-2, 10-2, 5x10-3, 10-3, 10-4, 10-5 ,10-6 |  | 4x10-3, 10-5 , 6x10-8 | 
SDU error ratio | 10-1, 10-2, 7x10-3, 10-3, 10-4, 10-5 |  | 10-3, 10-4 , 10-6 | 
Similar to ITU-T, services are classified into 4 classes based on the their one-way delay requirements
Within each service class, a range of residual BER and SDU error ratio are supported

## Slide 26: IETF QoS Classification
Service Class | DSCP name | Application Example
Administrative | CS7 | Heartbeats
Network Control | CS6 | Network Routing
Telephony | EF, CS5 | IP Telephony
Multimedia Conferencing | AF41-AF43 | Video Conferencing, Interactive Gaming
Multimedia Streaming | AF31-AF33, CS4 | Broadcast TV, Pay per View, Video Surveillance
Low Latency Data | AF21-AF23, CS3 | Client/Server transactions, peer-to-peer signaling
High Throughput Data | AF11-AF13, CS2 | Store & Forward applications, Non-critical OAM&P
Standard | DF (CS0) | Undifferentiated applications
Low Priority Data | CS1 | Any flow that has no BW assurance
“9” Service Classes are defined and mapped to DiffServ Code Points (DSCP) [14]
ITU-T Y.1541, ITU-T Y.1540 and G.1010 considered

## Slide 27: Propose Requirements for 802.20
4.1.7 Latency and Packet Error Rate
The system shall support a variety of traffic classes with different latency and packet error rates performance, in order to meet the end-user QoS requirements for the various applications, as recommended by ITU G.1010, Y.1541. These traffic classes should be mapped to the appropriate QoS classes as defined for the QoS architecture described in Section 4.4.1. Depending on the network configuration, the AI should support appropriate latency and packet error rate performance targets associated with each traffic class, such that the end-to-end QoS requirements for these applications can be achieved. In the case of IETF DiffServ, the requirements for the AI are shown in the following table.
The numbers quoted in the table use the following assumptions:
  MAC SDU size = 1500 bytes
  Network Delay = 20 ms, 100 ms
  Size of IP packet: 1 MAC SDU / IP packet
  For UDP and very low-latency TCP traffic:
    End-to-end One-way Delay ≈ 802.20 Latency + Network Delay

## Slide 28
IETF Service class | Transport Protocol | End-to-end One way Delay (s) | Network Delay (ms) | 802.20 Delay (ms) | MAC SDU Packet Error Rate | IP Packet Error Rate
Administrative | TCP | 0.10 | 20 | 20 | 10-6 | 10-6
Network Control [8,9,13] | TCP | 0.25 | 20 | 30 | 10-6 | 10-6
Telephony [8,13] (Voice over IP) | UDP/ RTP | 0.15 | 100 | 50 | 3 x 10-2 | 3 x 10-2
Multimedia Conferencing [8,13] | UDP/ RTP | 0.15 | 100 | 50 | 10-2 | 10-2
Multimedia Streaming [8,13] | UDP/ RTP | 5 | 100 | 200 | 10-2 | 10-2
Low Latency Data [8,13] (E-transactions) | TCP | 2 | 20 | 30 | 10-5 | 10-5
High Throughput Data (Email) [4,8,9,13] | TCP | 6* | 20 | 30 | 10-4 | 10-4
Standard (FTP) [4,8,9,13] | TCP | 10* | 20 | 50 | 10-4 | 10-4
Low Priority Data [4,8,9,13] | TCP | 100 | 100 | 100 | 10-3 | 10-3
*Time required to transfer all the packets for the email or file.

## Slide 29: References
G. Xylomenos, F. Polyzos, P. Mahonen, M. Saaranen, ‘TCP Performance Issues over Wireless Links’, IEEE communications Magazine, April 2001.'
C802.20-04-29, Contribution to 802.20 Plenary meeting, March 2004.
J. Padhye, V. Firoiu, D. Towsley, J. Kurose, “Modeling TCP Reno Performance: A Simple Model and Its Empirical Validation”, IEEE/ACM Trans. On Networking, Vol. 8, No.2, April 2000.
“Network performance objectives for IP-based services”, ITU-T Y.1541, May 2002.
“Internet Protocol Data Communication Service – IP packet transfer and availability performance parameters”, ITU-T Y.1540, Jan 2002.
“IEEE Standard for local and metropolitan area networks: Overview and Architecture”, IEEE Std. 802-2001, March 8, 2002.
“Functional Requirements for the 802.16.3 Interoperability Standard”, IEEE 802.16.3-00/02r4, September 22, 2000.
3GPP TS 22.105 V 6.2.0 (2003-06), Technical Specification Group Services and Systems Aspects, Service Aspects; Services and Services Capabilities.
3GPP TS 23.107 V 5.10.0 (2003-09), Technical Specification Group Services and Systems Aspects, Service Aspects; QoS concept and architecture (Release 5).
Video Performance requirements for IP performance recommendations, ITU-T SG13 D.228 (WP4/13), Jan 14, 2002.
Multiplayer Game Performance over Cellular Networks, V1.0, Forum Nokia, Jan 20, 2004
Statistics of One-Way Internet Packet Delays, A. Corlett, D. Pullin, S. Sargood, 53rd IETF, March 18, 2002.
ITU G.1010 [“Draft New Recommendation G.QoSRQT – End-user Multimedia QoS Categories”, ITU-T study group 12, contribution 37, August 2001]
F. Baker et. al., IETF Draft “Configuration Guidelines for DiffServ Service Classes draft-baker-diffserv-basic-classes-02”, Feb 13, 2004.
802.20 Evaluation Criteria, Draft ver. 0.9, May 5, 2004.