## Slide 1
IEEE C802.20-04/56r1
Project | IEEE 802 Executive Committee Study Group on Mobile Broadband Wireless Access <http://ieee802.org/20> | 
Title | On Security Issues In Wireless Communications Systems | 
Date Submitted | 2004-05-11 | 
Source(s) | Mithat C. Dogan ArrayComm, Inc. 2480 North First Street, Suite 200. San Jose, CA 95131-1014. | Voice: +1 408-952-1831 Fax: +1 408-428-9083 Email: mcd@arraycomm.com

## Slide 2
IEEE C802.20-04/33
Re: | 802.20 WG Call for Contributions
Abstract | This document discusses security issues in wireless communication systems and their relevance to the 802.20 Requirements Document.
Purpose | Contribute to the discussion and development of the 802.20 Requirements regarding security.
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802 MBWA ECSG.
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>.

## Slide 3: On Security Issues In Wireless Communications Systems
Mithat C. Dogan
ArrayComm, Inc. 2480 North First Street, Suite 200.
San Jose, CA 95131-1014.

## Slide 4: Agenda

## Slide 5: Agenda
Review symmetric key encryption algorithms:
  Applied to wireless links with variable length payloads.
  Stream ciphers.
  Block ciphers and modes of operation.
  Stream cipher issues (RC4 in particular).
  Block cipher issues (AES in particular).
  Which cipher in which mode is the best?
We will not cover:
  Public key encryption.
  Entity authentication.

## Slide 6: Agenda
Review message integrity/authentication issues:
  Are block ciphers better against bit flip attacks?
    No!
  Traditional message integrity method:
    Digital signatures.
  How to integrate encryption and message integrity?
    Authenticated Encryption (AE).
    Most efficient forms need to be licensed.
  Is IP-free AE efficient?
    NO! Tradeoff between implementation cost vs. licensing.
  Which one to choose?
    None?

## Slide 7: Agenda
  Is authenticated encryption (AE) secure?
    Claim: As secure as the block cipher used (AES):
      Small tag lengths make AE vulnerable to birthday attacks.
      For example, AES-CCM may be used to provide a 4 byte authentication tag which is insecure.
      Rijndael algorithm with block sizes 192 and 256 is recommended for message integrity purposes in the specification. AES uses 128 bit blocks.
  Is AES secure?
    Designed against linear/differential cryptanalysis.
    Algebraic structure led to new attacks with unknown hardness.

## Slide 8: Relevant Documents in 802.20 on Security

## Slide 9: 802.20 Req. Documents V12
Draft 802.20 Permanent Document, IEEE P 802.20 V12.
Date: March 27, 2004
  http://grouper.ieee.org/groups/802/20/DropBox/802.20%20requirements%20Document%20rev%2012.doc
Two references:
  Table 1‑1, PAR Values (quoted from page 6)
    Security Support: AES (Advanced Encryption Standard)
  Security Algorithm (quoted from page 18)
    The authentication and encryption algorithms shall be publicly available on a fair and non-discriminatory basis.
    National or international standards bodies shall have approved the algorithms.
    The algorithms shall have been extensively analysed by the cryptographic community to resist all currently known attacks.

## Slide 10: Previous Discussion
Recent presentation on security issues on this forum:
  Clancy, Arbaugh, Nguyen, “IEEE MBWA Mobile Broadband Wireless Access Security Architecture,” March 11, 2004.
  http://grouper.ieee.org/groups/802/20/Contribs/C802.20-04-41.ppt
Goals (quoted from above):
  Support fast handoffs.
  Use current upper layer standards when possible.
  Meet minimum DoD requirements to protect sensitive but unclassified information.
  Free of intellectual property claims.
Claim (quoted from above):
  Data confidentiality/integrity: AES-CCM is the only solution/mode pair meeting all the requirements.

## Slide 11: Initial Observations
A Google search on ‘AES CCM 802.20’ displays the targeted ad (quoted):
  Ultra-compact AES core implements Rijndael encoding in compliance with the NIST Advanced Encryption Standard (AES) with 128-bit key. Base AES1 core is very small (less than 3,000 gates).
  Full flow-through implementation of the CCM encryption and decryption according to the IEEE 802.11i standard. The core is less than 9000 gates.
How did AES core get three times bigger with CCM?
  Because CCM is inefficient compared to IP-free authenticated encryption schemes.
Do I need to implement AES and its modes in hardware?
  Depends on your platform.
  AES block decryption is 30 percent costlier than AES encryption.
  No ad for hardware implementation of the RC4 stream cipher.

## Slide 12: Definitions

## Slide 13: Definitions
Confidentiality:
  Encryption: The process of disguising a message to hide its content.
  An encrypted message is called ciphertext.
  Decryption: Converting ciphertext back to message (plaintext).
  Cipher: Mathematical function used for encryption and decryption.
Message Integrity:
  Verification that the message is not modified in transit.
  An intruder should not be able to substitute a false message for a legitimate one.
Authentication (not discussed in this document):
  Receiver should be able to ascertain the origin of the message.
Nonrepudiation (not discussed in this document):
  A sender should not be able to deny its message.

## Slide 14: The Ideal Cipher
Ideal cipher: Given ciphertext only:
  Plaintext and ciphertext are statistically independent.
One time pad is an ideal cipher:
Plaintext bits
XOR
Truly
Random
Bits
Ciphertext
XOR
Truly
Random
Bits
Plaintext bits
ENCRYPTION
DECRYPTION

## Slide 15: Stream Ciphers

## Slide 16: Stream Ciphers
Stream ciphers can be viewed as random bit sequence generators.
STATE TABLE
f ( )
secret key
next state
g ( )
keystream
h ( )
plaintext
ciphertext

## Slide 17: Stream Ciphers
Attempt to realize a one time pad.
Stream ciphers process plaintext in small blocks, as small as a bit.
Stream cipher operations:
  Update state:
    state(t+1) = f ( state(t) , secret_key );
  Produce Keystream:
    keystream(t) = g ( state(t) , secret_key );
  Produce Ciphertext:
    ciphertext(t) = h ( keystream(t) , plaintext(t) );
  Binary additive stream ciphers: Function h() is the XOR operation. Example: current use of RC4.

## Slide 18: Case Study: Bit Flip Attacks
Claim 1: Binary additive stream ciphers are vulnerable against bit flip attacks.
  Response : Encryption does not provide message integrity, it provides privacy.
Claim 2: Use block ciphers which mix plaintext better in a large block against such attacks.
  Response: Block ciphers suffer from the same problem.

## Slide 19: Case Study: Bit Flip Attacks
Assume the following 10 bit plaintext (message):
1 0 0 1 0 0 1 1 1 1
With the keystream (pseudo-random bits from stream cipher):
0 1 1 0 0 0 1 1 0 1
The ciphertext (keystream XOR-ed with plaintext):
1 1 1 1 0 0 0 0 1 0
Add 2 bit linear CRC (first bit = sum of odd bits, second bit = sum of evens):
1 1 1 1 0 0 0 0 1 0 1 0
Attacker flips the first bit and the first CRC bit:
0 1 1 1 0 0 0 0 1 0 0 0
CRC check passes at the intended receiver.
Plaintext is recovered as:
0 0 0 1 0 0 1 1 1 1
First bit is in error as intended by the attacker.

## Slide 20: Case Study: Bit Flip Attacks
Perhaps, if we encrypt the CRC, then the problem will go away?
  For example, WEP encrypts linear CRC.
  If the CRC is linear, then the attack remains unchallenged.
  Encrypted CRC: provides the redundancy to test the key hypothesis by the attacker.
What happens if the attacker:
  knows the location and content of the destination header in the stream (www.arraycomm.com) from my user terminal,
  And flips the corresponding bits to change it to a destination of its own user terminal?
  The base station may decrypt the message and forward it to the attacker’s user terminal depending on the protocol.
  Known as: Bit flip redirection attack. Requires extreme timing accuracy on attacker but feasible.

## Slide 21: Case Study: Bit Flip Attacks
Encryption functions provide confidentiality but not integrity.
Options:
  Encrypt a nonlinear CRC. Typical CRC lengths are 16 or 32 bits.
    On average, 28 or 216 bit flip attempts will be required to implement a birthday attack per burst.
    This approach may be good enough with multiple bursts.
    But: overloading CRC is inefficient for physical layer.
    But: encrypting CRC provides redundancy for an attack.
  Use a nonlinear function (with memory) instead of XOR.
    The stream cipher gets a little more complicated.
    Let us see whether block ciphers are immune to bit flips.

## Slide 22: Block Ciphers

## Slide 23: Block Ciphers
A symmetric key block cipher is a one to one function parametrized by a key K:
  Maps n-bit plaintext blocks.
  Into n-bit ciphertext blocks.
  n is called the blocklength.
x1
xn
BLOCK
CIPHER
plaintext
c1
cn
K
ciphertext
Attacks:
Ciphertext only
Known Plaintext
Chosen Plaintext
c = EK(x)

## Slide 24: Block Ciphers
Block ciphers process plaintext in large blocks compared to stream ciphers.
  n = 64 in DES.
  n = 128 in AES.
Wireless systems have variable length payloads:
  Burst payloads may not be a multiple of cipher block size.
  Do we need to pad bits to match the cipher block size and reduce information rate on the air interface? YES!
  Last encrypted word can not be decrypted until the next burst in case of payload and block size mismatch.
  What happens with repeat requests?
  With undetectable channel errors (failed CRC)?

## Slide 25: Block Ciphers
Selection Criteria:
  Estimated Security Level/History
    AES is a very recent algorithm.
    Despite minimal history, algebraic attacks appear promising.
  Key Size
    128, 192, 256 with AES.
  Throughput
    AES is faster than DES with 32 bit CPUs.
  Block Size
    Fixed at 128 bits.
  Complexity of Cryptographic Mapping
    AES is designed with efficient hardware implementation in mind.
  Data Expansion: unavoidable in certain modes.
  Error Propagation: unavoidable in certain modes.

## Slide 26: Block Cipher Modes
Electronic Code Book Mode (ECB):
Encrypt
K
n
cq
n
xq
With n-bit plaintext blocks:
  {x1,x2, …,xq}
Encrypting each plaintext
block independently yields:
  {c1,c2, …,cq}
cq = EK(xq)

## Slide 27: Block Cipher Modes
Electronic Code Book Mode (ECB):
cq = EK(xq), in which xq is the q-th n-bit plaintext block.
Identical plaintext blocks result in identical ciphertext with the same key.
Chaining dependencies: None.
  Reordering ciphertext blocks result in reordered plaintext blocks.
Error Propagation: None across blocks.
Not recommended for plaintext longer than a block.

## Slide 28: Block Cipher Modes
Cipher Block Chaining (CBC):
Encrypt
K
n
cq
cq-1
c0 = IV
n
n
xq
n

## Slide 29: Block Cipher Modes
Cipher Block Chaining (CBC) Mode:
  Requires an n-bit initialization vector IV.
  Encryption:
  c0 = EK(IV), c1 = EK(c0 + x1), …, cq = EK(cq-1 + xq),
  Identical plaintexts result in different ciphertexts.
  Chaining Dependencies: Proper decryption of a block requires proper decryption of the previous block.
  Error Propagation:
    A bit error in block p affects decryption of blocks q and (q+1).
    Predictable bit changes: Recovered plaintext for block (q+1) will have bit errors precisely where received ciphertext for block q did.
  Error Recovery: CBC recovers from an error in a ciphertext block if two successive ciphertext blocks are received correctly.

## Slide 30: Block Cipher Modes
Cipher Feedback Mode (CFB):
Encrypt
K
n
cq
I0 = IV
r
r
xq
r bits
n-r bits
k
Ij
r bit shift
n
Plaintext dependent
keystream generating
stream cipher.
What happens in a
known plaintext attack?

## Slide 31: Block Cipher Modes
Cipher Feedback Mode (CFB):
  An attempt to scale the block size from n to r.
  n-bit IV, and r-bit plaintext blocks,
  Uses only the encryption function of the block cipher for encryption and decryption.
  Similar properties to CBC in terms of chaining:
    Effect of a ciphertext error propagates to blocks.
  Can be viewed as a stream cipher with plaintext dependent keystream.

## Slide 32: Block Cipher Modes
Output Feedback Mode (OFB):
Encrypt
K
n
cq
I0 = IV
r
r
xq
r bits
n-r bits
k
Ij
n
n
Uses the block
cipher as a random
number generator.
Only encryption
operation is needed
for both encryption
and decryption.

## Slide 33: Block Cipher Modes
Output Feedback Mode (OFB):
  Stream cipher mode.
  Keystream is independent of plaintext.
  No error propagation.
  Keystream can be precomputed.
  Block decryption module is not used.
  Special case: the counter mode (CTR).
    Keystream computation can be done in parallel.

## Slide 34: Block Cipher Modes
Counter Mode (CTR)
  Special case of OFB.
  Keystream computation can be done in parallel.
Encrypt
K
n
I0 = IV
k
Ij = Ij +1
n
Note:
Encryption is
performed in AES-CCM
using the CTR mode.
To be XOR-ed with plaintext

## Slide 35: Block Ciphers and Variable Size Payloads
Regardless of encryption algorithm:
  ECB: not recommended for plaintext longer than a block.
  CBC:
    Introduces one block overhead.
    Block boundaries may not match burst boundaries.
    Short messages suffer considerable overhead.
    Error propagation.
    Block chaining interferes with acknowledgements/retransmits.
    No resistance against bit flip attacks.
  CFB: all the problems of CBC, plus:
    A stream cipher which uses plaintext dependent keystream.
  What is left: OFB/CTR.

## Slide 36: Block Ciphers and Variable Size Payloads
CTR (a specific case of OFB):
  Best mode of a block cipher is to emulate a stream cipher!
  No error propagation.
  Block size mismatch is not a problem.
  All the benefits of the stream cipher, but:
    Block ciphers are slower and inefficient than stream ciphers.
  Why emulate a stream cipher with a block cipher?
    We may like to incorporate authenticated encryption AE.
    The only way to do AE is with a block cipher? AES-CCM?
      NO!
    Let us discuss message integrity first and the authenticated encryption later.

## Slide 37: Message Integrity and Authenticated Encryption

## Slide 38: Message Integrity
Encryption alone does not provide message integrity.
Use digital signatures:
  Consider an arbitrary length message M.
  A one-way, collision resistant hash function hSHA-1 with constant output length (160 bits) for arbitrary length input.
  Encrypt hSHA-1 (M) with an encryption algorithm of your choice using a secret key Z.
  Transmit [EK (M), EZ( hSHA-1 (M)) ]
  Receiver decrypts the ciphertext containing the message.
  Receiver attempts to match the received signature using decrypted ciphertext, hSHA-1, Z and the cipher.

## Slide 39: Message Integrity
Hash function computation is not very efficient.
Simplification: 160 bits (for SHA-1) for integrity check may be an overprotection:
  Decimate the signature, i.e., send only a portion of it.
  Beware of birthday attacks, 160 bits require 280 messages.
Is it possible to combine the integrity check and encryption together?
  Would like to compute an integrity check while we are encrypting data.
  Is combining two operations with different objectives safe?

## Slide 40: Authenticated Encryption
Attempts to substitute the cryptographic hash function with simpler checksums lead to security problems:
  N. Bellare and C. Namprempre, “Authenticated encryption: Relations among notions and analysis of the generic composition paradigm,” Advances in Cryptology, ASIACRYPT 2000.
Combine encryption with authentication with minimal additional computational cost:
  C. Jutla, “Encryption modes with almost free message integrity,” Cryptology ePrint archive, Report 2000/039, August 1, 2000.
Provably secure if the employed block cipher is secure.

## Slide 41: Authenticated Encryption
OCB (Offset Codebook) Mode:
  P. Rogaway, M. Bellare, J. Black, and T. Krovetz, “OCB: a block cipher mode of operation for efficient authenticated encryption,” Eighth ACM Conference on Computer Communications and Security, 2001.
    http://csrc.nist.gov/CryptoToolkit/modes/proposedmodes/ocb/ocb-spec.pdf
  Improvement over Jutla’s scheme.
  Requires block cipher calls.
    |M| is the message length.
    n is the block size of the cipher.
  Encrypts a nonce N to compute offsets for each data block.
  Encrypts data blocks similar to ECB but with offsets.
  Provably secure if the block cipher is secure.
  Efficient one pass scheme, parallelizable given M.

## Slide 42: Authenticated Encryption
What is wrong with it?
  Intellectual property issues on all one pass AE schemes.
  802.11 selected OCB for a draft standard then rejected it due to licensing issues.
  Two-pass schemes emerged to bypass the IP issues:
    CCM, EAX: Encrypt using AES-CTR, generates hash using AES-CBC.
    CWC: Encrypts using AES-CTR, generates hash using Carter-Wegman hash function.
  Two pass schemes are not as efficient:
    Tradeoff: licensing payments for implementation costs/limitations.
  But provably secure if the block cipher is secure.

## Slide 43: Authenticated Encryption
AES-CCM:
  CCM: Counter with CBC-MAC.
    D. Whiting, R. Housley, and N. Ferguson, “AES encryption and authentication using CTR mode and CBC-MAC,” IEEE P802.11 doc 02/001r2, May 2002.
      http://csrc.nist.gov/CryptoToolkit/modes/proposedmodes/ccm/ccm.pdf
  Uses AES-CTR to encrypt data.
  Uses AES-CBC to compute MAC:
    Form authentication blocks.
    Encrypt them together with data blocks in AES-CBC mode to obtain authentication data.
    Employs the encryption function of the block cipher only.
  Twice as many block cipher calls as OCB.
    Encryption is parallelizable due to CTR mode.
    Authentication is not parallelizable due to CBC mode.

## Slide 44: Authenticated Encryption
Problems with AES-CCM:
  Natural inefficiency of two-pass structure.
  Non-parallelizable MAC computation.
  Various unrelated parameters are linked in the authentication blocks.
  Summary of criticisms:
    P.Rogaway and D. Wagner, “A critique of CCM,” April 2003. Available at: http:/eprint.iacr.org/2003/070
  AES-EAX by above authors:
    Nonparallelizable authentication.
    Two-pass:
      CTR to encrypt.
      O-MAC (one key CBC-MAC) to authenticate.

## Slide 45: Authenticated Encryption
Parallelizable authentication component:
  CWC:
    http://csrc.nist.gov/CryptoToolkit/modes/proposedmodes/cwc/cwc-spec.pdf
    Another two pass design.
    Provably secure if the block cipher is secure.
    CTR mode for encryption.
    Carter-Wegman universal hash for authentication.
    Hash function is parallelizable but computed for ciphertext.
    One block encryption call for authentication tag after hashing.
Most of the authentication tag generation work is done without the block cipher.
Can’t we get rid of it and use a stream cipher?

## Slide 46: Authenticated Encryption
Stream cipher authenticated encryption schemes:
  Ferguson, Whiting, Schneier, Kelsey, Lucks, and Kohno, “Helix: Fast encryption and authentication in a single cryptographic primitive” http://www.cs.ucsd.edu/users/tkohno/papers/Helix/
  Hawkes and Rose, “Primitive specification of SOBER-128,” Cryptology ePrint Archive Report 2003/48, April 2003.
Both designs have intended strength of 128 bits.
Both are recent and did not receive full attention from research community.
Faster than AES (at least twice in software).
No ‘provably secure’ claims yet.

## Slide 47: Authenticated Encryption
Summary for Authenticated Encryption:
  Started as a good idea:
    ‘message integrity at almost no extra cost’.
  But due to IP issues:
    Resort to two pass schemes.
  Claimed to be secure if the cipher is secure:
    AES is a new cipher, not fully analyzed.
    AES has a unique algebraic structure:
      Cryptanalysis of AES created a new research field.
    Rijndael spec recommends the use of larger block sizes (192 or 256) for message integrity purposes, not 128 as in AES.
    For efficiency reasons, the authentication tag may be as low as 4 octets (see AES-CCM):
      Minimal protection against birthday attacks.

## Slide 48: RC4 Stream Cipher

## Slide 49: RC4 Stream Cipher
Designed by Ron Rivest (RSA Labs) in 1987.
Kept secret until 1994.
Extremely simple and efficient in software.
About 10-15 times faster than DES.
Once initialized, encryption cost is independent of key length. Accepts arbitrary key lengths in bytes.
Widely used, see SSL info page:
  http://developer.netscape.com/docs/manuals/security/sslin/contents.htm
  “RC4 with 128-bit encryption and MD5 message authentication.
  Because the RC4 and RC2 ciphers have 128-bit encryption, they are the second
  strongest next to Triple DES (Data Encryption Standard), with 168-bit encryption.
  RC4 and RC2 128-bit encryption permits approximately 3.4 * 1038 possible keys,
  making them very difficult to crack. RC4 ciphers are the fastest of the supported
  ciphers. Both SSL 2.0 and SSL 3.0 support this cipher suite.”

## Slide 50: RC4 Stream Cipher Structure
S[0]
S[1]
S[2]
S[255]
S[254]
S[253]
127
34
250
1
78
95
State Table: 256 entries, each 8 bits long. Stores a permutation
with 255! possibilities: state table can be represented by
approximately 1700 bits, i.e., 21700 states.
Two 8 bit pointers: i and j to shuffle the permutation matrix
and produce the keystream.

## Slide 51: RC4 Weak Keys
Common statement:
  “RC4 has weak keys: for such keys, initial keystream bytes are correlated with only a few bytes of the key. This reduces the work required to search for the key, especially with known plaintext.”
This originates from the simplicity of the initialization routine and can be corrected.
But it only applies to initial keystream bytes.
  Discard these bytes.
Next few pages provide a mathematical analysis.
  Will be skipped for this talk.

## Slide 52: RC4 Weak Keys - Analysis
Reference: A. Roos, “A Class of Weak Keys in the RC4 Stream Cipher”, 09/22/1995.
RC4 uses a variable key length to initialize a 256 byte state table. Before key insertion, the state table takes on the values:
  S[0]=0; S[1]=1; …;S[i]=i; …;S[255]=255.
Let us assume the secret key K is L bytes long:
  {K[0],K[1],K[2],…,K[L]}

## Slide 53: RC4 Weak Keys - Analysis
Key insertion procedure is as follows:
  j = 0;
  for (i = 0; i < L; i++)
  {
  j = ( j + K[i]+S[i%256] ) % 256;
  swap_byte( &S[i % 256], &S[j] );
  }
The state table contains a permutation of integers from 0 to 256.
Desirable: Each state table entry should be a function of all of the key bytes.

## Slide 54: RC4 Weak Keys - Analysis
State table is changed via the function call ‘swap_byte( )’.
Every state table entry is swapped at least once, due to i:
  swap_byte( &S[i % 256], &S[j] );
It may also be swapped due to j.
Assume that the variable ‘j’ in the loop is uniformly distributed, and L < 256.
  Probability of NO SWAP due to j:
    P = (255/256)255 = 0.37

## Slide 55: RC4 Weak Keys -Analysis
There is a 37 percent probability that S[m] depends only on K[0], …,K[m].
  Initial states are not affected by the full key.
  Most troublesome is S[0].
Most likely value for the initial states can be determined assuming that the ramp initialization is not disturbed in the beginning stages of key insertion:
  Expected Value{S[m]} = ( K[0] + … + K[m] + 0+ … + m ) mod 256.
  Expected Value{S[0]} = K[0].
  Expected Value{S[1]} = ( K[0] + K[1] + 1 ) mod 256.
  Expected Value{S[2]} = ( K[0] + K[1] +K[2]+ 1+2 ) mod 256.

## Slide 56: RC4 Weak Keys - Analysis
0-7 | 37.0 | 36.8 | 36.2 | 35.8 | 34.9 | 34.0 | 33.0 | 32.2
8-15 | 30.9 | 29.8 | 28.5 | 27.5 | 26.0 | 24.5 | 22.9 | 21.6
16-23 | 20.3 | 18.9 | 17.3 | 16.1 | 14.7 | 13.5 | 12.4 | 11.2
24-31 | 10.1 | 9.0 | 8.2 | 7.4 | 6.4 | 5.7 | 5.1 | 4.4
32-39 | 3.9 | 3.5 | 3.0 | 2.6 | 2.3 | 2.0 | 1.7 | 1.4
40-47 | 1.3 | 1.2 | 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.6
Prob. (%) of Matching the Expected Value with 80 bit keys
State Number
1/256 = 0.391%

## Slide 57: RC4 Weak Keys - Analysis
To generate keystream bytes:
  i=0; j = 0;
  i = (i+1) % 256;
  j = ( j+ S[i%256] ) % 256;
  swap_byte( &S[i], &S[j] );
  indx = (S[i]+S[j]) % 256;
  generated_keyStream_byte = S[indx];
What happens if S[1] = 1, when generating the initial keystream byte?
  generated_keyStream_byte = S[2];

## Slide 58: RC4 Weak Keys - Analysis
Expected values of states:
  S[0]=K[0],
  S[1]=K[0]+K[1]+1 mod 256
  S[2]=K[0]+K[1]+K[2]+1+2 mod 256.
Therefore, if K[0]+K[1] = 0 mod 256, then
Expected Value{generated_keyStream_byte} = S[2] = (K[2]+3) mod 256.

## Slide 59: RC4 Weak Key References
A. Roos, “A Class of Weak Keys in the RC4 Stream Cipher,” 09/22/1995.
  http://marcel.wanda.ch/Archive/WeakKeys-report.pdf
R. Rivest, “RSA Security Response to Weaknesses in Key Scheduling Algorithm of RC4”, RSA Labs Technical Note.
  http:/www.rsasecurity.com/rsalabs/technotes/wep.html
S. Fluhrer, I. Mantin, and A. Shamir, “Weaknesses in the Key Scheduling Algorithm of RC4,” Lecture Notes in Computer Science, 2001.
  http://citeseer.ist.psu.edu/fluhrer01weaknesses.html
A. Stubblefield, J. Ioannidis, and A. D. Rubin, “Using the Fluhrer, Mantin, and Shamir Attack to Break WEP,” AT&T Labs Technical Report, August 6, 2001.
  http:// www.isoc.org/isoc/conferences/ndss/ 02/proceedings/papers/stubbl.pdf

## Slide 60: WEP Disaster with RC4
40 bit secret key K. (not large enough).
24 bit known initialization vector IV. (repeats over the lifetime of K, results in key reuse!).
Diffusion not implemented (The first keystream byte is predictable).
64 bit composite key to initialize RC4 is [IV, K] (One out of every 256 keys is weak).
The first byte of the message is known, and this leads to a known plaintext attack.
CRC is encrypted: Attempts to crack the key can be verified by checking the CRC.

## Slide 61: WEP Disaster Recovery
Select proper size keys: The keystream generation process load is independent of the key size. Export requirements are relaxed by the government.
Diffuse keys properly, i.e., discard at least first 256 bytes of the keystream.
Limit the amount of data encrypted by the same key and by the same IV.
Select IV’s long enough to prevent key reuse.
Form composite keys properly from secret key and IV using hash functions MD5, SHA-1.
Do not encrypt CRC: Linear CRC does not provide any authentication benefit but helps the cracker to check results.

## Slide 62: RC4 Keystream Properties
With proper initialization (with diffusion):
  How difficult it is to distinguish RC4 keystream from truly random binary sequence?
    Known plaintext attack.
    Length of plaintext to perform a reliable test?
  What is the best result for recovering the secret key:
    From the observed keystream.
    This also applies to a known plaintext attack.

## Slide 63: RC4 Keystream Properties
Distinguishability against a truly random sequence
  By observing 230.6 keystream bytes:
    And analyzing the output pairs from the RC4 generator.
    Possible to detect RC4 stream cipher against a truly random binary sequence.
    Scott Fluhrer, David McGrew, "Statistical Analysis of the Alleged RC4 Keystream Generator", in Proceedings of FSE 2000.
    http://www.mindspring.com/~dmcgrew/rc4-03.pdf
  Against future attacks:
    Decimate the output of RC4, use every other output byte.
    Limit keystream generated with the same secret key and IV.

## Slide 64: RC4 Keystream Properties
Recovery of the secret key from keystream:
  L.R. Knudsen, W. Meier, V. Rijmen, S. Verdoolaege, “Analysis Methods for (alleged) RC4,” Advances in Cryptology - ASIACRYPT'98, Springer Verlag, 1998.
  Attempt to break modified/simplified versions of RC4.
  Requires known plaintext.
  Attack attempts to track RC4 states.
  Expected computational demand for RC4 with 8 bit words:
  This makes the attack unfeasible to the properly implemented cipher:
    It may be better to do an exhaustive search if the key size is less than 850 bits.
    For perspective, a 128 bit cipher requires at most 2128 attempts to discover the secret key.

## Slide 65: RC4 Summary
Very simple and efficient cipher.
An attempt to approximate a one time pad.
Keystream is not distinguishable from a truly random sequence, if:
  Keystream is decimated.
  Keystream is limited in duration.
Secret key recovery through output analysis is costlier than an exhaustive search if algorithm is properly implemented.
It can accept arbitrary key lengths and encrypt arbitrary blocks of data.
Most widely used cipher in the Internet era.
Available for cryptanalysis for more than a decade.
Flawed WEP implementation:
  Is a combination/comedy of errors.
  The issues were well understood before WEP (1995) but ignored.
There are no publicly known practical attacks against the properly configured RC4 generator.

## Slide 66: Block Cipher From A Stream Cipher

## Slide 67: Block Cipher From A Stream Cipher
Block ciphers can be made to operate as stream ciphers, e.g., CTR mode as in AES-CCM.
Reverse is possible. We will give a simple example to make one (not proposed for 802.20).
Next few pages will present you a simple example.
  Will skip in the presentation.

## Slide 68: Block Cipher From A Stream Cipher
The goal is to stress the point that stream ciphers are more versatile than block ciphers for wireless communications.
Our example:
  Should not reveal keystream when encrypting known plaintext.
  Should be able to encrypt a multitude of blocklengths.
  Should be unbreakable if the utilized stream cipher is secure.
  Should be simple to encrypt, and somewhat reasonable to decrypt.

## Slide 69: Block Cipher From A Stream Cipher
Consider M bits per block to encrypt.
Generate M keystream bits using the RC4 stream generator to initialize the first variable ‘A’.
Repeat for ‘B’.
ENCRYPT:
  Y = A * X + B in Galois Field 2M.
If A is all zeros, then set it to the identity element with respect to multiplication in GF(2M).

## Slide 70: Block Cipher From A Stream Cipher
  Y = A * X + B in GF(2M).
Two unknowns per equation with known plaintext. Unsolvable for A and B given X and Y!
If X = 0, then B is observable but A is not, happens with probability 1/2M for uniformly distributed X.
DECRYPTION:
  Z = inv(A )* (Y + B) in GF(2M).
  inv(A )*A = 1 in GF(2M), found using Extended
  Euclidean Algorithm.

## Slide 71: Block Cipher From A Stream Cipher
Example designed illustrates the asymmetries possible in a block cipher.
Encryption requires 1 multiplication and decryption requires 1multiplication and an inversion, approximately 11 multiplies.
It is possible to encrypt a burst of arbitrary length given the generator polynomial.
Can you state AES-256 in any mode is more secure than BC-RC4 with 256-1700 bits secret key and 128 bit blocks?
For other examples of variable size block ciphers and making block ciphers out of stream ciphers, refer to:
  http://www.ciphersbyritter.com/

## Slide 72: Issues with AES (Advanced Encryption Standard) Open problems with AES

## Slide 73: AES for 802.20?
For a wireless system with variable burst payloads:
  A block cipher architecture must have an essentially arbitrary and dynamically-variable block size.
  It is necessary that good diffusion be produced from all plaintext input bits to all ciphertext output bits.
  AES does not conform to the first requirement, unless it is used as a stream cipher (CTR mode).
  Why not use a true stream cipher:
    With less computational cost.
    RC4 is approximately 5-10 times faster depending on the platform.
    That received widespread efforts for its cryptanalysis.

## Slide 74: AES for 802.20?
Why not use a true stream cipher like RC4, rather than emulating one with AES?
  Federal Information Processing Standard, FIPS-197.
  Just because it is in a standard?
  From the NIST web page:
    “…The AES will be a public algorithm designed to protect sensitive government information well into the 21st century. It will replace the aging Data Encryption Standard, which NIST adopted in 1977 as a Federal Information Processing Standard used by federal agencies to protect sensitive, unclassified information…”
Are we going to enforce a DES/3DES substitute which has NO reference to wireless communications and air interface time optimization issues?
Is AES secure?

## Slide 75: AES Background
The AES is defined as the Rijndael cipher with a blocklength of 128 bits, and key lengths of 128, 192 and 256 bits, using 10, 12 or 14 rounds.
  http://csrc.nist.gov/CryptoToolkit/aes/rijndael/Rijndael.pdf
Designed to have immunity against classical attacks, such as linear/differential cryptanalysis.
Algorithm accepted as a standard in 2000: did not receive full attention until acceptance.
Designed to be implementation friendly (compared to DES and 3DES):
  AES with 128 bit secret key is approximately 3 times faster than DES on a 32 bit CPU.
  http://fp.gladman.plus.com/cryptography_technology/aes/
  About similar speed to DES on an 8-bit smart card processor.

## Slide 76: Is AES Secure?
Despite the short period since acceptance, new attacks appeared which take advantage of the algebraic structure of AES:
  N. Ferguson, R. Schroeppel, and D. Whiting, “A simple algebraic representation of Rijndael,” Selected Areas in Cryptography, Proc. SAC 2001, Lecture Notes in Computer Science #2259, pp. 103–111, Springer Verlag, 2001.
  http://www.macfergus.com/pub/rdalgeq.html
AES can be written as an overdefined system of multivariate quadratic equations (MQ):
  N. T. Courtois and J. Pieprzyk, “Cryptanalysis Of Block Ciphers with Overdefined Systems of Equations,” AsiaCrypt 2002.
  http://eprint.iacr.org/2002/044.pdf

## Slide 77: Is AES Secure?
Although MQ is an NP-hard problem:
  Complexity drops substantially when the MQ becomes overdefined.
    A. Shamir, J. Patarin, N. Courtois, A. Klimov, “Efficient algorithms for solving overdefined systems of multivariate polynomial equations,” pp. 392-407, Eurocrypt’ 2000.
    http://www.minrank.org/xlfull.pdf

## Slide 78: Is AES Secure?
According to Courtois and Pieprzyk:
  If the MQ is sparse and has a regular structure, it becomes much easier to solve it.
  For 128-bit AES, the problem of recovering the secret key from one single plaintext can be written as:
    A system of 8000 quadratic equations with 1600 binary unknowns.
  Therefore, security of the AES relies on:
    the assumption that it is not feasible to solve such systems in the near future.
  Paper claims minimal plaintext requirement compared to classical attacks (linear/differential cryptanalysis).

## Slide 79: Is AES Secure?
To reiterate, we quote the full abstract of:
N. Ferguson, R. Schroeppel, and D. Whiting, “A simple algebraic representation of Rijndael”
  “We show that there is a very straightforward closed algebraic formula for the Rijndael block cipher.
  This formula is highly structured and far simpler than algebraic formulations of any other block cipher we know.
  The security of Rijndael depends on a new and untested hardness assumption: it is computationally infeasible to solve equations of this type.
  The lack of research on this new assumption raises concerns over the wisdom of using Rijndael for security-critical applications.”

## Slide 80: Summary: Is AES Secure?
For an updated list of attacks and algorithms, refer to:
  http://www.cryptosystem.net/aes/
In summary, AES:
  Provided cryptanalysts a new problem to attack.
  Introduced integration issues for certain platforms that require hardware implementation of AES.
  In its most practical mode (CTR), generated yet another stream cipher whose properties are not yet fully analyzed.
  Its security is based on the unfeasibility of a sparse and structured MQ problem.
    UNTESTED assumption.
  Led to Authenticated Encryption (AE) schemes whose provable security in turn are based on that of AES.

## Slide 81: Recommendations Note: ArrayComm will propose a change to the Requirements Document.

## Slide 82: Make Stream Cipher Mode Mandatory
Problems with block ciphers in general:
  Data expansion and overhead.
  Block fragmentation (burst and block size mismatch).
  Error propagation.
  Block chaining interactions with ARQ.
  Relative complexity.
For encryption, regardless of the type of cipher:
  Best mode of operation is to emulate a stream cipher.
Restrict encryption to stream cipher mode:
  Natural mode for stream ciphers like RC4.
  CTR mode for block ciphers like AES.

## Slide 83: Do Not Make AES Mandatory
AES has the following particular problems:
  Relatively recent algorithm.
  Did not receive full attention until acceptance in 2000.
  Its security appears to be based on an untested hardness assumption.
Still relatively complex compared to stream ciphers. About 5-10 times slower than RC4 depending on platform.
  May not serve the best interests of the standard.
  May not serve the best interests of the market (level of end-user security versus cost/complexity of devices).
Authenticated encryption methods that use core algorithms other than AES are available, AES is NOT a prerequisite.
Let the rest of the industry assume the full risk of a new algorithm. Reconsider it in the future.

## Slide 84: Use Properly Implemented RC4 as the Initial Encryption Method
With the proper implementation of RC4:
  Proper use of secret key and initialization vectors.
  Key diffusion.
  Limited amount of keystream per initialization.
  Decimated output.
  Non-encrypted CRC.
It is not practically possible:
  To detect whether RC4 keystream is different than truly random data. Good approximation to one time pad.
  Track the internal state of the generator to recover the secret key.

## Slide 85: Use Properly Implemented RC4 as the Initial Encryption Method
RC4 is extremely efficient for both software and hardware implementations.
Withstood expert public cryptanalysis for more than a decade.
  Its simple state propagation equations enabled widespread analysis.
Arbitrary key lengths are supported.
  Recommend 256 bit keys.
Most widely used cipher in the Internet era.
May serve the best interests of the standard and the public:
  Secure yet simple design helps time-to-market issues, especially with low computational power devices.

## Slide 86: Do Not Make Authenticated Encryption Mandatory
Message integrity/authentication methods with less than 128 bits are not cryptographically secure.
  Rijndael spec suggests the use of 192 or 256 bit block lengths for secure hashes with CBC mode.
  AES supports Rijndael with 128 bit blocks.
One-pass authenticated encryption (AE) schemes are licensed but more efficient.
  But they are block encryptors not in line with our stream cipher mode requirement.
Most license-free AE schemes require twice the number of block encryption calls.
  Half of which are non-parallelizable.

## Slide 87: Do Not Make Authenticated Encryption Mandatory
Recent AE schemes provide means to generate the authentication tag without the block cipher:
  Using hash functions (Carter-Wegman hash in AES-CWC).
  Only the final hash is encrypted by the block cipher.
  Similar methods can be used with stream ciphers.
This field has the potential to bear new methods:
  No need to restrict ourselves to current two-pass inefficient methods because they are license free.
  No need to adopt a block cipher just because most of the AE schemes assume the use of one.
It is plausible to defer message integrity to application layer rather than promising a false sense of security with a short authentication tag.

## Slide 88: List of Recommendations
Make stream cipher mode mandatory.
Do not make AES mandatory.
Use properly implemented RC4 as the initial encryption method.
Do not make authenticated encryption mandatory.
  May even consider deferring it to higher layers.