## Slide 2: 802.20 Evaluation Criteria and Traffic Models Status Update
Farooq Khan
IEEE 802.20 Plenary Meeting
Portland, Oregon, USA
July 12-16, 2004

## Slide 3: Evaluation Criteria Status
Two AHGs during the May Interim:
  Link-system interface
  Channel Models
Three conference calls since May Interim:
  06/06: RF Performance Characteristics
  06/15: Traffic models
  06/29: Link-system interface
Open issues not discussed:
  Phased approach, Link budget criteria, application specific fairness/outage criteria and system simulation calibration etc.
Updated 802.20 Evaluation Criteria Version 10 document available in the email drop-box:
  Evaluation criteria and traffic models documents merged

## Slide 4: RF Performance Characteristics
Proposed key RF performance characteristics
  Transmitter power, Transmitter Emission Mask, Adjacent channel (power) Leakage Ratio
  Receiver Sensitivity, Receiver Selectivity, Receiver Blocking
Decided to use normalized Transmitter power
  43dBm/MHz
Decided to model the adjacent channel leakage
  Exact method and/or values are TBD
Not yet decided if a Transmitter Emission Mask would be defined.
Need further investigation if and how receiver characteristics (Receiver Sensitivity, Receiver Selectivity, Receiver Blocking) are going to be modeled.

## Slide 5: Traffic Models
Specification of traffic mix
  Discussed various possible approaches
  Phase 1 use full buffers model
  A few other traffic scenarios can be defined for the subsequent phase of the simulations, for example:
    Separate simulation with VoIP traffic only
    Separate simulation with web browsing traffic only
    A traffic mix scenario
FTP traffic model
  Decided (06/15/2004) not to modify the “think time” behavior in the existing FTP traffic model.
VoIP Traffic Model
  Need to finalize on VoIP source traffic model
Contributions invited on Wireless multi-party Gaming traffic models

## Slide 6: Link-System Interface
Actual link curves is the default methodology for the link-system interface:
  Can always be used even if an agreement on a common methodology is reached.
The group is trying to define a common methodology for the link-system interface.
  If a common methodology is used then no justification is required from the proponent
In the absence of a common methodology, a technology specific methodology can be used if provided with full verification subject to the satisfaction of the group.

## Slide 7: Common LSI Methodology
A contribution, summarizing different possible methods, was discussed over the 06/29 conference call:
  3GPP2 1xEV-DV/DO Method-1Quasi-Static Method,
  1xEV-DV/DO Method 2 - Convex Method
  European IST project FITNESS Polynomial based method
  Methods to Predict Performance of Convolutional Codes
  3GPP Exponential Effective SIR Mapping (EESM) for OFDM
Need to define the test cases and the accuracy requirements that would be used in the method selection process
  The baseline for the accuracy will be actual link curves

## Slide 8: Phased Approach
The details of phase 1 are currently being discussed in the evaluation criteria:
  Agreed to use 19-cells 3-sector wrap-around configuration, Full buffers (hungry) traffic, simulation calibration, link-system interface etc.
  Current Recommendation is to use suburban macro, 3 Km/h pedestrian B and 120Km/h Vehicular B channel models.
The issues that need further consideration:
  Full-duplex simulation, and handoff modeling etc.
The 802.20 evaluation will be structured with multiple phases with each phase progressively adding more complexity. The evaluation work for each proposal may then be compared at each phase to ensure a progressive "apples to apples" comparison of proposals. This structured approach will also provide performance metrics for the physical and link layer performance early rather than later in the evaluation process.
Phase 1 of the evaluation will consist of:
- Items/issues/criteria that are required for the calibration of simulations
- Items/issues/criteria that will draw out the important differences between the various proposals that cannot be otherwise inferred.
The goals at the end of phase 1 are, first, to achieve confidence that different simulation models are calibrated and, two, to present fundamental performance metrics for the physical and link layer of various proposals.

## Slide 9: Link Budget Criteria
Consensus on most of the link budget parameters
Open issue: Should maximum range (link budget) be used as a performance metric for proposal comparison or not?

## Slide 10: Application specific criteria
A fairness criteria is defined for the best effort data traffic:
  application specific outage and QoS (FER, delay etc.) criteria need to be defined for other applications!
Contributions are also invited on additional fairness metrics
In the evaluation of spectral efficiency and in order to make a fair comparison of different proposals, it is important that all mobile users be provided with a minimal level of throughput. The fairness for best effort traffic (HTTP, FTP and full buffers) is evaluated by determining the normalized cumulative distribution function (CDF) of the user throughput, which meets a predetermined function. For applications other than best effort, application specific outage criteria are defined. The proposals will also provide additional fairness metrics. The details of the additional fairness metrics are TBD (see for example IEEE C802.20-04/05).

## Slide 11: System simulation calibration
The evaluation criteria would specify a system simulation calibration process.
  Calibration would be done as part of phase 1 of simulations
However, it is not clear, at this stage, to what level of detail simulations need to be calibrated.
The group is open to proposals to nail down the calibration specifications.

## Slide 12: Channel Models
Joint 802.20 Channel Models and Evaluation Criteria AHG (05/13/2004)
Link-system interface:
  Use random phase in the link channel model;
  Use AOA/AOD as random phase to do the link/system simulation;
Simplify the SCM in order to make link curves and link-system interface (LSI) approach feasible
Agree upon the table of model parameters which comply with ITU models
Other alternative - the procedure to make sure that SCM-MIMO model collapses to ITU SISO model
Channel mix issue needs to be addressed;
Investigate the necessity of additional power delay profile randomness across all users

## Slide 13: Proposed AHGs
Link-System Interface (1hr)
RF Performance Characteristics (1hr)
Joint Ad Hoc with Channels Models CG (1hr)
?