## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | Link-system interface simulation methodologies | 
Date Submitted | 2004-07-12 | 
Source(s) | Anna Tee 1301 E Lookout Dr., Richardson, TX 75082 | Voice: (972) 761-7437 Fax: (972) 761-7909 Email: atee@sta.samsung.com
 | Seokhyun Yoon 416 Maetan 3-Dong Suwon, Korea 442-742 | Voice: +82-31-279-5841 Fax: +82-31-279-5130 Email: skhyun.yoon@samsung.com
 | Joseph Cleveland 1301 E Lookout Dr., Richardson, TX 75082 | Voice: (972) 761-7981 Fax: (972) 761-7909 Email: jclevela@sta.samsung.com
Re: | MBWA Call for Contributions, Session #9, July 2004 | 
Abstract | This contribution discusses the possible methodologies for link-system simulation interface. The various methodologies are compared and recommendation is made to adopt the most appropriate method for the simulation and evaluation of IEEE 802.20 proposals. | 
Purpose | For discussion and adoption into IEEE 802.20 Evaluation Criteria Document. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: Link-System Interface Simulation Methodologies
Anna Tee
Seokhyun Yoon
Joseph Cleveland
June 29, 2004

## Slide 3: Topics
Problem statements
Advantages & Requirements of a Link-System Simulation Interface (aka: PHY Abstraction) Methodology
General Overview of Methods used in other Communication Standards Organizations
  Methods based on Shannon’s Theorem on Channel Capacity
  Estimates on effective Eb/No for convolutional codes in fading channels
  Methods for OFDM based Systems
  Exponential Effective SIR Mapping
Simulation Results for EESM
References

## Slide 4: Problem Statement
Modeling Performance of Wireless Link in a System Level Simulation
In the System Simulation, the profile of Received Signal to Interference Ratio (SIR) is computed and sampled at regular time intervals for each user in the cell layout model.
The same SIR value in different channels environment typically results in different performance in BER and PER
  For example, in a frequency selective fading channel, the SIR value fluctuates from one subcarrier to another in an OFDM system. Thus the PER performance cannot be predicted correctly using the average packet SIR.
Infeasible and Impractical to Simulate the Instantaneous Performance of a Wireless Link in Real-time
A mapping is required between each sampled SIR value in the system level and the implied BER or FER performance

## Slide 5: Advantages & Requirements of a Link-System Simulation Interface Methodology
Reduce computation load for off-line link level simulation
An ideal method should have a computation load that is independent of the channel models
The link performance should be estimated accurately, based on performance of modulation and coding scheme
A method that computes the equivalent SIR which corresponds to the same BER/FER performance in an AWGN channel

## Slide 6: General Overview of Methods used in other Communication Standards Organizations
3GPP2: 1xEV-DV/DO [1,2]
  Method 1: Quasi-Static Method
Further account for:-
  Coding Gain
  Doppler Penalty
  De-mapping Penalty

## Slide 7: Methods based on Shannon’s Theorem on Channel Capacity
  1xEV-DV/DO Method 2 - Convex Method:
    Use Shannon’s Theorem to compute the instantaneous channel capacity based on the SIR sample at the system level
    Compute the equivalent SNR in an AWGN channel that results in the same average channel capacity
    A correction factor (Q) is included to account for practical performance degradation from Shannon’s capacity limit
where eff = Effective SNR
j = SIR of j-th segment in which channel response remains ~constant
N = Total number of segments that have ~constant channel response

## Slide 8: Methods for OFDM based system
  A similar method that is based on the application of Shannon’s Theorem on Channel Capacity is proposed by the European IST project: FITNESS [3]
    A mapping between Channel Capacity and Block Error Rate (BLER) is required and is modeled by a 2nd order polynomial
    Coefficients of the polynomial () can be found by the least squares fitting to simulation data
  The above method has also been proposed in IEEE 802.11n PHY abstraction ad hoc group [4]
    A packet is declared in error when the instantaneous data rate exceeds the channel capacity

## Slide 9: Methods to Predict Performance of Convolutional Codes
  Other methods that have been discussed in the literature and proposed in 802.11n include methods to predict error rate performance for convolutional codes based on the probability of error event sequence [5, 6]
  Two possible estimates have been derived based on the Bhattacharya bound for error rate performance of convolutional codes in [6].
  For a minimum distance error event of length D,
    where J(k) is the index of the Eb/No level corresponding to the bit in position k.
    Choose the minimum (Eb/No)eff , for k = 1, 2, … (N-D+1), N = length of frame
      Zworst = Max {Geometric mean of Zk} where Zk are the error probabilities at each Eb/No level (bit group k) corresponding to the bit sequence of length D
    Compute (Eb/No)eff corresponding to the same AWGN error rate performance as the Arithmetic Mean of the AWGN error probabilities for all (Eb/No)eff computed using the above equation for k = 1, 2, …, (N-D+1).

## Slide 10: Exponential Effective SIR Mapping (EESM)
EESM has been discussed and adopted in 3GPP feasibility study on OFDM [7,8,9,10]
Derivation of EESM is based on the Union-Chernoff bound for error probabilities
Basic idea is to find an equivalent SIR in the AWGN channel that results in the same BLER, using the Union-Chernoff bound to relate the error probability to the corresponding SIR in a channel/subchannel with an approximately constant channel response
An adjustment factor () is necessary for QPSK and higher-order modulation schemes
where eff = Effective SIR
j = SIR of j-th subcarrier, or segment in which channel response remains ~constant
N = Total number of subcarriers, or segments that have ~constant channel response

## Slide 11: Simulation results for EESM
Simulation data shown in [9] has indicated good match of results, independent of channel models, i.e., the same factor  has been used for different channel models with the same modulation and coding scheme (MCS)
Less accurate in case of M-QAM, for M > 4
Simulation Assumptions:
  Channel model unchanged during the simulation duration, i.e., either 10000 TTIs (2ms/TTI) or until 200 block errors were observed.
  Random interleaving applied to each OFDM symbol
For each MCS,  is estimated using the Minimum Mean Square Error (MMSE) criterion:
where eff () = Mean square error of the Effective SIR computed based on 
SIReff,m() = Effective SIR computed for the mth BLER point, as a function of 
SIRAWGN,m = SIR in AWGN channel which corresponds to mth BLER point
NB = Total number of BLER points

## Slide 12: Comments & Recommendation
EESM has been shown to be effective in predicting link-level performance in a system level simulation
Through a smaller number of link-level simulation runs, the parameter  can be estimated for each modulation and coding combination, using the least- squares criteria
For each SIR sample from the system simulation based on any multipath fading channel profile, the effective SIR in the AWGN channel can be computed using EESM. The corresponding BLER performance can be found through table look-up from the pre-computed AWGN BLER performance for each modulation and coding combination.
Recommendation:
Adopt EESM in IEEE 802.20 evaluation methodology

## Slide 13: References
“1xEV-DV Evaluation Methodology (V13), 3GPP2 / TSG-C.R1002
3GPP2 TSG-C, “1xEV-DO Evaluation Methodology (V1.3), C30-DOAH-20030807-004
“MTMR Baseband Transceivers Needs for Intra- & Inter-system transparent UMTS/WLAN Operation”, IST-2000-30116 FITNESS, D3.3.1/v1.0
S. Valle, A. Poloni, G. Villa, “802.11 TGn Proposal for PHY abstraction in MAC simulators”, IEEE 802.11-04/0184, February 16, 2004.
J. Ketchum, B. Bjerke, S. Nanda, R. Waldon, “PHY Abstraction for System Simulation”, IEEE 802.11-04/0174r1, February 2004.
S. Nanda, K. Rege, “Frame Error Rates for Convolutional Codes on Fading Channels and the Concept of Effective Eb/No”, IEEE Trans. Vehicular Technology, Vol. 47, No. 4, Nov. 1998.
“Considerations on the System-Performance evaluation of HSDPA using OFDM modulation”, Ericsson, 3GPP TSG_RAN WG1 #34, R1-030999, October, 2003.
“System-Level evaluation of OFDM - further Considerations”, Ericsson, 3GPP TSG-RAN WG1 #35, R1-031303, November 17-21, 2003.
“OFDM EESM simulation Results for System-Level Performance Evaluations, and Text Proposal for Section A. 4.5 of TR 25.892”, Nortel Networks, R1-04-0089, January, 2004
“Feasibility Study for OFDM for UTRAN enhancement, Release 6”, 3GPP TSG RAN, TR 25.892 v1.1.0, March 2004.