## Slide 1
Project
IEEE 802.20 Working Group on Mobile Broadband Wireless Access
<http://grouper.ieee.org/groups/802/20/>
Title
Overview of the Spatial Channel Model developed in 3GPP-3GPP2
Date Submitted
2004-11-15
Source(s)
Achilles Kogiantis
Rm. 1A-251, 67 Whippany Rd
Whippany, NJ 07981
Voice: (973) 386-4399 Fax: (973) 386-2651
Email: achilles@lucent.com
Re:
MBWA Call for Contributions
Abstract
This contribution provides a detailed overview of the spatial channel model that was developed jointly in the 3GPP and 3GPP2 standard bodies for link and system level simulations
Purpose
For Discussion
Notice
This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20.
Patent Policy
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>.
2004-11-15

## Slide 2: Overview of the Joint 3GPP 3GPP2 Spatial Channel Model Recommendation
Achilles Kogiantis
802.20 Session 11
San Antonio, TX
November 17, 2004

## Slide 3: SCM standards activity
A joint adhoc was created by 3GPP and 3GPP2 to specify spatial channel models (April 2002)
  The adhoc group completed its task in June 2003.
    Recommendation to 3GPP RAN1 was adopted as permanent document TR 25.996
    Recommendation to 3GPP2 WG3 made in June 2003
  SCM Participating Companies:
Atelier Telecom
DISA
Elektrobit
Ericsson
ETRI
France Telecom
Infineon
Interdigital
IP Wireless
LG Electronics
Lucent Technologies
MERL
Mitsubishi
Motorola
Nokia
Nortel Networks
Panasonic
Samsung
Spirent Communications
Telia
Texas Instruments
TTPCom
Qualcomm

## Slide 4: SCM Approach
The SCM AHG work was intended to be an extension to the available evaluation methodology for multiple antenna studies
The add-on features of the SCM recommendations are:
  System Level channel modeling are the core specifications (link level definitions are also provided for calibration)
  The wideband model addresses both 1.25MHz and 5MHz channel bandwidths
  Modeling is developed as a general framework for multiple antenna transmit and/or receive configurations
  No specific antenna topologies are enforced. Specifications are independent of antenna arrangements
  Specifications reflect on numerous measurement campaigns and literature surveys (also COST 259 recommendations)
  The SCM AHG sought a balance between the representation of realistic spatial environments and modeling complexity.

## Slide 5: SCM Structure
System Level Model
  Each drop is assigned spatial-temporal parameters from pre-determined distributions
Evaluation Methodology specifications
  Define the methods to be used for utilizing the SCM in system level simulations.
  Objective is not to deviate from currently established methodologies
Link Level Model
  Contains a specific set of fixed spatial-temporal parameters
  Used for calibration purposes only

## Slide 6: System Level SCM – Channel Scenarios
Choose a Channel Scenario common to all drops. Each channel scenario defines a specific set of typical physical parameter values.
  Suburban Macro
    BS-BS distance aprox. 3Km. BS antenna position: High
    Describes small angle spread (AS), small delay spread (DS) environments: rural areas
  Urban Macro
    BS-BS distance aprox. 3Km. BS antenna position: High
    Describes moderate to high AS, large DS environments: large cells with urban buildings in the vicinity; significant scattering
  Urban Micro
    BS-BS distance aprox. 1Km
    Describes large AS, moderate DS environments. BS antenna located at rooftop. Small urban cells with a wide range of per drop AS,DS values
  Additional modeling options:
    Line of Sight (LOS). Applicable to urban micro
    Far Scatterer Cluster. Applicable to urban macro. Models the bad urban case.
    Urban Canyon. Applicable to urban macro

## Slide 7: System channel model overview
3. Generate channel coefficients
2. Determine user parameters
1. Choose scenario
Suburban
macro
Urban
macro
Urban
micro
Angle spread
Lognormal shadowing
Delay spread
Pathloss
Orientation, Speed Vector
Antenna gains
Angles of departure (paths)
Angles of departure (subpaths)
Path delays
Average path powers
Angles of arrival (paths)
Angles of arrival (subpaths)
Polarization
LOS (urban micro)
Far scattering cluster (urban macro)
Urban canyon (urban macro)
Options

## Slide 8: Pathloss - Shadowing
Macro channels follow the Hata COST 231
Urban micro follows the Walfish-Ikegami pathloss model

## Slide 9: Correlation of Narrowband Parameters
Site to Site Correlation = 0.5
Correlation between Angle Spread, Delay Spread, Shadowing (LN) :
Define and as iid Gaussian, N(0,1) with BS index (n = 1 … N).
Intra-site correlations
Site to site correlation

## Slide 10: Generation of Narrowband Parameters
For a given channel scenario draw random lognormal realizations for AS, DS, LN ( ) in an MS drop and for each BS n :
The distributions are a priori determined.
Each macro channel scenario is characterized by a unique set of mean, variance values:

## Slide 11: Macro Narrowband Statistics
Angle Spead, Delay Spead lognormal distributions (model and simulated)

## Slide 12: Wideband Characterization
After narrowband parameters are drawn per drop, the per-path details are specified:
Generate Power Delay Profile (PDP) (path delays, path powers)
PDP is generated using N=6 paths (for all scenarios)
Generate per-path Angle of Arrival and Angle spread
Each path is assigned fixed angle spread with Laplacian Angular Power Spectrum at BS
Each path is assigned fixed angle spread with Laplacian Angular Power Spectrum at MS
Angle of Departure of each path at BS is Gaussian distributed
Angle of Arrival at MS is a Gaussian random variable but also a function of the path power

## Slide 13: Table of Channel Parameters

## Slide 14: Power Distribution Parameter
rDS = (delays/DS)
rAS = (AoD/PAS)
PAS Example: If Powers are assigned completely random in angle,
PAS = AoD so rAS = 1.0
When there is a trend of having stronger powers in the direction of the MS,
PAS < AoD thus rAS > 1.0
PAS = AoD
PAS
AoD
Values for rDS & rAS were selected based on measurements

## Slide 15: Power Delay Profile - Macro
Steps 4,5 - Power Delay Profile (PDP):
  PDP is not deterministic as in ITU models
  N=6 distinct paths are present at any time.
  Generate random delays for each path (exponentially distributed intervals from zero):
  Order delays and shift so as 1st path has zero delay. Quantize delays to 1/16 of chip interval.
  Generate relative powers for each path (exponential profile with shadowing randomization).
Step 6 – AOD Generation per path at BS
  Gaussian random AODs centered on the LOS direction:
  With r = 1.2 (suburban macro), r = 1.3 (urban macro)
Step 7 – PDP to AOD assignments:
  Order AODs in increased absolute value
  Assign path delays (in increasing order)
  to the ordered AODs.

## Slide 16: Special Definitions - Micro
Steps 4,5 - Power Delay Profile (PDP):
  Generate random delays for each path; uniformly distributed:
  Order delays and shift so as 1st path has zero delay. Quantize delays to 1/16 of chip interval.
  Generate relative powers for each path (exponential profile with independent path shadowing).
Step 6 – AOD Generation per path at BS
  Uniformly distributed random AODs centered on the LOS direction:
Step 7 – PDP to AOD assignments:
  No ordering of path AODs

## Slide 17: Path Angle Spread Generation
Step 8 – Per path channel generation at BS
  M=20 sub-paths used for each path, all equal power, unequal angle spacing
    2o per path angle spread for macro
    5o per path angle spread for urban micro
  Sub-path angles precalculated and fixed for all realizations
  Laplacian power azimuth spectrum, random phases.

## Slide 18: Diagram of Spatial Parameters

## Slide 19: Spatial Parameters Defined

## Slide 20: Path AOA Distribution at Mobile
Step 9 – Path Angle of Arrival (AOA) at the MS
  Per path AOA is a Gaussian random variable.
  Path AOA variance decreases with the path’s relative power.
  AoA = 104.12(1-exp(-0.2175*|Pr|)
  Per path AOA:
Measurements
provided
By Motorola
MS Path Angle of Arrival
(dBr)
Strong
Medium
Weak
LOS
LOS + 180o
LOS - 180o
Prob(dBr)

## Slide 21: Path Angle Spread at Mobile
Step 10 – Per path channel generation at MS:
  20 sub-paths used for each path, all equal power, unequal angle spacing
    35o per path angle spread for all scenarios
  Sub-path angles precalculated and fixed for all realizations
  Laplacian power azimuth spectrum, random phases.
Steps 11,12 – Pairing of BS-MS sub-paths, antenna gains.
  Random pairing of sub-paths
  Assign antenna gains for BS and MS

## Slide 22: SCM Generation
The per path channel realization between a Tx-Rx antenna pair is a
superposition of oscillators
  Only one quantity is time evolving.
  All other quantities are fixed for duration of the drop at initialization

## Slide 23: Model for Polarized Antennas
Model defined to allow any type of polarized antennas on the z-plane
by decomposition into vertical & horizontal polarizations
  Power mixing between Vertical (P1) and Horizontal (P2) pols is defined by a discrimination function: XPD=P1/P2
  For urban channels: P2 = P1 - A - B*N(0,1) (B is the St.Dev of XPD) where:
    Urban macro: A=0.34*(mean relative path power)+7.2 dB, and B=5.5dB
    Urban micro: A=8 dB, and B=8dB
  Fast Fading between the two pols is independent
  For each subpath on one pol a corresponding subpath is generated on the other pol with a different initial phase
  The propagation characteristics of V-to-V paths are assumed to be similar to the propagation characteristics of H-to-H paths.
  Example (X-pol transmit, X-pol receive): If BS transmits in X-pol then all path components are decomposed to V and H ones, a mixing is generated, and re-assembled at the Xpol receiver

## Slide 24: SCM Polarized Generation
A matrix describes the amplitude mixing
  Definitions follow the single polarization case ones

## Slide 25: Antenna Patterns
SCM Model allows any mix of antenna patterns in the MS or BS array
Only single polarization antennas defined in SCM
Base Station:
  3-sector and 6-sector antennas defined
  3-sector:
  6 sector:
Mobile:
  Omnidirectional antenna at the X-Y plane at –1 dBi

## Slide 26: Far Scattering Cluster Bad Urban Model
The modified procedure includes:
1. Drop MS within test cell as usual.
2. Drop three FS clusters uniformly across the cell hexagon, with a minimum radius of R = 500m.
3. Choose the FS cluster to use for the mobile that is closest to the mobile.
4. Main cluster is assigned 4 paths, FSC assigned 2 paths
5. Assign Powers, and delays based with the FSC components modified by:
  Excess delay due to path length
  1dB/uS additional attenuation
6. Independent shadow fading per cluster.
50% STS correlation applied
7. Normalize powers of the 6 paths to unity power.
Result:
Angle Spread and Delay Spread is increased as in a bad urban environment

## Slide 27: Line of Sight Model
Applied to Micro-cell
  Probability of occurrence is ~ 15%
  Cost 231 Walfisch-Ikegami for NLOS
    2.0 GHz: 34.53 + 38*log10(d), d in meters
    Log Normal = 10 dB
  Cost 231 Walfisch-Ikegami Street Channeling Model for LOS
    2.0 GHz: 30.18 + 26*log10(d), d in meters
    Log Normal = 4 dB
  Mixing function (Probability of occurrence):
  K-factor for LOS component:
  K = 13.0 – 0.03*d, K in dB, d < 300m
  A direct component is added to first arriving path, normalized with 6 other paths to unity power and ratio K (dB)
Result:
Angle Spread, Delay Spread, and Path Loss statistics affected by LOS component

## Slide 28: Urban Canyon Model No building grid required
Select a random street orientation which equals the direction of UE movement.
Select a random orientation for the subscriber antenna array
If  = U(0,1)<=  Select the UE AoAs for all arriving paths to be equal
If >  Select the directions of arrival for all paths using the standard SCM MS AoA model.
This model emphasizes the case of all paths arriving from a common direction.
Each Path has a AS = 35°, producing this minimum value for 90% of the mobiles.
The remaining 10% of cases represent a mix of other cases, with more random paths.

## Slide 29: Calibration – Output Statistics Micro
Composite Angle Spead at BS and Delay Spead distributions in NLOS and LOS cases of urban micro

## Slide 30: Calibration – Output Statistics Micro (II)
Composite Angle Spread distribution in NLOS and LOS cases of urban micro at the MS
Complementary CDF of resolvable path power in dBr:

## Slide 31: Path Statistics
Number of resolvable paths (fingers) as determined by the finger assignment procedure
Receiver-based finger assignment assumes 1.2288Mcps and root raised cosine filters with roll-off factor beta=0.22
Suburban Macro
Urban Macro

## Slide 32: Path Statistics (II)
Number of resolvable paths (fingers) as determined by the finger assignment procedure
Assumes NLOS case.
Urban Micro

## Slide 33: Evaluation Methodology
Ioc Modeling
  Explicit Spatial modeling of some of the interfering sources.
Channel Metric to FER mappings
  Proposal proponent should provide metric.
  An MMSE space-time receiver can be specified as a reference example design for advanced receivers.
  For most SIMO/MISO schemes the current methodology is sufficient
  For SIMO/MIMO schemes the use of the MMSE receiver offers a reference design
Ray Mapping
  Mapping of SCM paths into fingers for RAKE receivers

## Slide 34: Ioc Modeling
  Sophisticated receivers account for spatial characteristics of signals from interfering bases.
  Need to model the spatial characteristics of “strongest” B bases. (B = 8 for 120 degree sectors, B = 12 for 60 degree sectors.)
  Remaining bases are modeled as spatially white to reduce complexity.
  The impact of the Ioc components depends heavily on the receiver algorithm
  Methodology:
    Determine the pathloss (including antenna patterns) and shadowing of all bases.
    Rank bases in order of received power.
    Assign the strongest base as the serving base.
    Model the next strongest B bases as spatially correlated Gaussian noise processes whose covariances are determined by their channel matrices.
    Model the remaining bases as spatially white Gaussian noise processes whose variances are based on a flat Rayleigh fading process.

## Slide 35: Ray Mapping
Path delays appear at a resolution of 1/16 chip interval
A ray mapping method is needed for RAKE receivers to map the paths into resolvable paths.
The SCM AHG is recommending a finger assignment procedure:
  Determine F number of finger positions common to all receiver antennas.
  Calculate the local maxima of the channel convolution that include the transmit and receive filters. Valid local maxima are only those who satisfy both of the constraints below:
    A local maximum must be within 14dB from the highest local maximum.
    No two consecutive local maxima can be temporally located less than a chip interval apart (i.e. local maxima within a chip interval away from a previously selected maximum are ignored)
  Calculate the power contribution of each of the N paths to each finger assigned.

## Slide 36: SCM Complexity in System Simulations
Initialization:
  Performed once per drop. Stores geometrical, temporal, and spatial variables
  No computational impact in system level simulations
Runtime:
  With M=20 sub-paths per path the number of calculations per Tx-Rx antenna pair and channel sample (e.g. once per slot) are comparable to those in typical channel models
  Complexity increases linearly with the number of Tx - Rx antennas
  Polarization doubles the amount of calculations
  LOS, FSC, Urban Canyon do not impact complexity
  Ioc modeling: modeling the spatial parameters of B sectors per MS multiplies the complexity (factor of B)
  Ray mapping procedure executed per Tx-Rx antenna pair is a linear transformation (minimal impact)
  Overhead from Advanced Receiver (e.g. MMSE) is additional but minor

## Slide 37: Link Level Models
Link Level are considered. Models are a representative set of SCM implementations with fixed parameters.
Link Level models can be used for calibration purposes.

## Slide 38: Link Level SCM Calibration (1)

## Slide 39: Link Level SCM Calibration (2)

## Slide 40: Summary
The SCM recommendation is a comprehensive system level framework for evaluation of multiple antenna techniques.
The MBWA has already adopted most of the SCM modeling principles and has also extended the specification for additional (indoor) environments