## Slide 1
 | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | 802.20 Evaluation Criteria Document Issues | 
Date Submitted | 2004-11-15 | 
Source(s) | Arak Sutivong, Qualcomm, Incorporated 5775 Morehouse Drive San Diego, CA, 92121 Jim Tomcik, Qualcomm, Incorporated 5775 Morehouse Drive San Diego, CA, 92121 Rajat Prakash , Qualcomm, Incorporated 5775 Morehouse Drive San Diego, CA, 92121 Gwen Barriac, Qualcomm, Incorporated 5775 Morehouse Drive San Diego, CA, 92121 | Voice: 858-651-6957 Fax: 858-845-2651 Email: araks@qualcomm.com Voice: 858-658-3231 Fax: 858-658-5006 Email: jtomcik@qualcomm.com Voice: 858-845-1350 Fax: Email: rprakash@qualcomm.com Voice: 858-651-4990 Fax: Email: gbarriac@qualcomm.com
Re: | MBWA Call for Contributions | 
Abstract | Between the September and Novembers meetings of 802.20, the authors reviewed the 802.20 Evaluation Criteria document, and concluded that there are significant areas where more detail is required in order to develop a full technology evaluation. This contribution provides inputs to 802.20 on additional areas not fully covered in the Evaluation Criteria document, and some suggested text for inclusion. Areas cited are generally in the area of system simulation methodology, although a few miscellaneous areas for modeling are also suggested. | 
Purpose | To provide input to the Evaluation Criteria document. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: Evaluation Criteria Document Issues
Jim Tomcik, Rajat Prakash, Gwen Barriac,
Arak Sutivong

## Slide 3: Agenda
Traffic Models and Mixes
Simulation Methodology
Phase 1 vs. Phase 2
Performance Metrics
Control/Signaling Modeling
Mobility Support

## Slide 4: Traffic Models (1)
Several “applications” were discussed in the document
  FTP, HTTP, gaming, streaming, IM, MM, PDA synch, VoIP, etc.
Some are redundant, while others lack models
Proposal:
  Keep only those that highlight different aspects of system performance
    Full-buffer best effort  throughput
    Video, gaming, and other real-time traffic  latency
    HTTP  most common user’s experience
  Consolidate applications and associate them with appropriate models

## Slide 5: Traffic Models (2)
Application | Traffic Category | Model Availability
Full-buffer | Best-effort | Yes
VoIP | Real-time | N/A
HTTP (Web Browsing, WAP) | Interactive | Yes
Gaming (IM, MM) | Interactive | N/A (see Nov 04 contribution)
Streaming (Video, Audio) | Streaming | Yes
FTP (Email, file-sharing, PDA synch) | Best-effort | Yes

## Slide 6: Traffic Mixes
Current methodology calls for mixing of 15 applications!
  Difficult to decide on the right mix
  Not clear what we’ll get out of this
Simple traffic mixes  Better insights on system performance
Proposal:
  Individual traffic: full-buffer best-effort, gaming, HTTP, and streaming
  Gaming + Full-buffer
  HTTP + Full-buffer
  Video/Audio streaming + Full-buffer

## Slide 7: System Simulation Methodology
Current text is ambiguous and incomplete
Proposal: Refer to accompanying text

## Slide 8: Phase 1 Simulation Scope
Current scope:
  Basic calibration
  Full-buffer best-effort traffic only
Captures the “essence” of the proposal, but only from throughput standpoint
Should expand the scope to also capture latency performance
Proposal:
  Full-buffer best-effort
  Gaming
  Gaming + full-buffer best-effort

## Slide 9: Phase 2 Simulation Scope (1)
Comprehensive performance comparisons
Key metrics of interest for different traffic mixes
  Full-buffer best-effort only
    Metrics: Spectral efficiency (S.E.) and latency (subject to specified fairness)
  Gaming + Full-buffer
    Metrics: # Gaming users @ a given outage vs. S.E. of full-buffer traffic
  HTTP + Full-buffer
    Metrics: # HTTP users vs. spectral efficiency of full-buffer traffic
  Video/Audio streaming + Full-buffer
    Metrics: # Video streams vs. S.E. of full-buffer traffic

## Slide 10: Phase 2 Simulation Scope (2)
Other key metrics should include
  Number of simultaneous active users
    Requirement is given in the SRD
    How do we capture this?
  Access latency
    Mobile-initiated
    Network-initiated (i.e., paging)
  Control/Signaling
    Modeling
    Impact of control/signaling error
  Mobility support

## Slide 11: Feedback Errors
Proponents should model feedback errors; e.g.,
  Power Control
  Acknowledgements
  Channel Quality Indicator
  Channel assignments (if applicable)
  Rate indication etc.
Disclose feedback error rate average & distribution
Also disclose measurement error model & necessary parameters

## Slide 12: Mobility and Signaling Use Cases
Signaling for mobility management
Handoff design consideration
  Statistics of dead time on uplink and downlink in case of handoff
  Probability of missed pages due to handoff
Power consumption
  Duty cycle for receiver ON time

## Slide 13: Example: Connected State Handoff
The following events are part of handoff:
  T_Report_Trigger: Time taken by AT to trigger a PilotReport
  T_Transmit_Report: Time taken for report to reach AP
  T_Handoff_Direction: Time taken for handoff direction to reach AT
Dead time is incurred if handoff direction message is delayed
Exact sequence of operation may depend on system design

## Slide 14: Simulation Approaches
Full Mobility
  All users in the simulation are mobile, and perform signaling according to the event
  This may be too complex to implement
Single user mobility
  All users except one are fixed. The one mobile user moves according to a simple mobility model
  Reduced simulation time
C/I based model
  From conventional system sim, obtain performance vs C/I curves
  Simulate signaling events by considering the motion of one user and calculating the C/I at each point along the path

## Slide 15: Simple Model for Mobility
Two cells, A and B
Mobility models
  Model 1: Move from A to B along line joining the cells
  Model 2: Move from A to B with “around the corner” effect
    Rapid signal loss from A, signal gain to B. (built into propagation)
  Model 3: Move along cell edge

## Slide 16: Shadow Fading and Mobility
Path 1
Path 2

## Slide 17: Shadow Fading and Mobility - II
These models are representative of handoff scenarios
  Model 2 is the most stringent test (fast rising pilot scenario as the terminal enters an intersection)
  Models 1 and 3 are more likely and less stringent
Path 3

## Slide 18: Performance Metrics
Duration of frame loss during handoff
Probability of missed page during handoff
Power-save state power consumption (or ON duty cycle)
Plot metrics as a function of
  Mobile velocity
  Cell loading (in the system sim)