## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | Gaming Models for Evaluation Criteria | 
Date Submitted | 2004-11-15 | 
Source(s) | Jim Tomcik Qualcomm, Incorporated 5775 Morehouse Drive San Diego, CA, 92121 | Voice: 858-658-3231 Fax: 858-658-2113 Email: jtomcik@qualcomm.com
Re: | MBWA Call for Contributions | 
Abstract | IP-based gaming is likely to be an important application for the future 802.20 standard. Furthermore, gaming provides a simple model of a truly interactive application and as such can be used in 802.20 technology evaluation as a key traffic source. The author has taken an assignment to contribute (a) a survey of gaming models that may be of interest to the 802.20 group and (b), some suggested text for the 802.20 evaluation criteria document that encompasses this important traffic type. This contribution provides an update on gaming models, and proposes additional text for the 802.20 Evaluation Criteria document in this area. | 
Purpose | To provide a basis for developing models, and evaluation criteria for gaming-driven traffic in 802.20. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: Gaming Models for 802.20
Jim Tomcik
jtomcik@qualcomm.com

## Slide 3: Gaming Traffic on the Internet
Network Gaming is generating significant internet traffic today
  According to McCreary [2000] 3-4% of all internet backbone traffic is associated with 6 popular games!!
Continuing deployment of cable modem, DSL technology, etc makes gaming very accessible to today’s household!!
Gaming Traffic can stress a system to deliver the types of performance required for gamer success!
Gaming scenarios should be part of the evaluation criteria for a new wireless technology such as 802.20!

## Slide 4: Classes of Networked Games
First Person Shooting (FPS) Games
  Players “inhabit” the characters
  Games Take Place inside a “maze” of rooms
  Fights/matches between characters determine who survives
  Most have a timed-out “resurrection” for characters who have lost a match
  Examples: Quake, Quake 2, “Counter Strike”
Third Person Shooting (TPS) Games
  Players control characters from a “distance”
  Typical of many early video games (Super Mario Brothers, e.g.)
  Fights/Matches tend to be between either characters or between a character and a system-supplied “villian”
  Game Ends for Characters who lose
Strategy Games
  Players may control teams of characters such as “armies”
  Real Time fights/matches are not as important as overall strategy
  Games can take hours or days

## Slide 5: FPS Game Requirements
FPS Games
  Very Interactive – requires minimal delay
    ‘LAG” Players’ success depends on minimal delays
      Network
      Graphics Rendering
    Somewhat Packet Loss Sensitive
  How Interactive??
    Ping time <50ms -> Excellent game play results
    Ping time <100ms -> Good game play results
    Ping time > 100 ms -> Playability degrades noticeably
    Ping time >150 ms -> Often reported as intolerable, but
      Many players claim to have no trouble with ping times around 200 ms (?)
    (See Henderson, http://www.cs.ucl.ac.uk/staff/T.Henderson/docs.html “Latency and User Behavior on a mjultiplayer games server”)

## Slide 6: Gaming Architectures
Most Network Games use a “Client/Server” model
Server Location:
  Many internet game servers
  Newer Peer to Peer games locate servers on one player’s machine
For 802.20 I recommend the internet-located server architecture since it is more prevalent

## Slide 7: Typical Long Term Traffic Profiles
Server Transmit Cycle:
  Server maintains global state
  Server transmits state information in bursts
  Scenario changes result in reduced traffic
Client Transmit Cycle
  Synchronize local state with received info and render display
  Transmit “update” packets with movement and status information
Source: Farber, 2002

## Slide 8: Client-Side Traffic Measurements
Source: Farber, 2002
Experiment Shows 8 of 27 networked clients
Characterized by nearly constant packet size
Inter-arrival times >1 sec are removed to capture active play
Long-tailed behavior – caused by several interarrivals in the 600-800msec range
Note client behaviors differ, but within a range
Long-tailed behavior contributed by several packets with 200-300 bytes

## Slide 9: Server-Side Traffic Measurements
Source: Farber, 2002
Experiment Shows 8 of 27 networked clients
Characterized by bursts of packets
Long-tailed behavior – caused by several interarrivals in the 600-800msec range
Note client behaviors differ, but within a range
Long-tailed length behavior contributed by several packets with 200-300 bytes

## Slide 10: The Extreme Value Distribution
Both Borella[2000] and Farber[2002] suggest the “Extreme Value Distribution” to model tail-heavy traffic observed.
Borella further examines a “goodness of fit” criterion and shows that this is a very good fit
Farber agrees with this result.

## Slide 11: The Extreme Value Distribution
CDF:
Parameters: a: Correlated to the Mode of the Distribution
b: Correlated to the Variance of the Distribution
PDF:

## Slide 12: Suggested Parameters
Source: Farber, 2002
Borella advocates and Farber accepts using a Maximum Likelihood Estimator to Fit the Observed Data to the Extreme Value Distribution. See Borella for further information.
Borella goes a step further and defines/examines at a “Discrepancy Measure”

## Slide 13: Qualcomm Experiments
Game Title: FIFA Soccer 2002
Reverse link traffic ~ 3.5kbps
Forward link traffic ~ 3.8kbps
Traffic in both directions are similar in arrival rates and inter-arrival distributions
Inter-arrival times are mostly < 180ms.
Packet size distributions are a little different

## Slide 14: A Few More Observations
Most of the time the packets alternate in directions
From time to time, one side will send two (or three) packets after the other side sends one.
  When that happens, the time between the two (or three) packets from the same side are between 10 to 60ms
  This supports the burst-like observations in Borella, and Farber

## Slide 15: 3GPP2 Evaluation Model
Version: C30-2004-0719-034 C.P1002
Document Contains a RL Model
  This is only because of timing – proposed for cdma2000 rev D which was RL focused
Actual Parameters Differ from Published although they are “similar”

## Slide 16: 3GPP2 Text Review

## Slide 17: 3GPP Evaluation Model
3GPP Used a different Model from 3GPP2
Major Characteristics:
  Exponential Distributions for “Call Duration and “Reading Time”
  Log Normal Distribution for Datagram Arrival Times
  Formal “Call” Arrival Process with “Packet Arrival Process” contained
  “Closed Loop” model includes both FL and RL

## Slide 18: 3GPP Text Review

## Slide 19: 802.20 Gaming Model Options
802.20 Evaluation should include both UL and DL traffic models for wireless gaming
  Should they somehow be “linked”??
Option 1: Modify the 3GPP2 Model, to include downlink characteristics as in Farber[2002]
Option 2: Adopt or modify the 3GPP Model
Option 3: Combine the best of the two models
Option 4: Develop an 802.20 model based on more recent literature

## Slide 20: References
S. McCreary, “Trends in Wide Area IP Traffic Patterns – A View from Ames Internet Exchange”, ITC Spec. Seminar, 2000.
Michael S. Borella, “Source Models of Network Game Traffic”, Networld+Interop ’99 Engineer’s Conference, May, 1999
Johannes Farber, “Network Game Traffic Modelling”, NetGames2002, April 16-17, 2002, Braunschweig, Germany.
3GPP, “Feasibility Study for Enhanced Uplink for UTRA FDD” TR 25.896 V. 6.0.0, March 2003
3GPP2, “cdma2000 Evaluation Methodology, Revision 0”, C.P1002, version 0.3, July 23, 2004.

## Slide 21: Discussion Area