## Slide 2: Evaluation of VoIP application
Summary of previous 802.20 contributions on VoIP models
Review candidate vocoder characteristics
  Variable rate: EVRC
  Fixed rate: ITU-T G.729 B
Markov models
IP stack model
Network effects model
QoS metrics and performance
Conclusion
List of References

## Slide 3: Summary of Earlier Discussions on VoIP Traffic Model
Most recent contribution: 04/37
  Described Framework of VoIP model
    Voice source model
    IP stack model
    Network effects model
    End-to-end control model
  Reviewed Vocoder standards
    EVRC (TIA / EIA / IS-127)
    ITU G.729/A (DTX - Voice Activity Detection)
Earlier contribution: 04/12
  Discussed protocol overhead – TCP, UDP, RTP, PHY and MAC headers
  Discussed voice activity detection
  Techniques for improving capacity
    Header compression
    Frame aggregation
  Performance metrics and requirements
    Packet lost ratio
    Latency
    Delay jitter

## Slide 4: Voice Source Model
Choose Vocoder standard used in current and foreseeable future
Candidate vocoder standards
  EVRC
  ITU-T G.729 A, B
  ITU-T G.723.1 A
  Others
EVRC Vocoder standard
  TIA / EIA / IS-127
  Used in 3G technology (CDMA 2000)
  Variable data rates:
    Full Rate: 8.6 kbps
    Half Rate: 4.3 kbps
    1/8th Rate: 1.0 kbps (Background noise)
    Depend on average Vocoder input signal energy level
    Multiple thresholds used to determine data rate based on detected energy level

## Slide 5: Markov Model for Variable Rate Source Coder [IS-871]

## Slide 6: Markov Model for Variable Rate Source Coder [IS-871]
State transition probabilities defined in IS-871:
  “Markov Service Options for CDMA 2000 spread spectrum system”
Model has been used by 1xEV-DV evaluation methodology:
  Voice activity factor: 0.403
  Full rate (R-1): 29%
  Half rate (R-1/2): 4%
  Quarter rate (R-1/4): 7%
  One-eighth rate (R-1/8): 60%

## Slide 7: Fixed Rate Speech Coding Standard ITU-T G.729 - Silence Compression Scheme [Annex B]
ITU-T G.729 (CS-ACELP)
  8 kbps
  10 ms frame
ITU-T G.729 A
  Reduced complexity 8 kbps CS-ACELP speech codec
ITU-T G.729 Annex B (Silence compression scheme for G.729)
  Voice Activity Detection
  Discontinuous Transmission feature (DTX)
  Use a threshold to determine voice activity based on detected average energy level
  Two states:-
    8 kbps
    0 kbps (no transmission when inactive)
  Receiver detects DTX state to determine if:
    Active: Decode speech data
    Inactive: Generate comfort noise locally based on information on background noise level

## Slide 8: Markov Model for Fixed Rate Source Coder with Voice Activity Detection (DTX) [ITU-T G.729B]
Specify values for transition probabilities:
  P(A|I)
  P(I|A)
Assume similar Voice activity factor of 0.4
  P(A|I) ~ 0.4
  P(I|A) ~ 0.6

## Slide 9: IP Stack model
Protocol used for VoIP
  UDP
  RTP
  Evaluation criteria document does not have UDP, RTP model
    Not really necessary except to account for the overhead
Specify Header size [2]
  RTP ~ 12 bytes
  UDP ~ 8 bytes
  IP ~ 20 bytes
  RTP + UDP + IP ~ 40 bytes
Protocol header compression
  Should working group decide if header compression needs to be used in the evaluation?
  If used, what should be the compression ratio?
    20:1 bytes ? [2]
PHY/MAC headers are proposal dependent
  Proponents to specify the required header size

## Slide 10: Network Effects model
Network delay model defined in 802.20 evaluation criteria document V.12
Network delay distribution
  Shifted Gamma distribution
  Parameters specified in Table 8 of Section 5.3.1
Network packet loss
  Specified in Section 5.3.2
  Assumption: 0%
  Focus of evaluation is on the PHY and MAC layer technology
  In comparison, the network packet loss rate is negligible assuming no congestion

## Slide 11: QoS metrics for Telephony Applications
Transmission rating factor R-Value
  Described in ITU-T G.175
  Calculated using the E-model
    Relative measurement with respect to a reference condition
  Trend in transmission planning
  Value range from 0 – 100 (Very high quality)
  Ro ~ Basic signal-to-noise ratio
  Is: combination of all impairments ~ simultaneous with voice
  Id: impairment caused by delay
  Ie: Equipment impairment factor ~ caused by low bit rate codecs
  A: advantage factor ~ compensation of impairments in the presence of advantages
  Other quality measurement metrics can be computed from the R-values
    Mean Opinion Score (MOS)
    Percentage of Good or Bad (GoB%)
    Percentage of Poor or Worst (PoW%)

## Slide 12: QoS performance measurement – Subjective vs Objective
R-value lower limit | MOS | Speech Transmission Quality Category | User Satisfaction
90 | 4.34 | Best | Very satisfied
80 | 4.03 | High | Satisfied
70 | 3.60 | Medium | Some users dissatisfied
60 | 3.10 | Low | Many users dissatisfied
50 | 2.58 | Poor | Nearly all users dissatisfied
Sources:
  TIA / EIA / IS-810-A
  ITU-T G.175

## Slide 13: QoS Performance: R-value vs One-way Network Delay
G.729A: 8 kbps, 10ms frame, Voice Activity Detection (VAD)
“Many Users dissatisfied” when:
  Packet loss > ~ 2% (2 speech frames/packet)
  One-way Network Delay > ~180 ms (when packet loss = 0%)
Source: TIA / EIA / IS-810-A

## Slide 14: How about G.723.1 A ?
G.723.1 A: 6.3 kbps, 30 ms frame, Voice activity detection (VAD)
“Many Users dissatisfied” when:
  Packet loss > ~ 1% (1 speech frame/packet)
  One-way Network Delay > 110 ms (when packet loss = 0%)
Source: TIA / EIA / IS-810A

## Slide 15: Conclusion
ITU-T G.729 A,B
  Tolerates relatively higher packet loss and longer network delay than G.723.1A
    G.729 A,B can be chosen over G.723.1 A
  Need to decide on the state transition probabilities
EVRC
  Supports variable rate including voice activity detection
  Larger number of Markov states as a result of multiple source data rate
  Model for state transit described in detail in IS-871
  Used in current CDMA 2000 standard
  What is the R-value performance characteristics, as compared to G.729 A,B ?
Need to choose a vocoder for technology evaluation
  G.729 A, B?
  EVRC?
  Another vocoder standard?
Need to determine performance metrics for evaluation
  Somewhat dependent on the choice of vocoder standard for evaluation
  Packet loss ratio
  Latency
  Delay Jitter

## Slide 16: List of References
J. Tomcik, “VoIP Models-Update”, IEEE C802.20-04/37, May 2004.
F. Khan, “VoIP Models for 802.20 System Performance Evaluation”, IEEE 802.20-04/12, Jan 2004.
TIA/EIA, “Transmission requirements for Narrowband Voice over IP and Voice over PCM Digital Wireline Telephones”, TIA/EIA-810-A, Dec 10, 2000.
TIA/3GPP2, “Enhanced Variable Rate Codec, Speech Service Option 3 for Wideband Spread Spectrum Digital Systems”, TIA-127A, May 2004.
3GPP2, “Markov Service Option (MSO) for cdma2000 Spread Spectrum Systems”, IS-871, April 2001.
ITU-T, “Coding of speech at 8 kb/s using Conjugate-Structure Algebraic-code-Excited Linear-Prediction (CS-ACELP)”, G.729, March 1996.
  Annex A: Reduced complexity 8 kb/s CS-ACELP speech codec, Nov, 1996
  Annex B: A Silence compression scheme for G.729 optimized for terminals conforming to Recommendation V.70, Nov 1996.
ITU-T, “Transmission planning for private/public network interconnection of voice traffic”, G. 175, March 1997.
“IEEE 802.20 Evaluation criteria document Ver. 12”, November 2004.