## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | Update on Gaming Models for Evaluation Criteria | 
Date Submitted | 2005-01-18 | 
Source(s) | Jim Tomcik Qualcomm, Incorporated 5775 Morehouse Drive San Diego, CA, 92121 | Voice: 858-658-3231 Fax: 858-658-2113 Email: jtomcik@qualcomm.com
Re: | MBWA Call for Contributions | 
Abstract | C802.20-04/86 was presented at the November 2004 meeting of 802.20 and at a subsequent conference call on January 11, 2005. This contribution summarizes a few issues that were raised and offers additional material on traffic models for networked games. | 
Purpose | To provide a basis for developing models, and evaluation criteria for gaming-driven traffic in 802.20. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: Gaming Models Update
Jim Tomcik
jtomcik@qualcomm.com

## Slide 3: Classes of Networked Games
First Person Shooting (FPS) Games
  Players “inhabit” the characters
  Games Take Place inside a “maze” of rooms
  Fights/matches between characters determine who survives
  Most have a timed-out “resurrection” for characters who have lost a match
  Examples: Quake, Quake 2, “Counter Strike”
Third Person Shooting (TPS) Games
  Players control characters from a “distance”
  Typical of many early video games (Super Mario Brothers, e.g.)
  Fights/Matches tend to be between either characters or between a character and a system-supplied “villian”
  Game Ends for Characters who lose
Strategy Games
  Players may control teams of characters such as “armies”
  Real Time fights/matches are not as important as overall strategy
  Games can take hours or days

## Slide 4: FPS Game Requirements
FPS Games
  Very Interactive – requires minimal delay
    ‘LAG” Players’ success depends on minimal delays
      Network
      Graphics Rendering
    Somewhat Packet Loss Sensitive
  How Interactive??
    Ping time <50ms -> Excellent game play results
    Ping time <100ms -> Good game play results
    Ping time > 100 ms -> Playability degrades noticeably
    Ping time >150 ms -> Often reported as intolerable, but
      Many players claim to have no trouble with ping times around 200 ms (?)
    (See Henderson, http://www.cs.ucl.ac.uk/staff/T.Henderson/docs.html “Latency and User Behavior on a mjultiplayer games server”)

## Slide 5: 802.20 Gaming Model Options (from November)
802.20 Evaluation should include both UL and DL traffic models for wireless gaming
  Should they somehow be “linked”??
Option 1: Modify the 3GPP2 Model, to include downlink characteristics as in Farber[2002]
Option 2: Adopt or modify the 3GPP Model
Option 3: Combine the best of the two models
Option 4: Develop an 802.20 model based on more recent literature

## Slide 6: Assignments
Reference [1] in 3GPP Model document:
  “Source Models of Network Game Traffic", M. S. Borella, Proceedings, Networld+Interop '99 Engineer's Conference, May 1999.
Gaming Model History: this was not tracked by Qualcomm in 3GPP. No further information about why the quantities were modified.

## Slide 7: Additional Materials!
ACM sponsors a yearly workshop on networked games (Netgames)
Downloaded Papers from the following:
  Netgames ’02 – Braunschweig, Germany
  Netgames ’03 - Redwood City, CA
  Netgames ’04 – Portland, OR
Available through ACM or your local Technical Library

## Slide 8: Literature Search Results
Assessing User Experience: This is the Bulk of Materials
Borella, as well as Farber are quoted extensively, and have not been corrected or contradicted in any resulst.
Objective and Subjective Evaluation of the Influence of Small Amounts of Delay and Jitter on a Recent FPS Game ( “Unreal Tournament ’03”) – from Netgames 2004.
  Methodology: Emulate Delay with A Programmable Router
  Delay Impairment Negatively Affects Players’ Scores
  One Player’s Impairment Does Not Affect Other Players
  Players’ Perceptions of the Game are Tied to Delay Performance
G. Armitage – discusses similar considerations
  Issues in Emulating Jitter via FreeBSD
Sheldon, et al. “The Effect of Latency on User Performance in Warcraft III”
  This is for a “Real Time Strategy” game, so not as relevant.

## Slide 9: Summary Conclusions
The Study of Networked Games is becoming more established in the literature.
  NetGames – yearly workshop
Many of the results assess User Experience and Implementation Issues
Borella, and Farber are widely quoted, underlining their continuing relevancy today.
802.20 may do best to modify the 3GPP2 traffic model to include both Forward and Reverse Link traffic, in accordance with Farber.
ACM SigCOMM 2005 – August, 2005, Philadelphia