## Slide 2
Conference call summaries
Major open issues
  Open issues in Traffic models
  Other open issues addressed by contributions
  Other open issues not addressed by contributions
Open issues with options/text included in Evaluation criteria document V.14
Other updates in EC V.14
Phase 1 simulation methodology
Phase 2 simulation methodology
Fairness/QoS criteria

## Slide 3: Summary of Conference Call – Feb 8
Reviewed contribution C802.20-05-04r3 to recap the status of evaluation criteria document
Sections in Evaluation criteria document (EC) V.13 updated during January's Interim meeting
  section 3.2: Performance metrics for throughput vs SINR modified [04/88];
  section 4.3.8: Video source data rate changed to 64 kbps [04/88,05/11]
    New open issue on the size of video buffer
  section 4.1: 4 options listed for channel models mix [04/82r1];
Reviewed contribution 04/83r3a on system level simulator calibration
  Merge of contribution 04/83r2 and 05/07r1
  List of issues identified in the call:
    Fixed user locations need to be specified
    Clarify plots of C/I data
    Should MIMO channel models be considered in the calibration as well?
    Clarify the footnote on: "channel inversion power control";
    Minimum user distance from BS needs to be consistent with the channel models document
    Clarifications on technology and link budget assumptions
    Specify success criteria of the calibration

## Slide 4: Issues Discussed in Conference Call (CC) – Feb 22
Discussed contribution on the open issue as related to link budget
  New text proposed for clarification of link budget template in section 11
  New subsection under “Output metrics” proposed to evaluate maximum range and data rate at the cell edge
  Disagreement on the new output metrics for evaluation
  Alternative text proposed via email reflector after the CC
    Use of link budget template to provide information on simulation assumptions only
  Further discussion in the following CC
Reviewed contribution 04/83r3b on system-level calibration
  An update to address issues identified in the previous CC
  Major remaining open issues:
    Specific locations for fixed users
    Clarification on the success criteria
Plan for the following CC & meeting session #13
  Review evaluation criteria document for all remaining open issues
  Adopt proposed text from the contributions based on consensus during the CC

## Slide 5: Summary of Conference Call – Mar 8, 05
Conclude discussion on link budget
  Contribution revised with the alternative text as option 2
  Original proposed text modified as option 3
    New output metric: maximum range for a fixed data rate based on WG consensus
  Participants agreed to include all 3 options in EC V.14
Conclude discussion on system-level calibration
  Minor changes necessary to clarify the distribution of user locations
  Participants agreed to adopt the proposed text into EC V.14
Review evaluation criteria document V.13r1
  Proposed text for section 1.2, 2 and 3 to be included
  Options for Internet gaming model to be included
  Other updates that may be included in V.14 discussed
  Identified sections that require additional clarification text
  Inconsistency still exist between a few sections in the document

## Slide 6: Major Open Issues
Receiver Noise model (section 3.3/3.4)
Simulation flow description (section 5.1/5.2)
Reverse link model (section 5.5.2)
VoIP model (section 4.3.5)
Internet Gaming model (section 4.3.9)
  Text available for one of the proposed options
Traffic model mix (section 4.4)
Handoff simulation model (section 5.4/5.5) – option 2 in 05/10r2 adopted in March meeting, need to modify as per members’ comments
Fairness criteria/QoS criteria for various applications to be evaluated as in Table 11 for phase 2 evaluation (section 15):
  VoIP
  Internet Gaming
  Video Streaming
  Web Browsing
  Broadcast/Multicast (model: not in the evaluation criteria document)

## Slide 7: Open Issues on Traffic Models
Traffic models
  VoIP model
    Related contributions: 04/12, 04/37, 05/05, 05/23
    Complete, specific model TBD
  Internet gaming model
    Contribution 04/86, 05/06
    4 options proposed in 04/86
    Specific text for option 2 proposed in 05/06
  Traffic model mix
    Entries in Table 5 for the percentage mix remain open
    Consistency between Table 5 and 11, for phase 2 traffic types
    Contribution 04/85r1 proposed traffic model mix
      Not including all traffic types to be evaluated in Phase 2
  Multicast/Broadcast
    One of the traffic types to be evaluated in phase 2 based on Table 11
    No model has been discussed

## Slide 8: Other open issues addressed by contributions
Receiver Noise model
  Contribution C802.20-04/89r1 discussed in January
  Need agreement to include or refine proposed text
Simulation flow description
  Contribution C802.20-04/85r1
Output metrics
  Contribution C802.20-04/85r1
Forward link overhead channel
  Contribution C802.20-04/85r1
Reverse link model / signaling error
  Contribution C802.20-04/85r1
Handoff simulation
  Initial contribution C802.20-04/85
  Update contribution C802.20-05/10r1, 10r2
=> Need agreement to include or refine proposed text

## Slide 9: Other open issues addressed by new contributions1
Fairness criteria/QoS criteria for various traffic types to be evaluated as shown in Table 11 for phase 2 evaluation:
  VoIP (05/22)
  Internet Gaming (05/20, 05/22)
  Video Streaming (05/22)
  Web Browsing (05/22)
  Broadcast/Multicast
  Any other additional traffic types based on the resolution of “TBD”s in the Table
1: meeting session #13, March 2005.

## Slide 10: Open Issues with options / text included in Evaluation Criteria Document V.14r1
System level Calibration
  Proposed text included to address open issues in sections 6.1.2 and 8
  Based on latest version of the contribution 04/83r5
Channel model mix
  Proposed options from contribution 04/82r1 included in V.13 during Interim meeting in January
  Dependent on resolution in channel models document
Link Budget
  3 options included in V.14r1 to clarify section 11
  Option 1 & 3 include a new subsection: 13.2 with additional output metric for cell edge performance
Internet gaming model
  4 options from contribution 04/86 included
  Text for option 2 adopted from contribution 05/06

## Slide 11: Other Updates included in EC V.14r1
Alternative texts for sections 1.2, 2 and 3
Most changes from Berlin accepted
Updates to description text in section 4.3.10: Full buffers model
Updates to text in section 4.4: Traffic mix (Table 1: TBD)
Clarification for: (to be revised)
  Section 5.1.1: Distribution of users
  Section 5.1.2: User usage model
Section 12.3: Deployment characteristics
  Further description text required for clarification
Section 13.1.4: Computing of spectral efficiency
  New text included for consistency with system requirements document
Alternative text for section 14.1: Capacity performance evaluation criteria
Section 16: Simulation and evaluation of various block assignments
  New text added to clarify the case of unpaired block assignments

## Slide 12: Phase 1 Simulation Methodology
Full-Duplex, 19-cells, 3-sectors/cell wrap around configuration
Traffic Type
  Full-buffer (Hungry user; infinite backlog) model
Channel model
  Suburban Macro
  Pedestrian B, 3 km/h, all users
  Vehicular B, 120 km/h, all users
Progress on open issues:
  System Calibration – further revision
    Revised contribution adopted into EC V.14r1
  Link Budget – WG accepted modified text, with data rates for each test environment TBD
    Revised contribution with 3 options included into EC V.14r1
  Performance metrics / output metrics
    Consensus on Section 3.2 achieved during Interim meeting in January
    Additional system-level performance metrics (C802.20-04/85r1)
  Receiver noise model
    Need to achieve consensus on the proposed or refine text in Contribution 04/89r1
  Simulation flow
    Proposed text in Contribution 04/85r1 need to be reviewed for adoption into EC
  Reverse link simulation model
    Modeling of feedback / reverse link signaling errors discussed in Contribution 04/85r1
    Need further discussion or appropriate text for EC

## Slide 13: Phase 2 Simulation Methodology - Configurations
Full Duplex, 19-cells, 3-sectors/cell wrap around configuration
Traffic Types - as listed in Table 11 in the evaluation criteria document
  VoIP (RTP)
    Model to be specified (proposed options for model: 05/23)
  Web Browsing (TCP)
  File Transfer (FTP)
  Internet Gaming (TCP)
    4 options, but only one with detail text
  Video Streaming (RTP)
    Buffer size to be determined
  Broadcast/Multicast (RTP/UDP)
    Model not specified
  Other traffic types in the Table are “TBD”
  Percentage mix not specified

## Slide 14: Phase 2 Simulation Methodology - Details
Channel models
  Depending on adopted 802.20 Channel models
Updated text in contribution adopted in March meeting [05/10r2]
  Handoff simulation model [05/08, 05/10r1]
  Handoff performance metrics [05/10r1]
Open issues that required further discussion:
  Reverse link / Control signaling model [04/85r1]
Open issues that require further work on new contribution 05/22r1:
  Fairness / QoS criteria for various applications for phase 2 evaluation

## Slide 15: Fairness / QoS Criteria
Fairness criteria for applications other than the best effort traffic need to be specified
  Phase approach table listed various applications to be evaluated:
    Real-time Interactive traffic (VoIP, gaming)
    Streaming traffic (Video streaming)
    Non-real-time data traffic (HTTP)
  Performance criteria not yet specified
    QoS performance – Delay, Error Rate [VoIP: 05/05]
    Outage criteria
What would be the performance criteria for each traffic type to ensure that the spectral efficiency is computed based on system resources being shared fairly amongst the simulated users in the same sector?
Contributions are required if additional metrics are to be adopted