## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | QoS for Evaluation Criteria Gaming Models | 
Date Submitted | 2005-03-16 | 
Source(s) | Jim Tomcik Qualcomm, Incorporated 5775 Morehouse Drive San Diego, CA, 92121 | Voice: 858-658-3231 Fax: 858-658-2113 Email: jtomcik@qualcomm.com
Re: | MBWA Call for Contributions | 
Abstract | IP-based gaming is likely to be an important application for the future 802.20 standard. Furthermore, gaming provides a simple model of a truly interactive application and as such can be used in 802.20 technology evaluation as a key traffic source. This contribution further addresses the issues of providing adequate Quality of Service to support internet gaming (in the form of first person shooter games) properly. A short piece of text is also proposed for the evaluation criteria document. | 
Purpose | To provide a basis for developing models, and evaluation criteria for gaming-driven traffic in 802.20. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: QoS for Evaluation Criteria Gaming Models
Jim Tomcik
jtomcik@qualcomm.com

## Slide 3: Classes of Networked Games
First Person Shooting (FPS) Games
  Players “inhabit” the characters
  Games Take Place inside a “maze” of rooms
  Fights/matches between characters determine who survives
  Most have a timed-out “resurrection” for characters who have lost a match
  Examples: Quake, Quake 2, “Counter Strike”
Third Person Shooting (TPS) Games
  Players control characters from a “distance”
  Typical of many early video games (Super Mario Brothers, e.g.)
  Fights/Matches tend to be between either characters or between a character and a system-supplied “villian”
  Game Ends for Characters who lose
Strategy Games
  Players may control teams of characters such as “armies”
  Real Time fights/matches are not as important as overall strategy
  Games can take hours or days

## Slide 4: FPS Game Requirements
FPS Games
  Very Interactive – requires minimal delay/latency/jitter
    ‘LAG” Players’ success depends on minimal delays
      Network
      Graphics Rendering
    Somewhat Packet Loss Sensitive
  How Interactive??
    Ping time <50ms -> Excellent game play results
    Ping time <100ms -> Good game play results
    Ping time > 100 ms -> Playability degrades noticeably
    Ping time >150 ms -> Often reported as intolerable, but
      Many players claim to have no trouble with ping times around 200 ms (?)
    (See Henderson, http://www.cs.ucl.ac.uk/staff/T.Henderson/docs.html “Latency and User Behavior on a multiplayer games server”)

## Slide 5: A Recent QoS Study
Beigbeiter et al. (Worcester Poly) Published Laboratory results
  Game: “Unreal Tournament 2003”
    Game type is a First Person Shooter
  Deliberately induced packet loss and delay to study user experience
Measured Player’s Ability to:
  Move his avatar around the board
  Aim and shoot precisely
  Also measured several other aspects of gaming
  Most significant are the “precision shooting” results

## Slide 6: Laboratory Setup
Simple lab setup to illustrate effects of delay and loss
NIST Net Router is Programmable to simulate network conditions
Game server attached “close” (topologically) to the client
NISTnet 7 network emulator runs on the “router” (really a linux box)

## Slide 7: Precision Shooting: Hits vs Packet Loss

## Slide 8: Precision Shooting: Hits vs Latency

## Slide 9: Conclusions
QoS is usually specified as
  Packet Loss Constraints
  Latency Constraints
    Latency is composed of both fixed delay and “jitter”
  Outage Constraints
Recommendation for gaming traffic:
  Packet Loss: <1 percent for gaming traffic
  Latency (one way delay): <30ms
  Latency >50 ms implies an “outage” condition
Simulation report includes histogram of latencies, and outage probability for the simulation run
  Enough data to ensure that the system can deliver the required QoS under the simulation scenarios and traffic mixes selected

## Slide 10: Text Review

## Slide 11: Suggested Text
This section provides QoS requirements for traffic simulated as gaming traffic. The system shall guarantee QoS parameters consistent with the following table:
Parameter | Value
Latency (one way) | <30ms
Outage | Latency >50 ms
Packet Loss | < 1 %
Simulation reports shall provide QoS data for gaming traffic to insure that the system can deliver the required user experience for this important traffic type. Data reported shall include, mean latency seen by each mobile’s client (not in outage), mean packet loss percentage for gaming traffic, and percent of mobiles in outage during the simulation run.

## Slide 12: References
Tom Beigbeter et al., “The Effects of Packet Loss and Latency on User Performance in “Unreal Tournament 2003”, ACM SigComm ’04 Workshops, Portland Oregon, September 2004.
S. McCreary, “Trends in Wide Area IP Traffic Patterns – A View from Ames Internet Exchange”, ITC Spec. Seminar, 2000.
Michael S. Borella, “Source Models of Network Game Traffic”, Networld+Interop ’99 Engineer’s Conference, May, 1999
Johannes Farber, “Network Game Traffic Modelling”, NetGames2002, April 16-17, 2002, Braunschweig, Germany.
3GPP, “Feasibility Study for Enhanced Uplink for UTRA FDD” TR 25.896 V. 6.0.0, March 2003
3GPP2, “cdma2000 Evaluation Methodology, Revision 0”, C.P1002, version 0.3, July 23, 2004.

## Slide 13: Discussion Area

## Slide 14: Reference Architecture
Assumes a Client/Server Gaming Model
Client 1
Client 2
Client “n”
Base Station
IP Network
Gaming Server