## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | E- Model based VoIP Evaluation for MBWA | 
Date Submitted | 2005-SEP-09 | 
Source(s) | Radhakrishna Canchi 2480 N. First Street #280 San Jose, CA 95131 Kazuhiro Murakami 2-1-1 Kagahara, Tsuzuki-ku, Yokohama, KANAGAWA 224-8502, JAPAN Minako Kithara 2-1-1 Kagahara, Tsuzuki-ku, Yokohama, KANAGAWA 224-8502, JAPAN | Voice: +1-408-952-4701 Fax: +1-408-954-8709 Email: cradhak@ktrc-na.com Voice: +81 45 943 6130 Fax: +81 45 943 6175 Email: kazuhiro_murakami@csg.kyocera.co.jp Voice: +81 45 943 6102 Fax: +81 45 943 6175 Email: Minako_kitahara@csg.kyocera.co.jp
Re: | MBWA Call for Contributions for Evaluation Criteria for VoIP application | 
Abstract | This document proposes parameters for E-Model based Evaluation of VoIP for MBWA | 
Purpose | This document addresses the open issue on VoIP Quality Evaluation in the IEEE802.20 Evaluation Criteria Document Version 17. To Discuss and Adopt. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: E- Model based VoIP Evaluation for MBWA
IEEE802.20 WG had a consensus on considering ITU- G107 (E-Model) to be considered for evaluation of VoIP in MBWA Systems.
Identifying the parameters that would affect VoIP

## Slide 3: E-Model
E-Model is a computational model to assess the conversation quality of Narrowband voice. taking account of all transmission parameters in the End to End path (Mouth to Ear). End to End path can be classified in to Four broad sections in the present context of MBWA system:
  Terminal Devices
  Access Network (MBWA)
  Transport Network (MBWA-Mobile Broadband Gateway)
  Core Network (Mobile Broadband GateWay -mobile Gateway/media gateway/Internet Gateway)

## Slide 4: MBWA
Internet
PSTN/
ISDN
Media
Gateway
Broadband Connection and Control Servers
Mobility Connection & Control Servers
Mobile Internet
Application Platforms/Servers
IP Corenetwork
MBWA
Wide Area
Mobility
Mobile/
Broadband
Gateway
Mobile
Gateway

## Slide 5: VoIP Architecture
UDP
IP
MAC/DLC
TCP
PHY
AUDIO
VIDEO
RTP
RTCP
SIP
H.245
Q.931
H.225
RAS
RTSP

## Slide 6: E-MODEL
Principle Assumption:
  Transmissions impairments can be transformed into psychological factors
  Psychological Factors on Psychological Scale are additive.
Computational Model
  Transmission Planning Tool not measurement tool
  Combines all impairments in the path: Mouth to Ear.
The basic result of the E-Model is the calculation of R-Factor (Total Quality Index), a simple measure of voice quality.
R-Factor Can be translated in Mean Open Score in the scale 1-5 as perceived by the end user using the formulae from G.107:
  For R  0:
  For 0  R  100:
  For R  100:

## Slide 7: Total Quality Index: The R-Factor
R= Ro – Is – Id – Ie,eff + A
Advantage factor
Complements the effect of the convenience of mobile or other communication on a subjective quality (satisfaction).
Equipment impairment factor
Represents subjective quality impairments due to low bit rate CODEC, packet/cell loss, etc.
Delay impairment factor
Represents subjective quality impairments due to talker echo, listener echo, and absolute delay
Simultaneous impairment factor
Represents subjective quality impairments due to OLR (loudness), sidetone, and quantization distortion.
Basic signal-to-noise ratio
Represents subjective quality impairment due to circuit noise, room noise at sending and receiving sides, and subscriber line noise.
Noise
Loudness
Echo and delay
Distortion/
discontinuity
Notes: The basic model is: R = Ro - Is - Id - Ie + A
Where Ro is a base factor determined from noise levels, loudness etc.
Is represents impairments occurring simultaneously with speech,
Id represents impairments that are delayed with respect to speech,
Ie represents the so-called "equipment impairment factor"
and
A the "advantage factor" and W is a wideband correction factor.
The Equipment Impairment factor, Ie, is typically used to represent the effects of Voice over IP.
For example, assuming default values for everything else then the R Factor for an "ideal" G.729A connection with no loss, jitter or delay would be R = Ro - Ie = 94 - 11 = 83
The Advantage factor, A, is used to represent the convenience to the user of being able to make the phone call, i.e. a cellphone is convenient to use therefore people are more forgiving on quality.

## Slide 8
Default values and permitted ranges for the parameters
Parameter | Abbr. | Unit | Default value | Permitted range
Send Loudness Rating | SLR | dB | +8 | 0 ... +18
Receive Loudness Rating | RLR | dB | +2 | 5 ... +14
Sidetone Masking Rating | STMR | dB | 15 | 10 ... 20
Listener Sidetone Rating | LSTR | dB | 18 | 13 ... 23
D-Value of Telephone, Send Side | Ds | – | 3 | –3 ... +3
D-Value of Telephone Receive Side | Dr | – | 3 | 3 ... +3
Talker Echo Loudness Rating | TELR | dB | 65 | 5 ... 65
Weighted Echo Path Loss | WEPL | dB | 110 | 5 ... 110
Mean one-way Delay of the Echo Path | T | ms | 0 | 0 ... 500
Round-Trip Delay in a 4-wire Loop | Tr | ms | 0 | 0 ... 1000
Absolute Delay in echo-free Connections | Ta | ms | 0 | 0 ... 500
Number of Quantization Distortion Units | qdu | – | 1 | 1 ... 14
Equipment Impairment Factor | Ie | – | 0 | 0 ... 40
Packet-loss Robustness Factor | Bpl | – | 1 | 1 ... 40
Random Packet-loss Probability | Ppl | % | 0 | 0 ... 20
Circuit Noise referred to 0 dBr-point | Nc | dBm0p | 70 | 80 ... 40
Noise Floor at the Receive Side | Nfor | dBmp | 64 | –
Room Noise at the Send Side | Ps | dB(A) | 35 | 35 ... 85
Room Noise at the Receive Side | Pr | dB(A) | 35 | 35 ... 85
Advantage Factor | A | – | 0 | 0 ... 20

## Slide 9: VoIP QoS
Affected by
    Packet Loss
      Network
        Wireline
        Wireless
      Jitter Buffer
      PLC
    Delay
      Network
        Wireline
        Wireless
      Codec
    Delay Jitter
      Jitter Buffer
      Codec

## Slide 10: R-Factor Estimation For MBWA
If all parameters are set to the default (ideal) values, the calculation results in a very high quality with a rating factor of R = 93.2
However, the achievable R-Factor is dependent on the MBWA system inttroducing the impairmaent factors:
RMBWA = Rdefault(93.2) –Id –Ieff

## Slide 11: Effective Equipment Impairment factor
codec specific value for the Equipment Impairment Factor at zero packet-loss Ie and the Packet-loss Robustness Factor Bpl
Ppl corresponds random packet loss

## Slide 12: Packet Loss Models
Bernoulli Loss Model
2-state Gilbert Model
Other Complicated Packet Loss Models
  3-state Markov models
  4-state modified Markov models
  8-state Markov chain models
  general nth order extended Gilbert model
  The 4-state one has been used in Extended E-model.

## Slide 13: Delay impairment factor
Represents subjective quality impairments due to talker echo, listener echo, and absolute delay
In the PSTN, EL is typically 21 dB (due to 4-to-2 wire hybrid echo)
If the packetized voice call is terminated over the PSTN to a traditional phone, EL21 dB
If the packetized voice call is terminated over a packet-based network on
  a PC, the EL is likely to be smaller (<21 dB) due to acoustic echo in the PC
  an IP-phone, EL40 dB
Echo control increases the EL by 30 dB, perfect echo control increases EL to infinity

## Slide 14: VoIP Quality Evaluation
Channel Influence (Wireless/Wireline)
  Packet Loss
  Delay
  Jitter
Architecture effects
  Dejitter Buffer
  Packet Size
  Codec Frame Size
  MAC Frame Size
Packet Loss Concealment at Decoder
Equipment Impairment Factor

## Slide 15: VoIP QoS
Affected by
    Packet Loss
      Network
        Wireline (Transport Network)
        Wireless (Access Network)
      Jitter Buffer
      Packet Loss Concealment
    Delay
      Network
        Wireline (Transport Network)
        Wireless (Access Network)
      Codec
    Delay Jitter
      Jitter Buffer
      Codec

## Slide 16: Conclusion
It is proposed that consider the impairment parameters:
  Effective Equipment Impairment Factor (IE-EFF) and associated Packet Loss Robustness factor
  Delay impairment factor ID-EFF
    Assuming an echo loss of 21dB/51dB/Perfect Loss
  Jitter effects (Packet Loss and Delay) may be incorporated into IE-EFF and ID-EFF

## Slide 17: Appendix on Codec

## Slide 18: Speech Coding Families
Notes: Waveform coders: only explore the correlation in time-domain and frequency-domain
and attempt to preserve the general shape of the signal waveform. e.g. G.711 PCM (64
Kb/s) and G.726 ADPCM (40/32/24/16 Kb/s)
- Voice coders (vocoders): based on simple (voiced/unvoiced) speech production model
and no attempts are made to preserve the original speech waveform. The speech is synthetic.
e.g. 2.4/1.2 Kb/s LPC
- Hybrid coders: incorporate the advantages of waveform coders and vocoders to achieve
good speech quality at 4.8 to 16 Kb/s, includes all the modern codecs, e.g. G.729 CSACELP
(8Kb/s), G.723.1 MP-MLQ/ACELP (6.3/5.3 Kb/s), AMR (Adaptive Multi-Rate,
ACELP) and iLBC (Internet Low Bit Rate Codec).

## Slide 19: Speech Coding Families

## Slide 20: G729B/G.723.1/AMR
Belong CELP Analysis–by-Synthesis
Parameters of CELP:
  Linear Prediction/LP filter coefficnts (which are transformed into Line Spectral Frequencies)
  Adafitve/Fixed Code block Indices and Gains
Codec Differ in excitation signal. Partitiion of excitation space delay and filter coeff representation
Frame Size: 10ms(729) , 20ms (AMR) and 30ms (723) ->80/160/240 samples at 8KHz
Bulit-in Concealmemt, VAD, SID (Silence Insertion Description) frame, Null frame (non-txed frame).