## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://grouper.ieee.org/groups/802/20/> | 
Title | BEST-WINE: A Complete and Fully Compliant TDD Technology Proposal Overview | 
Date Submitted | 2005-OCT-28 | 
Source(s) | Radhakrishna Canchi 2480 N. First Street #280 San Jose, CA 95131 Kazuhiro Murakami 2-1-1 Kagahara, Tsuzuki-ku, Yokohama, KANAGAWA 224-8502, JAPAN Miinako Kithara 2-1-1 Kagahara, Tsuzuki-ku, Yokohama, KANAGAWA 224-8502, JAPAN | Voice: +1-408-952-4701 Fax: +1-408-954-8709 Email: cradhak@ktrc-na.com Voice: +81 45 943 6130 Fax: +81 45 943 6175 Email: kazuhiro_murakami@csg.kyocera.co.jp Voice: +81 45 943 6102 Fax: +81 45 943 6175 Email: minako.kitahara.nf@kyocera.jp
Re: | MBWA Call for Proposal | 
Abstract | This document presents the Summary Classification Statement + Technology Overview + Draft Technology Specfications for the MAC and the PHY layer of the of IEEE 802. 20 MBWA | 
Purpose | To disucus and Adopt BEST-WINE for Draft Specfications of IEEE802.20 MBWA | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2: BEST-WINE (Broadband MobilE SpaTial Wireless InterNet AcEess ) A Complete and Fully Compliant TDD Technology Proposal For IEEE 802.20: MBWA
IEEE 802.20 Plenary Meeting
Vancouver, Canada
November 14-18, 2005

## Slide 3: BEST-WINE (Broadband MobilE SpaTial Wireless InterNet AcEess )
Proposed Draft Technology Specifications
  Enhanced MAC Layer and PHY layer Draft Specifications to the base specifications of HC-SDMA*
  AND
    Base Technical Specifications “ATIS-PP-0700004-2005, High Capacity-Spatial Division Multiple Access (HC-SDMA)*”.
    * The copyright of this document is owned by the Alliance for Telecommunications Industry Solutions. Any request to reproduce this document, or portion thereof, shall be directed to ATIS, 1200 G Street, NW, Suite 500, Washington, DC 20005.
    * For Electornic Downloads, Paper Copy or CD-ROM please follow the link https://www.atis.org/atis/docstore/doc_display.asp?ID=3617

## Slide 4: BEST-WINE Technology Proposal Overview
High Spectral Efficiency (Bits/Sec/Hz/Sector) = 9.78 with Spatail Channels
Mobile Broadband Peak Per User Rates:
  Maximum User Data rates of 1.473Mbps (Downlink) and 566Kbps (Uplink) with Single Channel of 625 KHz.
  Maximum User Data rates of 5.89 Mbps (Downlink) and 2.26 Mbps (Uplink) with TDD Block assignemnet of 2.5 MHz
Improved Coverage
Greater Capacity by handling more than 100 Active sessions per sector and
Reduced Spectrum Requirments and Spectrum Reuse less than 1 with no frequency Planning
Effcient Mobile Handover
  Radio Layer Handover
    Mobile Directed using BS Load and Signal Strength indiacators
    Make Before Break For Transparency
  Network Handover
    Simple IP – Efficient Micromobility
    Mobile IP – For Inter System Mobility
Security
  Authentication
  Encryption
  AES

## Slide 5: Description of BEST-WINE System
  Mobile Broadband IP data Transport over the AirinterfSystem Architecture
    LoS/NLoS, Outdoor/Indoor
    Layered Architecture
      PHY/MAC Layers reference Model and 802.2 LLC Functionality
      Separation of Functionality Between User/Data/Control plane
      Bi directional IP traffic
      High Mobility
    Transports IP data from variety of applications

## Slide 6: BEST-WINE Proposal Overview PHY Summary
AAA Processing and SDMA with 4 Spatial Channel in Typical Deployment
  Base Station 9 /12 Antennas
  User Terminal with 4/2/1 Antennas
625 KHz Channel and 16 Channel Aggregagtion
Fixed Symbol Duration of 2us.
TDAM-TDD Frame of 5ms
10 Modulation and Coding Modes

## Slide 7: BEST-WINE Proposal Overview MAC/LLC Summary
Bi – Directional IP traffic w
QoS Support: (VoIP, BCMCS, Streaming)
Link Adaptation
Power Control
Slot/Channel Aggregation
ARQ
Security: Authentication & Encryption
High Mobility Support
Support more than 100 Simultaneous Active Sessions
Power Managaement
Radio Network Quality monitor and control and OP&AM services

## Slide 8: BEST-WINE SYSTEM OVERVIEW
Highest Spectral Efficiency
  Adaptive Antenna Array
  Space Division Multiple Access
  Link Adaptation & Adaptive Modulation & Coding
  Power Control

## Slide 9: BEST-WINE System Architecture
ハブ
BS
ハブ
BS
POP GW
PPP
Subscriber
Subscriber
Subscriber
TWAN
WAN
Internet
Service Provider
Enterprise
Application Service
Provider
EMS
Server
PSS
（Packet Service Switch)

## Slide 10: BEST-WINE Layered Protocol Architecture
End User Device
(PC/PDA etc)
ISP
User Terminal
Base station
PSS
Packet Services Switch
IP
Synchronous
PPP
MAC
Physical
(Ethernet)
MAC
Physical
(Ethernet)
BEST-WIN
MAC/DLC/PHY
UDP/IP
L2TP
Physical
BEST-WIN
MAC/PHY
UDP/IP
L2TP
Physical
PPP/IP
L2TPxn
Physical
PPP/IP
UDP/L2TPxn
Physical
(User)
IP
Synchronous
PPP
Air
Interface
BEST-WINE Specification

## Slide 11: BEST-WINE (Enhanced HC-SDMA)
Built on the Base specifications of HC-SDMA
Added Enhancements that meet SRD Requirements
  MAC/DLC Layer Enhancements
    QoS Support (VoIP, Streaming)
    BCMCS support
    Security Support AES
  PHY Layer Enhancements
    System Spectral Efficiency and Peek Per User Data Rates
    Supports High Mobility

## Slide 12: BEST-WINE Base Specification Overview
Physical Layer (Layer 1) | Modulation and Coding Radio Performance (transmit and receive) Performance and Test
MAC Layer (Layer 2) | Channel Structure (frame and slot) Access Management Data and Control Flow over logical channels Mapping between logical and physical (transport) channels Automatic Repeat Request (ARQ)
Connection Layer (Layer 3) | Connection, Registration, Mobility Management (CM, RM, MMC) Radio Resource Control (RRC) Authentication and Security (i-HAP, i-TAP, i-SEC) Packet Segmentation, Slot Aggregation Link Adaptation and Power Contol

## Slide 13: HC-SDMA Specification Overview Layer 1 Features
TDD/TDMA with 5 ms frame period
  3 uplink/downlink slots per frame
  One third of slot for uplink and two thirds for downlink
  2:1 asymmetry
» Range extension allows UT to use all slots at up to 15km
  Single slot at even higher range

## Slide 14: BEST-WINE Base Specification Overview Layer 1 Features
TDD/TDMA/FDMA organization with 5 ms frames
  Multiple resources permit granular allocation, low latency
  TDD well matched to adaptive antennas, asymmetric data
625 kHz carriers, constant symbol rate
  Low complexity processing
  Good spatial coherence properties
Synchronized network
  Over-the-air AT synchronization, external BS synchronization
  Predictable inter- and intra-cell interference
Adaptive modulation and coding
  Provide robust link, options for inexpensive terminals
  Link budget matching of directive, non-directive transmissions

## Slide 15: BEST-WINE Base Specification Overview Layer 2
Network Security
  Authentication & Authorization
    i-HAP: Base Station Authentication
    i-TAP : Mobile Terminal Authentication
  Privacy Encryption & Message Integrity
    i-SEC: Secure over-the-air transfer of user control/data information
Security Functions | i-HAP | Authentication of BS equipment
 | i-TAP | Authentication of UT equipment
 | i-SEC | Secure over-the-air transfer of user control/data information

## Slide 16: BEST-WINE Enhanced Specification
Spectral Efficiency
  Average Aggregate Throughput/Sector divided by Spectrum Block Assignment
    3Kmph, 120Kmph
    Block Assignments supported
Peak Per User Data Rate
  Down link and Uplink
Number of Simultaneous Sessions per sector
Link Level QoS:
  Support of IPv4 and IPv6
  Support of IETF Differentiated Service (RFC 2475) Architecture and DiffDerv QoS
Multi Antenna Capability
Coverage Enhancing Technology

## Slide 17: Enhanced Functional Specification of BEST-WINE
Network Security
  Protection to Denial of Service Attack
  Support AES Algorithm

## Slide 18: Functional Specification of Enhanced System MAC (Media Access Control) Layer
Layer 2 QoS Mechanisms
  VoIP
Persistence | Persistent channel allocation to minimize latency/jitter
Link Level Reliability | Power control and link adaptation enhancements for low throughput channels

## Slide 19: Functional Specification of Enhanced System PHY/RF LAYER
Link Adaptation
  Modulation & Coding Classes
  64QAM,24QAM
Equalization to Support High Mobility

## Slide 20: Functional Specification of Enhanced System Layer 3 + Support
IPv4 and IPv6 Support
IP Level hand-off
OA & M Support to Control Support and Monitor
Power Conservation Feature
Scheduler Functions

## Slide 21: IPv4 and IPv6 Support
MBWA Base Station (BS) and User Terminal (UT) supports IPv6 based on 3GPP2
PPP
IPv4 / IPv6
PL
R-P
PL
PL
MBWA
Air
Interface
R-P
PPP
IPv4 / IPv6
Link
Layer
PL
Link
Layer
IPv4 / IPv6
MS
RN(Base Station)
PDSN
End Host
3GPP2 Base Network Protocol Stack (Simple IPv6)
GRE
MBWA
Air
Interface