## Slide 1
Heesoo Lee
heelee@etri.re.kr
ETRI Proposal

## Slide 2: Contents
Basic aspects
Downlink
Uplink
Salient features
  Multiuser precoding MIMO
  Intercell interference management for downlink (Virtual MIMO)
  Intercell interference management for uplink (Whispering resource)
  Macro diversity in multicast/broadcast

## Slide 3: Basic Aspects

## Slide 4: Basic Aspects
Duplexing
  FDD
User Multiplexing/Multiple Access
  Downlink : OFDMA
  Uplink : SC-FDMA
Modulation
  QPSK, 16QAM, 64QAM (Optional in Uplink)
Data Channel Coding
  LDPC : Mandatory
  Convolutional turbo code : Optional
  Code rate : 1/4 ~ 4/5
H-ARQ
  Chase combining and Type-II & Type-III H-ARQ

## Slide 5: Basic Aspects
Multiple antenna transmission
  Medium to high speed users
    STBC
    Spatial multiplexing
  Low speed users
    Multi code words (MCW) transmission
    Multi user precoding MIMO
      S-PUSRC (SIC-based Per User & Stream Rate Control)
Adaptive transmission
  Frequency domain adaptation : chunk based channel
  Time domain adaptation : short TTI (0.5 ms)
  Space domain adaptation : SDMA (Multi-user precoding MIMO)

## Slide 6: Basic Aspects
Intercell Interference Management
  Downlink
    Virtual MIMO based on coordinated symbol repetition
      Intercell interference cancellation
      Full frequency reuse
      Cell planning not required
  Uplink
    Inter-cell interference avoidance/concentration with resource coordination
      Full frequency reuse
      Cell planning required to optimize performance
Multicast/Broadcast support
  Space-time (or frequency) diversity among cells
  Rotation of STBC (or SFBC) antenna combining pattern

## Slide 7: Downlink

## Slide 8: Downlink OFDM Parameters
Scalable Channel Bandwidth

## Slide 9: Frame Structure
Frame duration : 20ms
Subframe (DTP) duration : 0.5ms
Partition of resources : RS0 ~ RS10
RS7~10 are further divided into several resource subspaces (RSS)

## Slide 10: Physical Channels
DPICH
  Downlink pilot channel
CCFPCH
  Control Channel Format Physical Channel
CCPCH
  Common Control Physical Channel
SCPCH
  Shared Control Physical Channel
DSDPCH
  Downlink Shared Data Physical Channel

## Slide 11: DPICH
Support four transmit antennas
  DPICHi
    Channel estimation for antenna i
    Resource space RS0, RS1, RS5, and RS6, are used for DPICH0, DPICH1, DPICH2, and DPICH3 respectively.
Pilot symbol modulation
  Orthogonal sequences among sectors
  Pseudo Random M-PSK sequences among cells
    Joint channel estimation for multiple cells

## Slide 12: Control Physical Channels
CCFPCH
  SCPCH format information
  RS2 is used.
CCPCH
  Broadcasting common control information
  RS3 is used.
SCPCH
  ARQ information, scheduling information for up/down physical data channels
  RS4 is basically used.
  RS7 is additionally used if necessary.

## Slide 13: DSDPCH
Transmit user data
A maximum of 40 DSDPCHs in a subframe (DTP) for 10MHz channel bandwidth
Modulation
  QPSK, 16QAM, 64QAM
Channel coding
  LDPC, Convolutional turbo code
  Code rate : ¼ ~ 4/5
Each DSDPCH consists of a number of DSDSCHs (Downlink Shared Data Sub-Channels)
Four types of DSDSCH
  DS-DSDSCH (Distributed & Spreading type DSDSCH)
  DN-DSDSCH (Distributed & Nonspreading type DSDSCH)
  LN-DSDSCH (Localized & Nonspreading type DSDSCH)
  LS-DSDSCH (Localized & Spreading type DSDSCH)

## Slide 14: DS-DSDSCH
DS-DSDSCH
  There are 3*DRS7 (Dimension of RS7) DS-DSDSCHs.
  Each DS-DSDSCH consists of a RSS of RS7.
  Distributed channel structure
  Spread each symbol over a DSB (Distributed spreading block)
  A DSB consists of 3 distributed frequency-time bins.
    Spreading factor is 3.
  Spreading and scrambling sequence
    Orthogonal spreading sequences among sectors
    Pseudo random scrambling sequence among cells
  Apply interference cancellation with Virtual MIMO
  Assigned to high speed users suffering from large intercell interference

## Slide 15: DN-DSDSCH
DN-DSDSCH
  There are 3*DRS8 (Dimension of RS8) DN-DSDSCHs.
  Each DN-DSDSCH consists of a RSS of RS8.
  Distributed channel structure
  Assigned to high speed users relatively free from intercell interference

## Slide 16: LN-DSDSCH
LN-DSDSCH
  There are 3*DRS9 (Dimension of RS9) LN-DSDSCHs.
  Each DS-DSDSCH consists of a RSS of RS9.
    A RSS of RS9 consists of a chunk (15 consecutive subcarriers)
  Localized channel structure
  Not spread symbols
  Assigned to low speed users relatively free from intercell interference

## Slide 17: LS-DSDSCH
LS-DSDSCH
  There are 3*DRS10 (Dimension of RS10) LS-DSDSCHs.
  Each LS-DSDSCH consists of a RSS of RS10.
    A RSS of RS10 consists of a chunk (15 consecutive subcarriers)
  Localized channel structure
  Spread each symbol over a LSB (Localized spreading block)
  A LSB consists of 3 consecutive frequency-time bins.
    Spreading factor is 3.
  Spreading and scrambling sequence
    Orthogonal spreading sequences among sectors
    Pseudo random scrambling sequence among cells
  Apply interference cancellation with Virtual MIMO
  Assigned to low speed users suffering from large intercell interference

## Slide 18: Resource Space Partition
Example : 10MHz
RS0~RS4
  1st OFDM symbol
  Distributed
RS5~RS6
  2nd OFDM symbol
RS7~RS10
  Over 2nd ~ 7th OFDM symbols
  Unit of allocation
    BCS : Bundle of chunk
  Variable size
    Parameters
      DRS7 ~ DRS10

## Slide 19: Resource Subspace partition

## Slide 20: Resource Subspace for RS7

## Slide 21: Resource Subspace for RS8

## Slide 22: Uplink

## Slide 23: Uplink Transmission
Single carrier FDMA based system
  Orthogonal transmission within cell
Modulation:
  QPSK, 16QAM
  Optional: 8PSK, 64QAM
Channel coding
  LDPC and convolutional Turbo code
  Code rate: 4/15~4/5
MIMO
  Up to 2 transmit antennas
  Up to 4 receive antennas
Inter-cell interference avoidance/concentration with resource coordination

## Slide 24: SC-FDMA (1)
Low PAPR
Cyclic prefix guard interval: enable cost-effective frequency domain block processing at receiver side
Two types of SC transmission
  Localized transmission: multi-user scheduling gain in frequency domain
  Distributed transmission: robust transmission for control channels and high mobility UE

## Slide 25: SC-FDMA (2)
Localized transmission
  Need to feedback channel state information
  Mainly for low-to-medium mobility users
Distributed transmission
  Mainly for high mobility users
Orthogonal resource subspace division
  Transmission bandwidth is divided into localized band and distributed band
  Each band is further divided into several subbands for inter-cell interference avoidance/concentration
  A subband out of each band in a cell is operated in whispering mode; UEs using a channel belonging to the same subband in neighboring cells can be operated in speaking mode

## Slide 26: SC-FDMA Parameters
Transmission BW | 5 MHz | 10 MHz | 15 MHZ | 20 MHz
Subframe duration | 0.5 ms |  |  | 
Subcarrier spacing | 15 kHz |  |  | 
Sampling frequency | 7.68 MHz | 15.36 MHz | 23.04 MHz | 30.72 MHz
FFT size | 512 | 1024 | 1536 | 2048
Number of occupied subcarriers | 301 | 601 | 901 | 1201
Number of blocks of symbols per subframe | 6 Long blocks + 2 Short blocks |  |  | 
CP length (us/samples) | (4.04/31)  7, (5.08/39)  1 | (4.1/63)  7, (4.62/71)  1 | (4.12/95)  7, (4.47/103)  1 | (4.13/127)  7, (4.39/135) 1

## Slide 27: Frame Structure
Frame duration: 10 msec
One frame consists of 20 UTPs (Uplink Traffic Packet, UTP and sub-frame are the same in this context)
  UTP: 0.5 msec
  UTP: 6 regular symbol blocks + 2 half-length symbol blocks

## Slide 28: Pilot Channel
Pilot
  For uplink channel quality measurement (channel sounding)
  For channel estimation and coherent detection at receiver side
TDM pilot structure
  Easy to keep low PAPR characteristic
  Pilot symbols are carried on two short blocks
  Support both localized and distributed channels
Alternating transmission for fitting into short block structure

## Slide 29: Physical Channels
SPDCH (Shared Physical Data Channel): transmit data traffic and some data-dependent control signals.
SCPCH (State Control Physical Channel): transmit control signal for state management of user equipments.
UACH (Uplink ACK Channel): transmit ACK/NACK information responding to downlink data channel.
UFCH (Uplink Feedback Channel): transmit feedback information for downlink transmission.
PFCH (Path-loss Feedback Channel): transmit long-term channel quality of serving and neighboring cells for uplink interference coordination
Additional physical channels for link set-up, synchronization, etc.

## Slide 30: Channel Multiplexing
Multiplexing of Shared Channels:
  TDM pilot structure is used
  Data-independent control channels are multiplexed in frequency domain
  UE data and data-dependent control are multiplexed in time domain

## Slide 31: Multiuser Precoding MIMO

## Slide 32: S-PUSRC
Multiuser multistream precoding MIMO
S-PUSRC
  Transmitter and receiver structure
  Feedback information
  Scheduling rule
Capacity comparison

## Slide 33: Multistream precoding MIMO
Transmission of multiple parallel streams
  Independent coding for each stream
  Per stream rate control
  Known to achieve open-loop MIMO capacity when combined with stream-by-stream SIC reception
Precoding
  Precoding vector for each stream (phase and amplitude variation across transmit antennas)
  Choice of precoding matrices (or vectors) depending on cell environment and UE channel

## Slide 34: Multiuser MIMO
Single-user MIMO schemes
  PARC, S-PARC etc.
  All streams to one user
  Stream-by-stream SIC
  Spatial domain multiuser diversity is NOT available
Multi-user MIMO schemes
  PU2RC
  Multistreams to multiple users
  Spatial domain multiuser diversity
  Larger diversity gain than single-user MIMO
  Stream-by-stream SIC is NOT available
Single-user MIMO
Multi-user MIMO

## Slide 35: S-PUSRC
SIC based Per User and Stream Rate Control (S-PUSRC)
  Multiuser precoding MIMO (multiple precoded streams to multiple users)
  Spatial domain multiuser diversity gain
  Ordered stream-by-stream SIC
  Feedback information
    stream order for SIC, SINRs for multiple streams

## Slide 36: S-PUSRC
Transmitter structure

## Slide 37: S-PUSRC
Receiver structure

## Slide 38: S-PUSRC
Feedback information
  SIC order information: the stream with the largest post-detection SINR is first decoded and cancelled at each step of SIC.
  Post-detection SINRs for each stream under the assumption of perfect cancellation of the stream with preceding orders
Multiuser scheduling with the following constraints
  One data stream cannot be allocated to more than one user.
  When n streams are to be allocated to a user, these should be the first n consecutive streams in the decoding order list of the user.
Note that the scheduling constraints enable stream-by-stream SIC at the receiver

## Slide 39: S-PUSRC
Scheduling example
  If streams 2 and 3 have been allocated to UE2 and stream 4 to UE3, the remaining stream 1 cannot be allocated to UE1 or UE3.
  If streams 3 and 1 have been allocated to UE1, streams 2 and 4 can be allocated to UE2 and UE3, respectively.
UE | Decoding order of data streams
UE1 | 3 1 4 2
UE2 | 2 3 1 4
UE3 | 4 2 1 3

## Slide 40: Capacity comparison
Capacity of multi-stream MIMO in multi-user environment
  PARC: all streams to the UE with the largest capacity
  PU2RC: each stream to the UE with the largest SINR for the stream
  S-PUSRC: multiuser stream allocation for a maximum capacity under the scheduling constraints

## Slide 41: Capacity comparison

## Slide 42: Capacity comparison
S-PUSRC gives the largest capacity regardless of the number of users
  Small number of users
    SIC gain, similar to PARC
  Large number of users
    Spatial-domain multiuser diversity gain, similar to PU2RC
S-PUSRC achieves both SIC and spatial-domain multiuser diversity gain.

## Slide 43: Intercell interference management for downlink (Virtual MIMO)

## Slide 44: Virtual MIMO
Downlink inter-cell interference mitigation
  Coordinated symbol repetition
  Transmission and Detection
  Resource partitioning and allocation
  Simulation results

## Slide 45: Coordinated symbol repetition
  Inter-cell interference mitigation based on coordinated symbol repetition for cell-edge UEs and control channels
  The resources for symbol repetition of one cell/sector are set to exactly collide with those of other cell/sectors.
    Identical repetition-resource allocation among different cell/sectors
R(f1,t1)
R(f2,t2)
S1
R(f1,t1)
R(f2,t2)
S2

## Slide 46: Coordinated symbol repetition
    The transmission and reception is equivalent to a MIMO system (thus, called virtual MIMO)
    Symbol detection using ZF, MMSE, IC etc
Serving Cell
Interfering Cell
f1,
f2
Cell-edge UE
S1
S2
“2 X 2 Virtual MIMO”

## Slide 47: Repetition-resource allocation pattern
Cluster type
- Localized data subchannels
Comb type
- Control channels
- Distributed data subchannels
Block-random type
Repetition factor G

## Slide 48: Joint detection on repeated symbols
Received signal
    Repetition factor G
    Number of cell/sectors J (G ≥ J)
scrambling/orthogonal codes
data symbols from J cell/sectors
received signals

## Slide 49: Joint detection on repeated symbols
Combining weights

## Slide 50: Code sequences for detection performance improvement
To enhance symbol detection, double-layered sequences are multiplied to repetition symbols
    Cell-specific scrambling sequences as signature randomizers e.g. M-ary random phasors
        Easy cell planning
        Improve diversity among repetition symbols
    Sector-specific orthogonal codes
        Minimize correlation between the desired symbol and interfering symbols from neighboring sectors within the same cell.

## Slide 51: Resource partitioning and allocation
    Logical resource partitioning
      Two large resource blocks
        Type-A resources for traffic channels
        Type-B resources for control channels
      Type-A resource block
        Subblock A1 for interference-free UEs
        Subblock A2 for interference-susceptible UEs

## Slide 52
  Every cell adopts the same resource allocation scheme.
  The sizes of subblocks A1 and A2 can be adjusted dynamically by taking into account the interference-susceptible traffic.
Resource partitioning and allocation

## Slide 53: Resource allocation (geographical)
Traffic channels
Control channels

## Slide 54: Simulation results
Simulation parameters
  Number of cells : 3
  Modulation : QPSK
  Repetition factor : 4
  Scrambling sequence : Random 8PSK phasors
  Channel : Pedestrian A (3 km/h)
  Joint symbol detection : ZF
  Subcarrier allocation : Comb type
  Ideal channel estimation

## Slide 55: Simulation results

## Slide 56: Intercell interference management for uplink (Whispering resource)

## Slide 57: Directivity of Interference (UL)
    For a UE in UL, there exists a neighboring BS (or BSs) suffering from severe interference.
Big
Interference
Small Interference
Medium Interference
Medium Interference
Small Interference

## Slide 58: Concentration of Interference (UL)
    By concentrating big interferers, it becomes usual that big interference doesn’t exist.
Usual Case
Special Case
Big
Interference
Medium
Interference
Medium
Interference
Medium
Interference
Small
Interference
Small
Interference

## Slide 59: New ICI Management (UL)
ICI Management Based on Avoidance/Concentration of Interference
  Concentrating big interference using directivity of interference
    Large increase of SIR for most cases
    Serving users only with very good channels in special case
    Predictable ICI with bound: even the denominator of S/I
  Large Increase of SIR for Cell Boundary Users
    Large increase of fairness among users
    Increase even in total system throughput

## Slide 60: ICI Management Procedure (UL)
ICI Vector
  Interference relation between a UE and each neighboring BS measured by pilot
Resource Region Allocation by BS Based on ICI Relations of Each UE
  Orthogonal resources such as frequency and time are divided as follows:
    Special case: whispering resource region
      Big ICI from adjacent cells
    Usual case: speaking resoure region
      Small ICI from adjacent cells
      Permitted generation of big ICI toward a specific direction (or BS)
    Isolated case possibly by irregular cellular deployment: private resource region
      Small ICI from adjacent cells
      No generation of big ICI

## Slide 61: Geographical Resource Allocation
    W: whispering
    S: speaking
    Simultaneous activation of the same numbers
S1
W1
S1
W2
W4
W6
W5
W7
W3
S1
S1
S1
S1
S6
S4
S2
S3
S5
S7

## Slide 62: Distribution of Whispering Resource
Only One Concurrent Whispering Resource
  7-cell structure
  The cycle of whispering cells: 7
W
W
W
W
W
W

## Slide 63: Assumptions for Simulation
MS Distribution
  Uniform over cells, random generation
Traffic Generation
  Always queued
Channel
  Correlated shadowing without fast fading (no mobility)
Resource Allocation
  The same amount of resource (or time) allocation for all MS’s regardless of position or channel
  Proportional fair (PF) scheduling without channel variation  similar to round robin

## Slide 64: Simulation Measure
SIR Distribution
  No link-level result
    No SIR-capacity-BLER result
  95% worst SIR (5th percentile) from SIR distribution  Measure
    Only in UL
    Shannon capacity in AWGN :
SIR
pdf
95% worst SIR

## Slide 65: SIR Distribution in UL
  Resource region decision threshold
    The smallest path loss value from neighboring BSs under a fixed UE power
9dB
10dB
Excluding inferior 1%
Excluding inferior 5%

## Slide 66: Capacity Distribution in UL

## Slide 67: Reduced Number of Resource Regions
    Easier radio frame design
    Less ICI management gain, but more frequency scheduling gain
Pattern 3
Pattern 4

## Slide 68: Rotation of Resource Regions
    Frequency scheduling gain for delay insensitive traffic
S4
S3
S2
W1
S3
S2
W1
S4
S2
W1
S4
S3
W1
S4
S3
S2
time
frequency

## Slide 69: UE Nonuniformness
Maintaining the size of each resource region
  Excessive UEs are moved to other regions.
  Moving UEs from a whispering resource region to speaking resource regions does not affect other UEs.
  Moving UEs from a speaking resource region to other regions will force them to reduce their transmission power.
Changing the ratio of resource regions
  Enlarging a whispering resource region does not affect other cells.
  Enlarging a speaking resource region in cell A will force the corresponding whispering resource region in the neighboring cell to be enlarged. The disjoint whispering resource region of cell A has not to be shrunk.

## Slide 70: Irregular Multi-Cellular Environments
The Number of Patterns: 7, 3, 4, etc.
  Adjacent two cells do not hold the same pattern in common for efficiency.
    When all patterns are consumed in adjacent cells,
      The whispering resource region of the cell can be determined randomly.
Pattern Allocation
  Occurrence of pattern allocation/reallocation
    First system deployment
    New insertion of a cell
  Pattern adjustment
    After some period for gathering path loss information between a UE and its neighboring Node B’s, each Node B determines which Node B’s are adjacent to it with UEs as mediators.

## Slide 71: Sectored Multi-Cells
    Three sectored multi-cells are equivalent to omni-cells in neighboring relations.

## Slide 72: Macro diversity in multicast/broadcast

## Slide 73: Proposed Macro Tx Diversity Method
2 cell group case
  Space frequency block coding (SFBC) between 2 cell groups
Cell Planning

## Slide 74: Proposed Macro Tx Diversity Method(2)
3 cell group case
  A coded packet is divided into the three parts
  Different cell group combinations for SFBC in each part
Cell Planning

## Slide 75: Cell Sites with 2 Tx Antennas
Conventional method
Proposed method

## Slide 76: Simulation Parameters
Parameters |  | Values
Carriers frequency |  | 2 GHz
Bandwidth |  | 5 MHz
Sampling frequency |  | 7.68 MHz
OFDM symbol duration |  | 66.66 us
OFDM guard interval |  | 16.67 us
FFT size |  | 512
# of used subcarriers |  | 300
# of resources / sub-frame |  | 300 subcarriers 6 OFDM symbols = 1800 resources
# of pilot resources / sub-frame |  | 150 (300 for 2 antennas)
# of data resources / sub-frame |  | 1650 (1500)
Turbo code (N,K) | QPSK | K=1280, N=3300 (3000)
 |  | Code rate = 0.39 (0.43)

## Slide 77: Simulation Conditions
Three cell configuration

## Slide 78: Cell border performance for single antenna
Ped-A 3km/h
Veh-A 60km/h

## Slide 79: Cell interior performance for single antenna
Ped-A 3km/h
Veh-A 60km/h

## Slide 80: Cell border performance for two antennas
Ped-A 3km/h
Veh-A 60km/h

## Slide 81: Cell interior performance for two antennas
Ped-A 3km/h
Veh-A 60km/h