## Slide 1
Project | IEEE 802.20 Working Group on Mobile Broadband Wireless Access <http://ieee802.org/20/> | 
Title | Dynamic PA backoff techniques and SC-FDMA | 
Date Submitted | 2007-01-17 | 
Source(s) | Jim Tomcik Qualcomm Incorporated 5775 Morehouse Drive San Diego, California, 92121 Voice: 858-658-3231 Fax: 858-658-2113 E-Mail: jtomcik@qualcomm.com | 
Re: | Assessment of PAPR effect for MBWA Reverse Link | 
Abstract | This contribution introduces a scheduling technique that mitigates the effect of PA on spectrum mask resulting in a dynamic PA backoff that depends on the scheduled bandwidth. Localized SC-FDMA (LFDMA) and OFDMA are compared in the context of dynamic PA backoff in terms of power efficiency, spectrum mask margin and interference caused by PA distortion. | 
Purpose | For consideration of 802.20 in its efforts to adopt an TDD proposal for MBWA. | 
Notice | This document has been prepared to assist the IEEE 802.20 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. | 
Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.20. | 
Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. | 

## Slide 2
Overview - I
OFDMA has link level advantage over LFDMA
  equalization loss for moderate to high C/I up to 2dB
L-FDMA has PAPR advantage over OFDMA
  ranging from ~1.5dB for 16QAM to ~2.5dB for QPSK
  PAPR advantage offset by multiplexing multiple waveform
PAPR advantage of LFDMA is often interpreted as power efficiency advantage
  “LFDMA can use a smaller backoff and transmit a higher average power that for the same power amplifier (PA) size”
  “hence PAPR advantage = C/I advantage”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3
Overview - II
We analyze performance loss of OFDMA versus LFDMA when both systems operate at the same backoff value and PA model
  spectral mask margin: measured as proximity to the allowed limit of out-of-band emission level
  self distortion: SINR loss seen by the user due to self-interference caused by non-linear distortion
  in-band distortion: average SINR loss seen by other users from a user that experiences non-linear distortion
  our analysis assumes 5MHz spectrum allocation
We introduce and analyze a simple mitigation technique that reduces the effect of non-linear distortion on spectral mask margin
  mitigation through a simple scheduling rule: no added complexity
  based on the suggested MBWA design
  helps all multiple access schemes, including OFDMA and LFDMA
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4
Mitigation of mask margin reduction - I
Out-of-band emission level depends not only on PAPR, but also on the total bandwidth spanned by the assignment and proximity of this span to the edge of spectrum allocation
  smaller assignment span  lower out-of-band emission level
  further away from the edge  lower out-of-band emission level
MBWA features subband hopping
  channels within a sub-tree of 128 tones (8 channels) hop locally within a subband
  gain through subband scheduling: based on user channel fading
  interference diversity through hopping within a subband
sets of 16 contiguous tones
hops
subband #1
base nodes
subband #2
subband #n
frequency
  
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5
Mitigation of mask margin reduction - II
Schedule power limited users predominantly on the inner subbands: away from the edge of spectrum allocation
  high QoS users with limited PA size at sector/cell edge
  best effort users at sector/cell edge that are not constrained by interference control (user’s TX power limited by a busy bit from adjacent sectors)
Schedule users without power limitation on the remaining spectrum:
  best effort users at sector/cell edge that are constrained by interference control (user’s TX power not limited by a busy bit from adjacent sectors)
  users with large enough PA size
  users with high C/I: these users marginally benefit from a further increase in C/I
Subband selection: scheduler takes into account user’s power limitation as well as channel selectivity across subbands
AT adjusts its PA backoff according to its assignment location
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6
Power amplifier model
We assume a popular Solid State Power Amplifier (SSPA) model commonly known as Rapp model
  amplitude distortion given by the following equation
  In this study we assume
  No phase distortion according to Rapp model
  Input PA backoff is w.r.t. 1dB compression point:
  Output PA backoff w.r.t. 1dB compression point
PA input voltage
PA output voltage
Rapp model parameter typical: P = 2 -- 3
PA saturation level
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7
Spectrum mask margin
Out of band emission level is measured according to FCC mask requirements for MMDS band meets three conditions:
  total transmit power integrated over any contiguous region of 1% of bandwidth allocation within 1MHz adjacent to the channel allocation should not exceed -13dBm
  total transmit power integrated over 1MHz which is 1MHz away from the edge of the channel allocation should not exceed -13dBm
  total transmit power integrated over 1MHz which is 5.5MHz away from the edge of the channel allocation should not exceed -25dBm
Definition of the mask margin
  difference between the allowed and the actual emission level
  select the worst case margin out of the three conditions
Mask limit
Total TX power: 23dBm
Measurement bandwidth
PSD at PA output
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Mask margin versus PA backoff
User assignment in the edge subband, 16 tones
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Mask margin versus PA backoff
User assignment in the edge subband, 32 tones
Note that such a difference between OFDMA and LFDMA in out-of-band emission level is due to scattered OFDMA assignment versus localized LFDMA assignment for assignment sizes >16 tones rather than PAPR difference
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Mask margin versus PA backoff
User assignment in the edge subband, 112 tones
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Mask margin versus PA backoff
User assignment in the middle subband, 16 tones
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Mask margin versus PA backoff
User assignment in the middle subband, 32 tones
Note that a drastic difference between OFDMA and LFDMA in out-of-band emission level is due to scattered OFDMA assignment versus localized LFDMA assignment for assignment sizes >16 tones rather than PAPR difference
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Mask margin versus PA backoff
User assignment in the middle subband, 128 tones
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14
Conclusions
Users scheduled in an edge subband
  for medium and large assignments, OFDMA needs about 2 dB additional PA backoff than LFDMA, in order to maintain similar margin to the spectral mask
  however, for small assignments, both OFDMA and LFDMA can operate with similar PA backoffs, while maintaining adequate margin to the spectral mask
Users scheduled in a middle (interior) subband
  both OFDMA and LFDMA can operate at similar (low) PA backoffs, while maintaining (more than) adequate margin to the spectral mask
By scheduling users in a middle subband, both OFDMA and LFDMA maintain sufficient mask margin even at 0dB backoff
  both OFDMA and LFDMA can operate at 0dB backoff
PAPR disadvantage of OFDMA does not affect its power efficiency relative to LFDMA as far as spectrum mask is concerned, when users are scheduled away from the edge of spectrum allocation
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15
Self distortion
Defined as degradation in C/I of a user caused by non-linear distortion of its waveform by PA
SINR loss through self distortion
Signal to distortion ratio
PA distortion model
unit power
input
Receiver
distortion
power
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16
Signal to distortion ratio versus PA backoff
User assignment in the middle subband, 16 tones
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17
Signal to distortion ratio versus PA backoff
User assignment in the middle subband, 128 tones
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18
Self distortion SINR loss versus C/I
User assignment in the middle subband, 16 tones, 0dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19
Self distortion SINR loss versus C/I
User assignment in the middle subband, 16 tones, 2dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20
Self distortion SINR loss versus C/I
User assignment in the middle subband, 16 tones, 4dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21
Self distortion SINR loss versus C/I
User assignment in the middle subband, 16 tones, 6dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22
Self distortion SINR loss versus C/I
User assignment in the middle subband, 128 tones, 0dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23
Self distortion SINR loss versus C/I
User assignment in the middle subband, 128 tones, 2dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24
Self distortion SINR loss versus C/I
User assignment in the middle subband, 128 tones, 4dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25
Self distortion SINR loss versus C/I
User assignment in the middle subband, 128 tones, 6dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26
Conclusions
Both OFDMA and LFDMA incur fairly small SINR loss even at low backoff values
  OFDMA with 2dB output backoff:
    less than 0.2dB @ C/I = 0dB, less than 1.2dB @ C/I = 13dB
  L-FDMA with 2dB output backoff:
    less than 0.1dB @ C/I = 0dB, less than 0.4dB @ C/I = 13dB
SINR loss at high C/I has limited effect for user throughout
The advantage of LFDMA at high C/I within 1dB is offset by equalization loss of about 1-2dB in this C/I region for relatively large assignments
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27
In-band distortion
Defined as degradation in C/I to other users within subband due to increased interference level cased by PA distortion of a given user
  Note that depends on PA model & backoff, assignment size & location, modulation order & multiple access scheme
SINR loss through in-band distortion
PA distortion model
Receiver
average in-band distortion power
average transmit power
Total RX interference PSD
Receive C/I of the distorted user
average received in-band distortion PSD
= ratio of user assignment to the remaining bandwidth within subband
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28
In-band distortion SINR loss versus C/I
User assignment in the middle subband, 122 tones, 0dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29
In-band distortion SINR loss versus C/I
User assignment in the middle subband, 122 tones, 2dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30
In-band distortion SINR loss versus C/I
User assignment in the middle subband, 122 tones, 4dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31
In-band distortion SINR loss versus C/I
User assignment in the middle subband, 122 tones, 6dB output backoff
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32
Conclusions
Both OFDMA and LFDMA have fairly small SINR loss even at low backoff values
  OFDMA with 2dB backoff:
    less than 0.2dB @ C/I = 0dB, less than 0.9dB @ C/I  13dB
  LFDMA with 2dB backoff:
    less than 0.1dB @ C/I = 0dB, less than 0.4dB @ C/I  13dB
The difference between OFDMA and LFDMA w.r.t. in-band distortion SINR loss is within 0.5dB for the C/I range of interest
  this is the worst case scenario in terms of in-band distortion. since the assignment size was assumed to be large
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33
Observations - I
LFDMA has advantage over OFDMA in terms of spectrum mask margin when power limited users with relatively small size assignments get resources close to the edge of spectrum allocation
Both OFDMA and LFDMA benefit from scheduling power limited users in a middle subband in terms of spectrum mask margin
Both OFDMA and LFDMA have an adequate spectrum mask margin when user is scheduled in a middle subband at a very low backoff values
  output backoff of 0dB w.r.t. 1dB PA compression point
LFDMA has ~1dB advantage in self-distortion SINR at high C/I
  this advantage is offset by LFDMA equalization loss (1-2dB) for relatively large assignments at high C/I
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34
Observations - II
The advantage of LFDMA in terms of in-band distortion SINR loss is small (within 0.5dB) in the C/I region of interest
  worst case (pessimistic) scenario
LFDMA suffers equalization loss for large assignments at medium to high C/I
At low C/I and relatively small assignment sizes LFDMA PAPR advantage is offset by multiplexing traffic with control
  alternatively time division multiplexing of traffic and control results in a permanent link budget hit for either or both of them because of a reduced duty cycle
To maintain PAPR advantage, LFDMA pilot design is limited to a narrow family of signals that have low PAPR and flat p.s.d.
  the number of such signals is limited (essentially GCL sequences)
  different sequences should be used in different sectors and/or by different overlapping users of the same sector (RL SDMA)
  the use of low PAPR pilot sequences requires careful cell planning
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35
System level analysis
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: Assumptions (I)
Eight cases:
  21 dBm Max Output Power (equivalent to 28 dBm PA with 7 dB static backoff)
  23 dBm Max Output Power (equivalent to 28 dBm PA with 5 dB static backoff)
  28 dBm PA (Output power at 1 dB compression point), with dynamic backoff for OFDMA and LFDMA
    Minimum backoff 5 dB
  26 dBm PA with dynamic backoff for OFDMA and LFDMA
    Minimum backoff 3 dB
  23 dBm PA with dynamic backoff for OFDMA and LFDMA
    Minimum backoff 0 dB
Dynamic backoff adjusts PA backoff based on assignment size and location, so as to maintain an acceptable margin to spectral mask

## Slide 37: Assumptions (II)
With dynamic PA backoff, max transmit power at the AT is modeled as a function of assignment size and location (interior vs. edge subband)
Impact of all associated distortions are modeled in the system sim
    self-distortion & in-band distortion
Scheduler assigns each user to a subband that provides the largest assignment with the user’s max power constraint for that subband
Equalization and diversity losses for LFDMA are not modeled
Simulation assumptions:
  Evaluation methodology in the following slides
  PedB 3 km/h
  4 and 10 users per sector

## Slide 38: Simulation Parameters
 |  | System Parameters | 
Network Topology |  | Hexagonal Grid, 19 cells. 3 sectors/cell | 
Site-to-Site distance |  | 2.0 km | 
Carrier Frequency |  | 2 GHz | 
Bandwidth |  | 5 MHz | 
Horizontal Antenna Pattern |  | 70 deg @3 dB bandwidth, 20 dB maximum attenuation. | 
Vertical Antenna Pattern |  | None | 
Propagation Model. |  | Modified urban HATA: PL[dB] = 28.6 + 35log10(D in meter) | 
BT-MS Minimum Separation |  | 35m | 
BTS Antenna Height |  | 32m | 
AT Antenna Height |  | 1.5m | 
Log-normal Shadowing |  | 8.9 dB | 
Site-to-Site Shadow Correlation Coefficient |  | 0.5 | 
Thermal Noise Density |  | –174 dBm/Hz | 
Noise Figure |  | 10 dB | 
Total Antenna Gain | Peak BS Antenna Gain with Cable Loss | 15dB | 15 -10 -1 = 4 dB
 | Penetration Loss | 10 dB | 
 | MS Antenna Gain | -1 dB | 
Admission Control |  | 140dB path loss | 

## Slide 39: Simulation Parameters (Cont’d)
 |  | System Parameters | 
Traffic Model |  | Full Buffer | 
Antenna Correlation | BS Tx/Rx (1/ 2) | IID | 
 | MT Tx/Rx ( 1/2 ) | IID | 
MT Rx Antenna Gain Mismatch |  | 0 dB | 
Channel Profiles |  | Ped B, 3 Km/h | 
YODA Numerology |  |  | 
FFT size |  | 512 | points
Subcarrier spacing |  | 9.6 | kHz
Guard carriers |  | 32 | subcarriers
Cyclic Prefix |  | 6.51 | μs
Windowing Duration |  | 3.26 | μs
OFDM Symbol Duration |  | 113.93 | μs
PHY Frame Duration |  | 8 | OFDM Symbols
HARQ Interlaces (FL/RL) |  | 6 | 

## Slide 40: 4 Users/Sector, System Loading
System is power limited
Transmit PSD is determined by delta-based power control
Transmit bandwidth is limited by maximum PA size
  21 dBm max output power results in 49% bandwidth usage
  23 dBm max output power results in 55% bandwidth usage
  Dynamic PA backoff results in 54-55% bandwidth usage for both OFDMA and LFDMA (essentially the same as 23 dBm max output power)

## Slide 41: 4 Users/Sector, User Throughput
21 dBm max output power is shown to have 10% loss in sector throughput compared to 23 dBm max output power
Dynamic PA backoff (with 26 dBm PA or 28 dBm PA) achieves almost identical performance as fixed, 23 dBm max output power
Same sector throughput
  Same mobile throughput fairness
With 23 dBm PA, dynamic PA backoff yields a difference of less than 5% between LFDMA and OFDMA throughput

## Slide 42: 4 Users/Sector, Resource Allocation
Proportional fairness scheduler tries to equalize the bandwidth resources allocated to each user.
  Edge users are allocated subcarriers over all interlaces.
  Maximum allocation size is subjected to PA constraints.
  On X-axis: subcarriers allocated for each user is normalized by the average number of subcarriers per user.
21 dBm max output power results in fewer subcarriers allocated to the edge users.
Dynamic PA backoff (with a 23 dBm PA) results in similar fairness as 23 dBm max output power.

## Slide 43: 4 Users/Sector, Decode C/I
Edge users are often allocated the minimum channel size due to PA constraints
Decoding C/I of edge users reflects the available PA output power
Dynamic PA backoff provides 0.5 to 1 dB C/I gain over 21 dBm

## Slide 44: 10 Users/Sector, User Throughput
System is not power limited; hence PA limitation does not impact the total sector throughput.
Geometric mean throughput:
  21dBm Max Output Power: 2475 Kbps
  23dBm Max Output Power: 2790 Kbps
  28dBm PA,OFDMA dynamic backoff: 2818 kbps
  28dBm PA, LFDMA dynamic backoff: 2832 kbps
  26dBm PA, OFDMA dynamic backoff: 2784 kbps
  26dBm PA, LFDMA dynamic backoff: 2807 Kbps
  23dBm PA, OFDMA dynamic backoff: 2493 Kbps
  23dBm PA, LFDMA dynamic backoff: 2634 Kbps
Improved geometric mean throughput shows fairness gain of 23dBm output power over 21dBm output power
Dynamic PA backoff with 26 and 28 dBm PA (1dB comp. point) achieves almost identical performance as fixed 23 dBm output power
With 23 dBm PA (1dB comp. point) and dynamic PA backoff, the difference in the LFDMA and OFDMA throughput is only 5%

## Slide 45: 10 Users/Sector, Loading and Resource Allocation

## Slide 46: 10 Users/Sector, IoT and and Decode C/I

## Slide 47: Conclusions
With PA sizes of 28 dBm and 26 dBm (at 1 dB compression point), OFDMA and LFDMA with their corresponding dynamic PA backoff values achieve a performance almost identical to the fixed, 23 dBm max output power (28 dBm PA with 5 dB fixed backoff)
  Same sector throughput
  Same fairness among users
With PA size of 23 dBm and dynamic PA backoff with a minimum backoff value of 0 dB, the difference in the LFDMA and OFDMA throughputs is at most 5%
OFDMA reverse link provides link performance gains at high SNR (not included in the above analysis)
OFDMA reverse link provides much better design flexibility
  Different types of waveforms (pilot tones, control channel segments etc) may be frequency-multiplexed, without incurring additional PAPR penalties
  Can be exploited to improve handoff performance, control-channel link budget etc