## Slide 1: Vision of the ITU-R on “Systems Beyond IMT-2000”
IEEE 802 MBWA ECSG
November 11-15, 2002
Kauai, Hawaii USA
C802m_ecsg 02/08

## Slide 2: Outline
ITU-R Draft New Recommendation, “Vision, framework and overall objectives of the future development of IMT-2000 and systems beyond IMT‑2000”
  Global growth of mobile and wireline subscribers
  Illustration of capabilities of IMT-2000 and systems beyond IMT-2000
  Communications relationships between devices in the three domains
  Future network of systems beyond IMT-2000 including a variety of potential interworking access systems
  Illustration of complementary access systems
  Phases and expected timelines for future development of IMT-2000 and systems beyond IMT-2000
ITU-R Preliminary Draft New Report, “Technology Trends”
  Utilization of Spectrum
  Access network and radio interfaces

## Slide 3: Recommendations and Reports of ITU-R Working Party 8F – Future Development of IMT-2000 and Systems Beyond IMT-2000
ITU-R Draft New Recommendation (DNR): Vision, framework and overall objectives of future development of IMT-2000 and systems beyond IMT-2000
  Adopted at the 9th meeting of WP8F (October 2002)
  Submitted for approval at the next meeting of ITU-R Study Group 8 (February 2003)
ITU-R Preliminary Draft New Report (PDNR): Technology Trends
  Scheduled for completion and adoption at the 11th meeting of WP8F (October 2003)

## Slide 4: Market Trends
Growing demand for mobile services
  The number of mobile subscribers worldwide has increased from 215 million in 1997 to 946 million (15.5% of global population) in 2001 as shown in Figure 4-1[1].
  It is predicted that by the year 2010 there will be 1 700 million terrestrial mobile subscribers worldwide.
Trends in services and applications
  Users will expect a dynamic, continuing stream of new applications, capabilities and services that are ubiquitous and available across a range of devices using a single subscription and a single identity (number or address).
  Multimedia traffic is increasing far more rapidly than speech, and will increasingly dominate traffic flows. There will be a corresponding change from predominantly circuit-switched to packet-based delivery.
________________
www.itu.int/ITU-D/ict/statistics
[1]

## Slide 5: Global growth of mobile and wireline subscribers

## Slide 6: Illustration of capabilities of IMT-2000 and systems beyond IMT-2000

## Slide 7: High Level Vision
Future development of IMT-2000
  There will be a steady and continuous evolution of IMT-2000 to support new applications, products and services.
New capabilities of systems beyond IMT-2000
  There may be a requirement for a new wireless access technology for the terrestrial component to complement the enhanced IMT-2000 systems and the other radio systems.
  Need to support data rates of up to approximately 100 Mbit/s for high mobility, such as mobile access
  Need up to approximately 1 Gbit/s for low mobility such as nomadic/local wireless access.

## Slide 8: High Level Vision
Relationship of IMT-2000, systems beyond IMT-2000 and other access systems:
  Continuing to develop between different radio access and communications systems, for example wireless PANs, LANs, digital broadcast, and fixed wireless access.

## Slide 9: New capabilities for systems beyond IMT-2000
It is anticipated that there will be a requirement for a new radio access technology or technologies at some point in the future to satisfy the anticipated demands for higher bandwidth services.
Systems beyond IMT-2000 will:
  Support a wide range of symmetrical, asymmetrical, and unidirectional services
  Provide management of different quality of service levels to realize the underlying objective of efficient transport of packet‑based services.
In parallel, there will be an increased penetration of nomadic and mobile wireless access multimedia services.
The technologies, applications and services associated with systems beyond IMT-2000 could well be radically different from the present, challenging the perceptions of what may be considered viable by today's standards and going beyond what can be achieved by the future enhancement of IMT-2000 working with other radio systems.

## Slide 10: Communications relationships between devices in the three domains
A similarity of services and applications across the different systems is beneficial to users, and this has stimulated the current trend towards convergence
The increasing prevalence of IP-based applications is a key driver for this convergence and facilitates the establishment of relationships between previously separate wireless platforms.
The formation of these relationships is distinct from the development of each wireless access system, including IMT-2000;

## Slide 11: Future network of systems beyond IMT-2000 including a variety of potential interworking access systems

## Slide 12: Future network of systems beyond IMT-2000 including a variety of potential interworking access systems
Different radio access systems will be connected via flexible core networks, allowing individual users to be connected via a variety of different access systems to the networks and services he desires.
The interworking between these different access systems in terms of horizontal and vertical handover and seamless service provision with service negotiation including mobility, security and QoS management will be a key requirement, which may be handled in the core network or by suitable servers accessed via the core network.
This "Optimally Connected Anywhere, Anytime" vision could be realized by a network comprising a variety of interworking access systems connected to a common packet-based core network.

## Slide 13: Illustration of complementary access systems
The enhanced IMT-2000 and the new mobile access of systems beyond IMT-2000 will be part of the cellular layer and hot spot layer. Nomadic/local wireless access of systems beyond IMT‑2000 will be part of the hot spot layer.
This figure illustrates a
flexible and scalable
environment which can
be used for the allocation
of system capacity in a
deployment area, where
one or several systems
may be deployed according
to need.

## Slide 14: Timelines
Timelines for the future development of IMT-2000 and systems beyond IMT-2000 depend on a number of factors:
  market trends, requirements and user demands;
  technical capabilities and technology developments;
  standards development;
  spectrum availability, including allowing sufficient time to re-locate systems that may be using proposed bands;
  regulatory considerations;
  system (mobile and infrastructure) development and deployment.

## Slide 15: Phases and expected timelines for future development of IMT-2000 and systems beyond IMT-2000

## Slide 16: Recommendations
Standardization
  that detailed standardization of the radio interface(s) should take into account the frequency band(s) in which it is intended to be used;
  that global and open standardization of the radio interface specifications should continue in the future to realize the benefits of mass market and ensure inter-operable equipment so that users, operators, manufacturers, etc. can continue to benefit from mobile communications;
  that the level and type of standardization should be adapted to meet technical and market requirements at that time;
  that standardization should be performed in a timely manner prior to system deployment and should take into account the availability of spectrum and market considerations;

## Slide 17: Recommendations
Focus areas for further study
  that research forums and other external organizations wishing to contribute to the future development of IMT-2000 and systems beyond IMT-2000, are encouraged to focus especially in the following key areas:
    radio interface(s);
    access network related issues;
    spectrum related issues;
    traffic characteristics;
    market estimations.

## Slide 18: Working Document towards a Preliminary Draft New Report – Technology Trends
Utilization of spectrum
Technologies for improving bandwidth efficiency
Technology solutions to support traffic asymmetry
Advanced system innovations using enhanced TDD
Adaptive antenna concepts and key technical characteristics
Multiple input multiple output techniques

## Slide 19: Working Document towards a Preliminary Draft New Report – Technology Trends
Access network and radio interfaces
Software-defined radios
High data rate packet nodes
Internet technologies and support of internet protocol applications over mobile systems
IP broadband wireless access
Radio on Fibre

## Slide 20: IP broadband wireless access technologies