## Slide 1: Requirements Topics and Proposals as discussed at Session #4 of 802.20
IEEE 802.20-03/16r1

## Slide 2: High Level Topic List
Reference Architecture
Channel Bandwidth
FER
Sustained Spectral Efficiency
QoS
Multicast
Repeater Delay
Synchronization
OAM

## Slide 3: Approach
One bite at a time !
How to eat a chocolate elephant …

## Slide 4: Reference Architecture
Associated Issues
  Need for clear indication that 802.20 follows layered design
  Clear statement that the goal is to allow joint optimized design of MAC and PHY layers to support mobility and antenna technologies, while adhering to above
  Use of an LLC or “Shim Layer” above the MAC to provide full service to layer and/or a switching layer on top of L2
  Relationship to 802 architecture compliance
  Detail sufficient to address FER requirement

## Slide 5: Reference Architecture
Most Recent Proposal (2003/9/5 – Mark Klerer e-mail)
  3.1.1 MBWA System Reference Architecture
  Adopting current communications systems specification principles, 802.20 MBWA systems will be specified using a layered architecture. The 802.20 standards, in conjunction with other 802 standards, will specify the services to be delivered by layers 1 and 2 to an IP based layer 3 or a switching layer, e.g. PPP, MPLS. To facilitate a layered approach, the 802.20 specification shall incorporate a reference partitioning model consisting of the MAC and PHY. This layered approach shall be generally consistent with other IEEE 802 standards and shall remain generally within the scope of other IEEE 802 standards as shown in figures 1 & 2. The 802.20 standards shall also address the needs of logical link control and how and when the 802.2 LLC functionality is used. The 802.20 standards include PHY and MAC layer specifications with a well-defined service interface between the PHY and MAC layer. To provide the best possible performance, the MAC layer design may be optimized for the specific characteristics of the air interface PHY. Figure 2 shows the relationship of various 802 PHY and MAC layer standards to other 802 architectural components. The 802.20 standards shall clarify how 802.20 fits into this architecture.

## Slide 6: Reference Architecture

## Slide 7: Channel Bandwidth
Associated Issues
  Desire to work in existing available BW allocations
  Desire to work with larger BW expected to be available in the future
  Requirements for systems beyond 10MHz (2 x 5MHz)
    Capacity increase for same services
    New Services
  Availability of Spectrum for 20-40MHz systems
  Power consumption of mobile terminals operating in 40Mhz channels
  Clear specification of TDD/FDD BW
  Relationship to 802.16e effort
  How to document requirements for the MegaBW systems (Defer decision)

## Slide 8: Channel Bandwidth
Most Recent Proposals (E-mails Wilson, Upton, O’Conner, Cleveland, Trinkwon)
  4.1.4. Support for different block assignments
  The AI shall support deployment of 802.20 systems in the following sized block assignments:
FDD Assignments | 2 x 1.25 MHz 2 x 5 MHz 2 x 10 MHz 2 x 20 MHz
TDD Assignments | 2.5 MHZ 5 MHZ 10 MHZ 20 MHz 40 MHz
The individual 802.20 AI proposals may optimize their MAC and PHY designs for specific bandwidth and duplexing schemes.

## Slide 9: Proposal from Cleveland, Crowley, Wieczorek and Wilson
4.1.4 Support for Different Block Assignments
Definition to be added to Appendix A – Terminology
  Block Assignment – A block assignment, which may include paired or unpaired spectrum, is the amount of licensed spectrum assigned to an individual operator.

## Slide 10: FER
Associated Issues (C802.20-03/83)
  Do we need to specify it
  If specified relationship to 802
  Application independence
  Simplicity to test
  Relationship of functions to sub-layer model
  Requirements for specific applications in criteria evaluation document or specification of scenarios under which to test and measure FER
Most Recent Proposals (Cleveland C802.20-03/83)) No agreement reached on text change. Deferred for further discussion at CG level.
  The PHY and MAC layers shall be capable of adapting the modulation, coding, FEC and ARQ and power levels to ensure that SDU frame error rates are reduced to a level to meet performance requirements of higher protocol layers (e.g., TCP over IP).
  For a frame error rate of TBD for a 1024 byte SDU frame size delivered to the PhSAP, the probability that a MSDU is not delivered correctly at an MSAP due to the operation of the Physical layer and the MAC protocol, SHALL be less than TBD per octet of MSDU length.
  The PHY and MAC layers MAY operate at higher frame and octet error rates for different applications, such as for decrease latency in real time applications (e.g., VoIP or streaming video).

## Slide 11: Proposed FER Requirement Model (modified)
Specify FER or BER for SDU delivered to MSAP
Specify FER or BER for SDU delivered to PhSAP
Require flexibility to disable ARQ or to operate at higher FER or BER for SDU frames
Give requirements for specific applications in Evaluation Document
Data Link
Layer
Physical Layer
(FEC)
MAC
Sublayer
PhSAP
PHY
Layer
LSAP
LLC
Sublayer
MSAP

## Slide 12: Sustained Spectral Efficiency
Associated Issues
  1 bps/Hz/sector vs 2 bps/Hz/sector
  Precise definition
  Realistic target value as determined by informed opinion on minimum market demands and maximum technological feasibility (time related)
  Should we look at total appearing on the backhaul per Hz of bandwidth used in the base station

## Slide 13: Multicasting/Broadcasting Requirement
Associated Issues
  Efficient use of air-interface by allowing use of a single air-link to broadcast/multicast content to all or multiple terminals
Proposal (Add to Section 3.1)
  The AI shall support broadcast and multicast services

## Slide 14: Repeater Support
Associated Issues
  Use of repeaters to fill coverage holes
  Use of repeaters to extend range
  Impact of solution on air-interface design
Proposal (New Requirement – (C802.20-03/76))
  The system should support the use of repeaters .

## Slide 15: Synchronization
Associated Issues (C802.20-03/84)
Proposal (Based on C802.20-03/84)
  The air interface shall support downlink synchronization and uplink synchronization. Synchronization between Base Stations is optional.

## Slide 16: Driving to procedural closure
Round 1 of iterative requirements development proposed to close in November
Work towards consensus between now and November on open issues that you believe need to be in round 1.