## Slide 1: Handoff for Multi-interfaced 802 Mobile Devices
Paul Lin
Intel Corp
May’03, Dallas

## Slide 2: How Does MN with Multiple Interfaces Help?
Initiate/Complete handoff while traversing in the overlapping area
AR
Internet
AR
 Acquire new CoA
 Initiate handover
AP
AP
AP
AP
 Probe
Authenticate
Associate
How big is the overlapping area to be useful & practical?

## Slide 3: Handoff Distance
Definition: distance traversed by a MN from acquiring a new CoA or initiation L2 handoff to completion of the handoff
    handoff scheme (route optimization)
    Processing (non-transport related) delay
Function of
  End-to-end delay
  User speed
  Packet loss rate

## Slide 4: One-way latency distribution
Both end points at Irvine, CA
11 hops
End points at Irvine and London
22 hops
sharp peaked distributions (shifted Gamma)
most delay values clustered within about 10% of both the mean and minimum values
Source: Andrew Corlett, et al, “Statistics of One-Way Internet Packet Delays,” 53rd IETF, Minneapolis, March 18 2002

## Slide 5: One-way Latency Distribution
100
10-1
10-2
10-3
10-4
10-5
10-6
Delay (ms)
101
102
103
pdf
100
10-1
10-2
10-3
10-4
10-5
10-6
10-7
10-8
100
200
300
400
500
Delay (ms)
Irvine – Irvine
Irvine – London
A. Corlett, et al., “Statistics of One-Way Internet Packet Delays,” 53rd IETF, Minneapolis, March 2002.
99.9% of delays occur within 30 ms and 115 ms

## Slide 6: L3 Handoff Distance
Handoff Distance (in meters) |  | Max MN Moving Speed w/o route optimization |  |  |  | Max MN Moving Speed with route optimization |  |  | 
 |  | 10 Km | 60 Km | 120 Km | 180 Km | 10 Km | 60 Km | 120 Km | 180 Km
Max one-way packet delay | 50 ms |  |  |  |  |  |  |  | 
 | 75 ms |  |  |  |  |  |  |  | 
 | 115 ms |  |  |  |  |  |  |  | 
0.6 (m) | 3.3 | 6.7 | 10.0 | 1.4 (m) | 8.3 | 16.7 | 25.0
0.8 | 5.0 | 10.0 | 15.0 | 2.1 | 12.5 | 25.0 | 37.5
1.3 | 7.7 | 15.3 | 23.0 | 3.2 | 19.2 | 38.4 | 57.5
For 99.9+% Packet Delivery

## Slide 7: L2 Handoff (Generic)
MN
AP’s within range
Probe Request
Probe Responses
Probe Request
Probe Responses
Authentication
Authentication
New AP
current AP
Send Security Block
Re-association Request
Re-association Response
Rcv. Security Block
Move Request
Move Response
Probe
Authentication
Re-association
Initiated outside overlapping area
completed inside overlapping area

## Slide 8: L2 Handoff Distance
40.0
26.7
13.3
2.4 (m)
L2 Handoff Distance (in meters)
180 Km/h
120 Km/h
60 Km/h
10 Km/h
Max MN Moving Speed
For 99.9+% Packet Delivery

## Slide 9: Practicality & Implications
Can the overlapping region be practically engineered? Seems OK, considering
  Macro cell: typically ~20 miles in diameter
  Micro cells: a mile or so in diameter
    Serve regions of high-traffic density
  Pico cells: diameter of a few hundred meters or less
    Provide mobile service in highly congested areas like shopping centers, exhibition centers, office buildings, etc.
  802.11: 150-2000 feet without special antenna
    Hot-spot, low-speed roaming users
  802.16: 5 Km
    Metropolitan, low-, medium- and high-speed roaming users
Simultaneous AP associations or IP connections for multi-interfaced mobile nodes can simplify and expedite handoff
Suggest to include corresponding handoff procedure(s) and network planning in the scope