## Slide 1: 802.21 L2 Services for Handover Optimization
David Johnston
david.johnston@ieee.org
dj.johnston@intel.com

## Slide 2: Purpose (of these slides)
Introduce 802.21
Describe work relevant to DNA
Solicit feedback

## Slide 3: 802.21
Approved as a full IEEE WG Feb 27th
Has been meeting as an ECSG for 1 year
Initial charter to study handover between
  802.x  802.x (where handover not supported)
  802.x  802.y (where x may not equal y)
  802.x Non 802 (e.g. cellular)
Now has approved PAR for ‘Media Independent Handover Services’

## Slide 4: Motivation
Multi-Interfaced Devices
  Laptops, PDAs, 11/16/PP/PP2 handsets etc.
Session maintenance
  Across heterogeneous media
Inadequate L2 support for L3 DNA and Mobopts activities.

## Slide 5: Problems We Are Addressing
You don’t know what you attached to when you associated/registered/plugged into a L2 network
Upper layers don’t know what is going on at L2 and so can’t make good handover decisions
There is no media independent way of asking for handover related information over a link. A conduit is needed.

## Slide 6: Relevant Elements in Network

## Slide 7: Work
DNA
  Put in place useful L2 network detection mechanisms
Handover Optimization
  Handover information definition and transport
  L2 Triggers
Other
  Cellular coupling methods

## Slide 8: DNA Related Proposals
CUPE (Controlled/Uncontrolled Port Entity)
  Builds on 802.1X fork
  Provides media independent access to ‘information’
  DNA is the primary purpose of that information
  Authenticity determined by which side of the fork the information resides on
  Media specific optimizations expected (through 802.11 FR and 802.16e)

## Slide 9: The Link Interface
A media independent protocol operating over 802 links
  Get handover or network detection and selection information
  Maybe act as conduit for event into
  Maybe act as conduit for backhaul signaling
CUPE model being promoted
  Controlled and Uncontrolled Port Entity

## Slide 10: 802.1x

## Slide 11: CUPE* Model *Controlled/Uncontrolled Port Model

## Slide 12: Upper Layer Event Binding

## Slide 13: Handover Information
Define Information semantics
  Am I likely to authenticate here?
  Subnet crossing indicators
  What is the L3 service (IP, AT, ATM, etc)?
  Neighborhood lists
  Vendor
Define Encoding
Define Transport

## Slide 14: Handover Information Equivalence
The utility of any information increases with its similarity in terms of structure and semantics to information in other network domains
  Try to align with structured information from non 802 groups to allow effective interworking with them
    IETF, 3GPP, 3GPP2
  Achieve levels of mapping
    Structure equivalence – easy
    Semantic equivalence – requires hard work
    Encoding equivalence – next to impossible

## Slide 15: Backhaul DNA
My current link is better at delivering data to me than my pre-association/pre-initial-ranging link to the AP/BS over there
Ask for the information via the local AP/BS who fetches it from the candidate AP/BS
Some level of protocol required to do this and L3 support to render media independence

## Slide 16: The Service

## Slide 17: Define L1,2 – L3 Triggers
This is the primary driver for the group
  To maintain L3 sessions during handoff L2 support is required eg. TRIGTRAN, SEAMOBY, MOBOPTS
  Triggers are the underlying mechanism for enabling seamless handoffs where possible
  Triggers can be generic (link_up, link_down, etc)
    It is the responsibility of an implementation to determine why and when it would fire a trigger.
    Enables proprietary differentiation in lower layer mechanisms while maintaining a standard interface
  Could be extensible. Vendor proprietary triggers?
Will talk about this further in mobopts

## Slide 18: Feedback?
We need this stuff to match well to the needs of mobopts and DNA, otherwise we are wasting our time.
  Approval at the 802.21 to iterate trigger and DNA proposals with the IETF to achieve a stable spec
?

## Slide 19: Where to Look
http://www.ieee802.org/handoff
  Details for the mailing list are there
    Its open to all