## Slide 1: Awareness of the handover to be distinguished from a L2 or L3
Soohong Daniel Park
Soohong.Park@SAMSUNG.COM
Samsung Electronics.
March’04, Orlando FL

## Slide 2: Miscellaneous Handover
FMIP6 proposes a Fast Handover mechanism in the 802.11.
MN don’t know whether it changes AP(MN1) or AR(MN2).
AP
AP
AP
AR
AR
MN2
MN1
L3 Handover ?
L3 Handover ?

## Slide 3: Problem Statement
#3 There is no standardized mechanism in 802 for information exchange between mobile terminals and network attachment points. This impacts the ability to make informed decisions to select between disparate network attachment points or to initiate handoffs between heterogeneous network types or between administrative domains within a single network type. Thus there is a need to develop a standard that permits mobile terminals and network attachment points to access information on which to base effective handoff decisions.

## Slide 4: Current Procedure of FMIP6
After discovering a new nearby AP, MN sends RtSolPr in order to resolve AP identifiers to subnet router information.
If the new AP is connected to the PAR’s current interface itself, PAR MUST respond indicating that the point of attachment is known, but is connected to current interface.
Handover does not require change of CoA.
AP
AR
MN1
AP
PrRtAdv (Code=5)
RtSolPr
RtSolPr: Router Solicitation for Proxy Advertisement
PrRtAdv: Proxy Router Advertisement

## Slide 5: Background
AP lets MN know the handover whether L2 or L3.
ARID (Access Router Identifier) can be simply configured in conjunction with the SSID on the AP.
Reduced the redundant message exchanges between MN and PAR when performing L2 handover.

## Slide 6: Potential Solution
ARID in the MAC Management Frame. (Preferred)
  Capability Information in the Beacon (and Probe response) can be used for letting MN know its movement whether it occurs on L2 or L3.
New MAC Management Frame for ARID.
  Delegation in conjunction with the Beacon interval.
  A large amount of frame in the 802.11 spot.

## Slide 7: Proposed Operation
AP
AR
AR
MN2
MN1
AP
AP
Scanning
Beacon or Probe response
with ARID (aaaa)
aaaa ?
L2 Handoff
aaaa
bbbb
Scanning
Beacon or Probe response
with ARID (bbbb)
bbbb ?
L3 Handoff
IETF is working on this area
(CAPWAP WG)

## Slide 8: ARID Format
Frame Control | Duration | DA | SA | BSSID | Sequence Control | Frame Body | FCS
Timestamp | Beacon Interval | Capability Information | SSID | Supported Rates | FH Parameter Set | DS Parameter Set | CF Parameter Set | IBSS Parameter Set | TIM
Beacon
Probe response
Timestamp | Beacon Interval | Capability Information | SSID | Supported Rates | FH Parameter Set | DS Parameter Set | CF Parameter Set | IBSS Parameter Set
ARID

## Slide 9: New MAC Management Frame
Frame Control | Duration | DA | SA | BSSID | Sequence Control | Frame Body | FCS
Type value | Subtype value | Subtype description
00 | Reserved (0110-0111) | AR Identification
ARID

## Slide 10: Operation with ARID
New defined L2 Trigger
L3_Change (?)
PAR (ARID=aaaa)
PAP
MN2
NAR (ARID=bbbb)
MN1
NAP
Association
No L3 Handover
Association
ARID (aaaa) wit Beacon
ARID (bbbb) with Beacon
L3_Change & Router Discovery
RtSolPr ( for the FMIP6 Operation )

## Slide 11: Conclusion
Develop a standard that permits mobile terminals and network attachment points to access information on which to base effective handoff decisions.
Suggest to work on the solution for distinguishing either a L2 handoff or a L3 handoff.
Reduce the redundant message exchanges and miscellaneous operation on mobile terminals.