## Slide 1: Interaction between L2 and Upper Layers in IEEE 802.21
Xiaoyu Liu
xiaoyu.liu@samsung.com
Youn-Hee Han
yh21.han@samsung.com
Samsung AIT
2004-03-04

## Slide 2: Background (1)
Handover Strategies
  STA Initiated, Network Assisted
  Network Initiated, STA Assisted
Alper Yegin, et al.
  draft-yegin-dna-l2-hints-01.txt
D. Johnston
  doc.: 802.21_IETF_DNA_r1, “802.21 L2 Services for Handover Optimization”

## Slide 3: Background (2)
What is addressed:
  L2->L3 triggers: for efficient handover
    L2 triggers (Alper Yegin, et al): Link Up/Link Down
    L2 triggers semantics (D. Johnston)
      Event: Link Up/Link Down
      Predictive: Link going up/Link going down
What is not addressed:
  Upper layers obtaining currently connected and potentially available link status information on demand
  Upper layers commanding the link-layer to take an action, such as connect to or disconnect from a radio link
IEEE 802.21 defines a standardized mechanism for the interaction between upper layer entities and different types of link

## Slide 4: Scenario 1: Optimal Selection of Radio Link
Upper Layer Entities, e.g. link management entities in STA, select optimal radio link when multiple nets are available
The handover criteria may be not only based on link quality, but also other factors, e.g. service price, network characteristics, costumer preferences, context, etc.
Upper Layer Entities should be able to monitor the status of different links in the STA through standardized interface and make optimal handover decision.

## Slide 5: Scenario 2: Network Initiated Handover
Upper Layer Entities in Network select optimal radio link when it detects that multiple nets are available
Network should be able to monitor the status of different links in the STA through standardized interface and make optimal handover decision. In some cases, the handover procedure may be more efficient.

## Slide 6: L2 and Upper Layers Interaction (Local)
MAC
PHY
LLC
IP
Other
Request
Response
Upper Layer Entities request the link status
Link Layer reports the link status to Upper Layers Entities
Upper Layer Entities make optimal handover decision and command the switch between available radio links
Link Layer reports the execution result of the switch command

## Slide 7: L2 and Upper Layers Interaction (Remote)
MAC
PHY
LLC
IP
Other
LLC
Upper Layer Entities in Network poll the link status of STA
STA reports the link status to Upper Layer Entities in Network.
Network makes handover decision and sends switch command to STA
STA reports the result of the switch command
MAC
PHY
LLC
IP
Other
Request
Response

## Slide 8: Semantics for Interaction Primitives (1)
Link_Poll_request
  Description: issued by Upper Layer Entities to discover the status of the currently connected and potentially available links
  Trigger Type: Event
  Source: Local / Remote
  Parameter:
    Link Type: 802.11/802.15/802.16e/GPRS/GSM/UMTS, etc
    MAC Address of polled radio interface
    MAC Address of polling network entity (in case of remote type)
    Others (to be defined later)
Link_Poll_response
  Description: corresponding to Link_Poll_request to report link status to Upper Layer Entities
  Trigger Type: Event
  Source: Local / Remote
  Parameter:
    Link Type: 802.11/802.15/802.16e/GPRS/GSM/UMTS, etc
    MAC Address of polled radio interface
    Link attributes: link quality, QoS parameters, security, attachment point address, etc.
    Others (to be defined later)

## Slide 9: Semantics for Interaction Primitives (2)
Link_Switch_request
  Description: issued by Upper Layer Entities to force a given interface to switch from one radio link to another
  Trigger Type: Event
  Source: Local / Remote
  Parameter:
    New Link type
    MAC Address of interface
    MAC Address of network attachment point
    Reason codes: service price / QoS / user preferences, etc
    Others (to be defined later)
Link_Switch_response
  Description: Link Layer reports the result of Link_Switch_requrest command
  Trigger Type: Event
  Source: Local / Remote
  Parameters
    Result codes: success / failure

## Slide 10: Reference Model
MAC
MLME
M
L
M
E
_
S
A
P
MAC_SAP
MAC_SAP Messages Defined with in H/O Spec
PHY
PLME
P
L
M
E
_
S
A
P
PHY_SAP
Pass interaction messages and/or handover decision data through management interface?
Generic Messages:
Link_Poll_request
Link_Poll_response
Link_Switch_request
Link_Switch_response
S
M
E

## Slide 11: Final Remarks
Properties of Trigger and Interaction
  Triggers are event messages passed from source to destination, do not require corresponding feedback from destination to source (“read only” in terms of API), e.g. L2 triggers
  Interactions include a pair of Request/Response message between source and destination (“read/write” in terms of API), e.g. Link_Poll_request, Link_Poll_response.
Open Issues
  Implementation of interaction behaviors depends on the reference model of IEEE 802.21
    Management frames through MAC_SAP or API
    Specific management messages through management interface (more suitable for static data?)
  Better term other than “interaction”?