## Slide 1: Awareness of the handover to be distinguished from a L2 or L3
Soohong Daniel Park
Soohong.Park@SAMSUNG.COM
Samsung Electronics.
March’04, Orlando FL

## Slide 2: Miscellaneous Handover
FMIP6 proposes a Fast Handover in 802.11.
MN don’t know whether it changes AP(MN1) or AR(MN2).
AP
AP
AP
AR
AR
MN2
MN1
L3 Handover ?
L3 Handover ?

## Slide 3: Current Procedure of FMIP6
After discovering a new nearby AP, MN sends RtSolPr in order to resolve AP identifiers to subnet router information.
If the new AP is connected to the PAR’s current interface itself, PAR MUST respond indicating that the point of attachment is known, but is connected to current interface.
Handover does not require change of CoA.
AP
AR
MN1
AP
PrRtAdv (Code=5)
RtSolPr
RtSolPr: Router Solicitation for Proxy Advertisement
PrRtAdv: Proxy Router Advertisement

## Slide 4: Background
AP lets MN know the handover whether L2 or L3.
ARID (Access Router Identifier) can be simply configured in conjunction with the SSID on the AP.
Reduced the redundant message exchanges between MN and PAR when performing L2 handover.

## Slide 5: Potential Solution (1/2)
ARID in the Beacon.
  Capability Information in the Beacon can be used for letting MN know its movement either L2 or L3.
New MAC Management Frame for ARID.
  Delegation in conjunction with the Beacon interval

## Slide 6: Potential Solution (2/2)
Frame Control | Duration | DA | SA | BSSID | Sequence Control | Frame Body | FCS
Type value | Subtype value | Subtype description
00 | Reserved (0110-0111) | AR Identification
AP
AP
AP
AR
AR
MN2
MN1
Capability Information Field in the Beacon
New MAC Management Frame

## Slide 7: Operation with ARID
New defined L2 Trigger
L3_Change (?)
PAR (ARID=aaaa)
PAP
MN2
NAR (ARID=bbbb)
MN1
NAP
Association
No L3 Handover
Association
ARID (aaaa) wit Beacon or New frame
ARID (bbbb) with Beacon or New frame
L3_Change & Router Discovery
RtSolPr ( for the FMIP6 Operation )

## Slide 8: Conclusion
Suggest to work on the solution for distinguishing either a L2 handover or a L3.
Reduce the redundant message exchanges and miscellaneous operation on the mobile node.