## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: IEEE802.21-05-0164-04-0000
Title: Optimal Beacon & Architecture for MIH
Date Submitted: March 4, 2005
Presented at IEEE 802.21 in Monterey, CA
Authors or Source(s): Michael Hoghooghi, Karl Heubaum, Jeff Keating, Dan Orozco, Michael Lee
Freescale Semiconductor, Inc.
Abstract: This contribution aims to facilitate MIH services for mobile nodes & networks able to support multiple protocols while adhering to the requirements of the IEEE802.21 WG.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: IEEE802.21 – Media Independent Handover Optimal Beacon & Architecture for MIH Freescale Semiconductor, Inc. DCN: IEEE802.21-05-0164-03-0021
Michael Hoghooghi
Karl Heubaum
Jeff Keating
Michael Lee
Daniel Orozco

## Slide 4: Overview
Considerations for mobility and HO
Network MIH Beacon
Focus on events and triggers
Focus on intra-layer communication to facilitate handover process
Focus on MIH call flows between protocol technologies
Scope matrix & MIH call flow
Summary

## Slide 5: Connection Analysis
HTTP Server
FTP Server
Video Server
. . . .
Internet
Cellular BTS
AN
BSC
PDSN
Ethernet
BSC-1
BSC-2
BSC-n
. . . .
AP-n
. . .
AP-1
STA-1
STA-2
STA-n
. . .
AP-2
STA-1
STA-2
STA-n
. . .

## Slide 6: Transport Protocol & MIH Function (Based on v.12, 21-04-0087-12-0000)
No restrictions on use of any transport protocol to exchange MIH function events between STA Fn-Entity & Net Fn-Entity

## Slide 7: MIH Recommendations for Mobility & HO
Important mobility enablers
  Network capability ID – modified Beacon (MIH-Beacon)
    Fits into existing protocols and may vary one to another protocol, in placement
    Minimal protocol impact with optimized channel utilization and spectral efficiency.
    Broadcast existence of network
  Triggers
    Seamless handover and service continuity
    Events occur and fire triggers
    Beacon is also a trigger
    Mobile node <---> Network actions
  Layer communications
    MIH layer down the stack
    QoS issues
    Handover selection decisions

## Slide 8: Logical HO Views
Interoperability to facilitate smooth network handover
All traffic types & payload converge on the Ethernet level – follow MoIPv6 (preferred) rules
  Home-Adr, c/o-Adr, subnet fields, etc.
Service engine plays a big role on Fast-HO
  Enables native & non-native traffic flows
  Net-controller can harmonize, when needed
MAC-xx
PHY-xx
MAC-zz
PHY-zz
MAC-yy
PHY-yy
> >
. ... .
MAC-xx
PHY-xx
MoIP addressing over Ethernet
802.11
802.16
Cellular

## Slide 9: MIH-Beacon Direction
Network to broadcast MIH beacon
  Periodic broadcast
  Beacon contains MIH capabilities of network
  Beacon can indicate MIH capability and details stored
Mobile Node to scan for MIH-Beacon in background
  MN decide when want to roam onto a new network
  Exchange basic capabilities with network during registration
  Capabilities exchanged during registration process
Modifications needed to protocol
  New management message (or other appropriate frame) to indicate MIH beacon – communicate MIH capabilities
  New data type to define capabilities, per recommendations

## Slide 10: MIH Network Selection Power-Up Example Scenario
Upon power-up, MN scans for MIH beacon
  Scan MN native mode first then proceed to other modes, if needed
  Immediately register in native mode, if available
If receive beacon from multiple networks, determine and track network types – could use influence from service engine, etc.
MN needs to determine primary function
  Adherence to service engine rules to determine network selection
  Link metrics will influence decision to associate, or not
Register with that network

## Slide 11: Content of MIH Beacon Message
TRUST
LEVEL
(4 Bits)
Carrier ID
(32 bits)
NET-TYPE
(4 Bits)
APPL CLASS
(4 Bits)
QOS Level
(4 Bits)
MAC Header
EXTENDED
SERVICES
(4 Bits)
CRC
CAPACITY
(4 Bits)
Optimization methods
  MIH-Capability (MIHC) flag  TRUE or FALSE (1 bit)
  Most spectrally efficient option (also provides rapid cognition)
  If MIHC is true, several options may be implemented
    MN could query the network for additional details or share its capability info
    Service engine may perform the lookup to get MIH details, i.e. each field maps to a lookup table for decode
  New fields to consider: MoIP-ver (2 bits), location (relative or absolute), device/user preferences, etc.
  If MIHC flag is not set, there may be other options for the MN
    It could still register with the network
    Send its visiting net info to its native net along with routing
    Service engine could determine association or other options

## Slide 12: Capability Advertising
Who advertises this information and how frequently is it done?
MIH-Beacon information may be exchanged by the network controller only during association with the MN
  Or, it may be exchanged more frequently – in this case MN may choose to look for this only when required, or it may choose to battery-save otherwise
Neighboring networks advertised
  Network controller (assuming it is MIH capable) will share this information
  MIH capable MN may periodically scan for supported protocols and report results to network controller or the service set
    This ability distributes the detection burden (power & time)
    Extends beyond network boundaries (if left only to network controller)
    Does not affect non-MIH MN

## Slide 13: MIH Logical Stack Interfaces
LLC
MAC 802.X/3GPP
PHY 802.X/3GPP
MIH Mobility Management Convergence
MIH Handover Control
MIH Physical Convergence
Mobility Mgmt
User Preferences
Net. operation preference
Applications
Convergence
Network
Application
MM-SAP
MAC-SAP
PHY-SAP
MIH-MM-SAP
MIH-PHY-SAP

## Slide 14: MIH Block Within the Stack
LLC
MAC 802.X/3GPP
PHY 802.X/3GPP
MIH Mobility Management Convergence
MIH Handover Control
MIH Physical Convergence
Mobility Mgmt
User Preferences
Net. operation preference
Applications
MIH
Mobility Events
MAC Events
PHY Events
Convergence
Network
Application

## Slide 15: MIH Layer Descriptions
MIH Mobility Management Convergence
Processes user/network requests based on defined preferences and network configurations and submits actions to the MIH Handover Control sub-layer
MIH Handover Control
Processes MAC layer events and QoS-related network events
In response to submitted actions, executes handover function and performs handover sequence between all MIH layers
MIH Physical Convergence
Processes RF-related indicators and submits actions to the MIH Handover Control sub-layer

## Slide 16: MIH Layer Interface Descriptions
MM-SAP
Carries messages of user preferences, network operation preferences, and applications between the MIH and MM
MAC-SAP
Carries network triggers and QoS parameters required by the handover control sublayer.
PHY–SAP
Carries RSSI, BER, CINR and RF-related parameters required by the handover control sublayer.
MIH-MM-SAP
Carries requests, commands, and services required by the handover control sublayer.
MIH-PHY-SAP
Carries link quality and RF-related parameters required by the handover control sublayer.

## Slide 17: MIH Triggers

## Slide 18: Event & Link Triggers
PHY RRM
  Signal strength (RSSI)
  BER
  CINR/SNR
  Loss of link
  Better link available
  Link error occurred
Network billing cost
MAC QoS
  Bit rate
  Voice quality
  Jitter
  Bandwidth availability
  Traffic congestion
MIH Preferences
  Roam priority
    i.e. Home, .11, .16, etc.
Authorized MIH Capable
  Force to leave network roamed to, if needed
  Pay for feature access
User-selected preferences
Applications

## Slide 19: Event & Link Triggers
Trigger Name Source Destination
MIH.MOB.COST MOB MIH Mobility Mgmt Conv
MIH.MOB.ROAM_PRIO MOB MIH Mobility Mgmt Conv
MIH.MOB.USER MOB MIH Mobility Mgmt Conv
MIH.MOB.APPL MOB MIH Mobility Mgmt Conv
MIH.MAC.NETWORK MAC MIH Handover Control
MIH.MAC.QoS MAC MIH Handover Control
  Bit rate
  Voice quality
  Jitter
  Bandwidth availability
  Traffic congestion
MIH.PHY.RRM PHY MIH Phys Conv
  BER
  Signal strength (RSSI)
  CINR/SNR
  Loss of link
  Better link available
  Link error occurred

## Slide 20: MIH Call Flow
Old Point of Attachment
Multimode STA
New Point of Attachment
HL
MIH Function
LL
LL
HL
MIH Function
LL
HL
MIH Function
MIH Mobility Conv
MIH HO Control
MIH PHY Conv
HO Rqst
Local
Trigger
Beacon Message
Handover association request and SS basic parameters
Query current network
Obtain subscriber details
Handover grant
Activate on new network
Notes: 1.) Shows an 802.X session in progress – a rough view of the data path is shown
2.) 802.3 PHY is detected I.E. the combo Station is plugged in
3.) Results in a MIH_PHY_EVENT sent to the MIH function
4.) A decision is made by some policy function to begin a handover
5.) MIH enters the HO Prepare State
6.) The “Make” process is started by sending a MIH_HO_PREPARE trigger to the HL
7.) This trigger contains routing info that the MIH function collected when it first accessed the system. This facilitates the acquisition of the new CoA.
8.) Similarly, HO_PREPARE is sent to prepare the new LL entity
9.) A new IP tunnel is established
10.) This example assumes “Multiple CoA registration” so at this point two IP streams are in place.

## Slide 21: Cellular Handover Example
Mobile Downward – “to” Cellular handover
Weak signal detected from current network
Access the cellular channel
Receive agent advertisement from cellular network
Handoff ready request from MN to cellular network
Data packets begin buffering in cellular network
Routing update completed
Assignment of cellular traffic channel
MN registers on the cellular network
Buffered packets are forwarded to MN
Disassociation with previous network
Mobile Upward – “from” Cellular handover
MN receives strong beacon from new network
Receive agent advertisement from cellular network
Handoff ready request from MN to cellular network
Traffic channel release request from MN
Reassociation request to new network
Data packets forwarded to new network
Release completed

## Slide 22
Media Independent Handover Proposal Scope Matrix for Discussion Part-I

## Slide 23
Media Independent Handover Proposal Scope Matrix for Discussion Part-II

## Slide 24: Summary
Key points:
  Beacon message to indicate network presence and MIH capability
  MN capable of querying network for capabilities
  MN can associate with newly detected network
Updated information on triggers to initiate handover
SAPs defined to carry information between MIH and other layers
Processing of triggers done at specific blocks within MIH layer
Call flow example to show how handover would be done using beacon as trigger